## Slide 1: Alignment Accuracy in Long Straight Sections
Dr. Johannes J. Prenting
SLRS: why do we need it ?

## Slide 2
Distribution of SLRS systems in the XFEL
SASE1: 535m
SASE2: 555m
SASE3: 443m
3 SLR-Systems
Distribution of SLR Systems inside the XFEL
Accuracy requirement: 1mm / ~600m
Accuracy requirements
  for initial setup of beamlines:
  Linac: 0.3mm wrt. 150m length
  Photon beamlines: 1mm wrt. ~600m length
  Additional relative alignment required after
    beam-based-alignment -> given nominal values.
SLRS: why do we need it ? // obstacles
Errors on classical optical survey allow certain accuracy
- systematic errors due to refraction (temperature gradient)
- Random errors: Instrument Accuracy, Measurement Geometry

## Slide 3: SLRS: why do we need it ? // obstacles
Systematic errors: refraction due to temperature gradient
Every line of sight gets bent to a spatial curve while travelling through the inhomogeneous medium of air. (Air layers with different density).
The turbulent part of refraction shows up as air flicker (not critical)
The static part of refraction shows up as a stable curvature of the line of sight (systematic error, critical)
Assumptions:
  The refractive index of air is constant
  The temperature gradient only is effective perpendicular to the line of sight
Then and only then:
  The line of sight is a segment of a circle.
  The sagitta „z“ can be estimated with the following approximation/rule of thumb:

## Slide 4
SLRS, obstacles: Numerical examples for various temperature gradients and measuring distances,
calculated from abovementioned approach. Shown are the angular error d delta (named alfa in the table) and the sagitta „z“ between straight line and line of sight:
Numerical examples of errors for various
Systematic errors: refraction due to temperature gradient

## Slide 5
Simulation of XFEL-Ref.pointgrid of
  600m length, without SLRS
Dark Blue:
Gridpoints, a ring with 6 points every
9m
Instrument stands in between two rings.
Cyan:
Error of a component coordinate at a designated position within the reference grid.
@ the edge: 2,25mm, in the middle: 1,6mm
Red:
relative error between the 1. component and the component at the designated position.
max.: 3,75mm
DVW Exkursion DESY/XFEL
2014-03-18, Dr. Johannes Prenting, DESY
Simulation of Random Errors
Random errors: Instrument Accuracy, Measurement Geometry

## Slide 6
Simulation of XFEL-Ref.pointgrid of
  600m length, without SLRS
Dark Blue:
Gridpoints, a ring with 6 points every
9m
Instrument stands in between two rings.
Cyan:
Error of a component coordinate at a designated position within the reference grid.
@ the edge: 2,25mm, in the middle: 1,6mm
Red:
relative error between the 1. component and the component at the designated position.
max.: 3,75mm
Simulation of Random Errors
Random errors: Instrument Accuracy, Measurement Geometry

## Slide 7
STRAIGHT LINE REFERENCE SYSTEM.
Simulation including SLRS
Simulation of XFEL-Ref.pointgrid of
  600m length, incl. SLRS
  with 60µm resolution
Dark Blue:
Gridpoints, a ring with 6 points every
9m
Instrument stands in between two rings.
7 SLRS Stations, evenly distributed over the lenght of 600m (every 75m)
Cyan:
Error of a component coordinate at a designated position within the reference grid.
max: 0.16mm
Red:
relative error between the 1. component and the component at the designated position.
max.: 0,32mm
Random errors: Instrument Accuracy, Measurement Geometry

## Slide 8
Random errors in a stretched geodetic network including refraction
The distortion due to refraction during the measurements is not detectable and not predictable.
Main reason for refraction: temperature gradients between the tunnel walls and the tunnel center.
Standard procedure: measuring across the tunnel from alternating sides to minimize refraction effects  not possible in an equipped tunnel
???
Simulation of random and systematic errors combined
Notes: 8

## Slide 9: System setup
Dx, Dz
Dx, Dz
Dx, Dz
System Integration
  The SLRS (Straight Line Reference Surveyor) is a refraction free alignment system
  It uses a collimated laser beam within an ISO200 vacuum tube
  SLRS is used like a ruler put into the seemingly bent (refraction) tunnel network
  There is no direct connection between the SLRS and machine components
  SLRS provides correction parameters (dx, dz) for the geodetic network
  Calibrated transfer pieces are used to connect the SLRS measuremets
    with the tunnel network

## Slide 10: System setup, Principle
  The SLRS (Straight Line Reference Surveyor) is a refraction free alignment system
  SLRS is used like a ruler put into the seemingly bent (refraction) tunnel network
  SLRS provides correction parameters (dx, dz) for the geodetic network
  It uses a collimated laser beam within an ISO200 vacuum tube
  A laser light source emits coherent light (see right side of sketch)
  A fiber end, aperture and a plano convex lens are used to expand and collimate the beam
  Spheres put into the beam along the measuring section originate a poisson spot behind the centre of the sphere which can be viewed with a ccd camera
  The centre of the sphere and the centre of its poisson spot in the image generate a straight line
  A lens system focuses the expanded beam to the dimensions of the CCD sensor
  Correlation algorithms are used to calculate the poisson centres in the image
Plano-convex lens
Targets
Plano-convex lenses
CCD Camera
Laser Point Source
Aperture
3m
520m
3m

## Slide 11: System setup
Actual setup:
      Aluminum pipes, 7.73m/3.87m long, 200mm diameter. Supports are placed every 3 to 4.5m with fixed point and floating point fixing.
      special housings for (laser, aperture, lenses) and (lenses & camera)
      Tee piece connector with bellows, every 24m, every 2nd is
      equipped with adapted measurement targets (aka target boxes)
      blue laser (wavelength = 405nm) allows for small targets and provides fine interference patterns
      revised plano convex lenses for minimal spherical aberration
      GigE-Camera with 2048x2048 pix. resolution
      Oerlikon/Leybold Trivac D 65 B Vacuum pumps
housing for laser, aperture, lens
camera housing
SLRS@SASE1, 482m
Tee piece connector & bellows

## Slide 12
actual corrections from SLRS SASE 1

## Slide 13
actual corrections from SLRS SASE 3

## Slide 14
Conclusions
Motivation for the operation of the SLRS
  The SLRS (Straight Line Reference Surveyor) is a refraction free alignment system
  SLRS provides correction parameters (dx, dz) for the geodetic network
  The correction parameters eliminate the systematic error caused by temperature gradient
  random errors get minimized to a non critical amount (see slide 10)
  at SASE1 and SASE3 correction values were in the order of +- 1,5mm
  These errors would not be detected without the SLRS and would remain as unavoidable alignment errors

## Slide 15
Different Measuring techniques
Referenzierung des Polygonzuges über Sollkoordinaten des Beschleunigers
Freie Stationierung, Referenzierung über Referenzpunkte des Festpunktnetzes
Polygonzugmessung über feste Standpunkte

## Slide 16
Simulation of random and systematic errors combined
Simulation of XFEL-Ref.pointgrid of
  600m length, without SLRS
Dark Blue:
Gridpoints, a ring with 6 points every
9m
Instrument stands in between two rings.
Cyan:
Error of a component coordinate at a designated position within the reference grid.
@ the edge: 2,25mm, in the middle: 1,6mm
Red:
relative error between the 1. component and the component at the designated position.
max.: 3,75mm
Schwarz:
Verbiegung des Netzes durch Refraktion
ca. 9mm bei dT = 0,2K / 1m