## Slide 1: DosiMon RadFet system requirements to the SASE3-VP Project
Location environment at SASE3 Helical Afterburner section
DosiMon System setup & requirements (frontend hw)
DosiMon System setup & requirements (backend hw, fw & sw)
Next steps
Open questions

## Slide 2: Location environment at SASE3 Helical Afterburner section
4 Helical Undulators w/t 3D-remote-adjustable gaps *
*  movable sensors needed
Synchrotron radiation from regular upstream undulators **
2 diagnostic crates w/t DosiMon interface available nearby (DI2943T4D, DI3065T4D)
**  shielded sensors needed
Well collimated beam from upstream undulator chambers ***
***  no chamber sensors
Offline radiation damage threshold measurements
Measure integrated dose from high energy shower absorbed at UNDs
(Afterburner Kick Off Meeting 26.4.2018 J. Pflueger, European XFEL,WP71)

## Slide 3: DosiMon System setup & requirements (frontend hw)
Established sensor frontend concept (RadFet (replaceable),TLD (ref.), Pt1000, ID-R, lead-cap)
Sensor holder with pre-defined, radially-adjustable displacement positions & stacked sensor positions for RadFet || TLD (NEW DESIGN!)
Special narrow lead cap shieldings (NEW DESIGN!)
Mounting holes needed
SPECIAL NEW LOW-SCALE SENSOR-HOLDER/LEAD-CAP DESIGN NEEDED !
(Afterburner Kick Off Meeting 26.4.2018 J. Pflueger, European XFEL,WP71)

## Slide 4: DosiMon System setup & requirements (backend hw, fw & sw)
Standard DosiMon frontend-readout electronics (DosiBox, DosiMon-FMC, DAMC2, MTCA.4 crate) => 1 DosiBox per Helical Undulator => 4 DosiBoxes (DosiMon-FMC available at the existing MTCA diagnostic crates)
Standard frontend firmware, standard device server & administration (ML-)server (MDI, MCS4/1)
standard operating procedures for regular SASE undulators apply - determination of radiation damage levels by magnetic-field degradation measurements (WP71) - configuration of new/individual radiation damage levels (normal/warning/error) - confirmation of level-warnings/-errors after recognition by the operators
Operating- & experts-panels have to be adjusted to different Helical Undulator structure/setup (MCS)
Cabling transfer-box to be mounted on existing side-plate

## Slide 5: Next steps
Fix sensor frontend setup & define sensor holder geometry (RadFet, TLD, Pt1000, ID-R, lead-cap) (MDI)
Define mounting positions (sensor holders, transfer box, cabling, …) (MDI, MVS, WP71, PSI)
Manufacture prototype of sensor frontend & assembly (MDI, ZM)
Check & release series assembly at Helical Undulator test-stand (WP71, PSI, MDI)
Manufacture sensor frontend series parts (16 series (+2 spare)) (MDI, ZM)
Mount 16 sensor frontends at the 4 helical undulators – all work to be done by MDI in close cooperation with WP71
Estimated production & working time: ~ 3/4 year from design-start to series hw components, ~1 week assembly & adjustment
Estimated start of work: late summer 2019.

## Slide 6: Open questions
Optimum mechanical alignment of sensors to frontside/inner edge of 1st magnet slice?
Calibration & definition of radiation damage-levels as appropriate for Helical Undulators?
Is the magnetic material equal to the material at the standard SASE undulators?
How & where can magnetic-field measurements be done? ( WP71) - In-Place at Helical Undulator inside the tunnel? - Dismounting/remounting of magnet slice(s) from Helical Undulator & magnetic-field measurement outside of the tunnel? - Measurement of complete Helical Undulator outside of the tunnel ( transport)?
determination of appropriate radiation damage levels probably needs … - offline measurement of magnetic field degradation (see above) - survey of typical longitudinal degradation vs em-shower development  how much degrade certain magnetic slices at „the typical“ shower?  how is polarized SASE affected by the typical longitudinal magnet-slice degradation-pattern?

## Slide 7: Thank you!
Questions?