## Slide 1: SENSE – Recommendations
SiPMs
Understand the potential for further improvements to the major parameters of SiPMs as sensors and outline the possible developments and interactions with possible industrial partners;
Give contours to a “standard brick” of the SiPM-based sensor of one or two-inch size;
Move towards the SiPM “standard brick” with a “universal” fast readout scheme. This would be a first step towards the LEGO-brick principle for assembling imaging cameras of arbitrary size;
Progress from semi-integrated standard brick to fully integrated LEGO-brick through the implementation of 3D integration.
No coating significantly reduces optical cross-talk rate; Consider as an approach for CTA.
Further reduce optical cross-talk by suppressing photons propagating through the backside of the device.

## Slide 2: SENSE – Recommendations
PMTs
Optimize light use - include reflecting surfaces when appropriate and use optical cavity properties of thin films (optical etalon) for some applications;
Investigate new gain designs, such as active transmission dynodes; this is especially useful in applications where miniaturization is desirable;
Improve the photocathode quantum efficiency, lifetime, and temporal response;
Improve photocathode crystal quality and stochiometry through monitored coevaporation (slow growth), lattice matched substrate (epitaxy), and bulk material;
Improve the understanding of the bulk properties of bialkali photocathode material as a semiconductor;
Grow materials without grain boundaries − and potentially with complex material junctions to optimize for charge transport, also by considering ion implantation;
Create photocathodes with internal fields via p/n doping and heterostructuring multiple antimonides, which requires control of film thickness and roughness;
Improve surface termination to optimize electron affinity without damaging lattice structure;
Investigate material purity when crystalline defects are under control.

## Slide 3: SENSE – Recommendations
Theoretical Modeling
Extend TCAD to modeling of multiplication in Geiger mode;
Improve IV curve model; implement parameterization approach of N. Otte, and theoretical models based on solid state physics (e.g.) by M. Biroth;
Improve SiPM model as a signal source, and take into account light shape and nonlinearities;
Pay more attention to avalanche timing within SER for ultimate time resolution (10 ps);
Pay more attention to statistical grounds for SiPM characterization/metrology;
Move forward in reward-renewal approach, i.e. include correlated effects and binomial nonlinearity;
Aim for a nonlinear model of arbitrary waveform signal detection.

## Slide 4: SENSE – Recommendations
Electronics
Any decent electronics are sufficient for slow applications as long as slow shaping is used;
Aim to maximize charge collection while minimizing impact of series noise;
Optimize the amplifier to achieve good SNR in fast and large area applications;
New hybrid (electronics embedded in the sensor) and 3D integration approaches should be developed to achieve the ultimate timing in large area detectors;
Fast waveform sampling offers the ultimate performance;
Custom ASIC with analogue shaping and dedicated ADC is the optimal solution for large systems.

## Slide 5: SENSE – Recommendations
Laboratory
Reference detectors should be sent to NIST every 4-5 years for recalibration;
NIST recalibrated detectors should be stored in a dry place and under vacuum if possible;
Reference detectors used in laboratories should be recalibrated every 6 months to 1 year;
Neutral density filters should be recalibrated every 6 months;
Use calibrated SiPM as reference detectors to avoid the use of neutral density filters and the large differences in signal between the SiPM and the reference photodiode;
Calibrated SiPM on-board a tile to simultaneously measure all other pixels may be useful for PDE measurements of SiPM tiles.

## Slide 6: SENSE – Discussion
What is missing in the roadmap?
What is the demand or motivation coming from application side to do certain R&D steps for SiPMs, PMTs or other types of photosensors?
Who can do what or is already working on what?
Where comes industry into play?
Where can we team up and join activities?
How and when to monitor progress (e.g. next Light workshop?)?
What kind of coordination is necessary?
To whom shall the roadmap be sent/presented?

## Slide 7: SENSE – How to continue
EU does not provide a frame to continue with SENSE as Coordination & Support Activity
Horizon 2020 FET Programme:
FET Open R&D projects (up to 3 Mio € for cutting-edge high-risk / high-impact interdisciplinary research (Radical vision, Breakthrough technological target, Ambitious interdisciplinary research) deadlines: 18.9.2019, 13.5.2020
FET Launchpad projects: (100k€ for turning results from FET-funded projects into genuine societal or economic innovations) deadlines: 8.10.2019, 14.10.2020
EU Science Europe (FP9) Programme:
European Innovation Council ?????????????????????????
National funding? Perhaps pooled in an APPEC Common Call activity?

## Slide 8: SENSE – How to continue
Horizon 2020 MSCA: deadline: 14.1.2020 (530.13 Mio €)
Research networks (ITN): support for Innovative Training Networks
Joint research training and/or doctoral programmes, implemented by European partnerships of universities, research institutions, and non-academic organisations.
The research training programmes provide experience outside academia, hence developing innovation and employability skills.
ITNs include industrial doctorates, in which non-academic organisations have an equal role to universities in respect of the researcher's time and supervision, and joint doctoral degrees delivered by several universities.
Non-European organisations can participate as additional partners in ITNs, enabling doctoral-level candidates to gain experience outside Europe during their training.

## Slide 9: SENSE – How to continue
Horizon 2020 MSCA: deadline: 14.1.2020
Research networks (ITN): support for Innovative Training Networks
4 years lifetime
Funding for up 540 person months
Funding for research costs, training, networking activities and coordination, as well as for management and overheads
Input from SENSE:
Supervisory board needed to co-ordinate network-wide training and establishing active and continuous communication and exchange of best practice among the participating organisations to maximise the benefits of the partnership.
Training program