## Slide 1: Machine Learning for PETRA IV
Orbit correction and beam accumulation
Andrei Ivanov
Hamburg, 03.12.2019

## Slide 2: Overwiew
01 Problem Formulation
Linear dynamics
Nonlinear effects
Misalignements
02 ML-based solutions
Learning dynamics
Control policy
03 Next steps
2

## Slide 3: Problem Formulation

## Slide 4: The linear models are used to correct orbit
Reference orbit is designed along centers of elements
3
dipole
x
quadrupole
sextupole

## Slide 5: The linear models are used to correct orbit
Because of imperfections the actual orbit has deviations
3
dipole
x
quadrupole
sextupole

## Slide 6: The linear models are used to correct orbit
To measure the beam deviation a BPM is used
3
dipole
x
quadrupole
sextupole
Δx1
Δx2
BPM1
BPM2
Orbit correction: Δx1⟶ 0, Δx2⟶ 0

## Slide 7: The linear models are used to correct orbit
Additional magnets correct the orbit
3
dipole
x
quadrupole
sextupole
Δx1
Δx2
BPM1
BPM2
corrector magnet С1
corrector magnet С2
Orbit correction: Δx1⟶ 0, Δx2⟶ 0
M
M is response matrix, is calculated from the lattice as an initial approach and clarified with measured data
SVD
Least-Squares Method

## Slide 8: The linear dynamics of particles
Linear dependencies between correctors and orbit deviation at BPMS
Control
Δx
Linear oscillations around the reference orbit
4
x
x'

## Slide 9: The linear dynamics of particles
Linear dependencies between correctors and orbit deviation at BPMS
Control
Δx
Nonlinear dynamics
5
x
x'

## Slide 10: The linear dynamics of particles
Linear dependencies between correctors and orbit deviation at BPMS
Control
Δx
Nonlinear dynamics
5
x
x'
The vibration of pivot point can cause both stabilization of the inverted position and chaotic regime for bottom position

## Slide 11: Dynamics between BPMs
Local bumps can arise
6
x
Δx1 = 0
Δx2 = 0
BPM1
BPM2
Δxhidden >> 0

## Slide 12: Misalignments
affect lattice optics
7
dipole
F2 ~ g2
x
quadrupole F1 ~ g1· x
sextupole F3 ~ g3· x2

## Slide 13: Misalignments
affect lattice optics
7
dipole
F2 ~ g2
x
quadrupole F1 ~ g1· (x + Δx)
sextupole F3 ~ g3· (x + Δx)2

## Slide 14: Misalignments
affect lattice optics
7
quadrupole F1 ~ g1· x
+
dipole F12 ~ g1· Δx
quadrupole F31 ~ g3· 2xΔx
+
dipole F32 ~ g3· Δx2
sextupole F3 ~ g3· x2
+
dipole
F2 ~ g2
x
quadrupole F1 ~ g1· (x + Δx)
sextupole F3 ~ g3· (x + Δx)2

## Slide 15: Misalignments
affect lattice optics
7
Design lattice
x
Actual lattice
dipole
F2 ~ g2
x
quadrupole F1 ~ g1· x
sextupole F3 ~ g3· x2

## Slide 16: PETRA IV
Challenges for the orbit correction and beam accumulation
Low emittance and strong sextupoles introduces sensitivity against lattice imperfections
Large amount of BPMs (~1000) along with the huge amount of control elements
8

## Slide 17: PETRA IV
Challenges for the orbit correction and beam accumulation
Low emittance and strong sextupoles introduces sensitivity against lattice imperfections
Large amount of BPMs (~1000) along with the huge amount of control elements
8
To tackle these problems one can enhance control with ML
Learning model of misalignments with the measurements from BPM
Predict model of misalignments for new runs
Virtual BPMs (simulation of dynamics between BPM)

## Slide 18: ML-based solutions

## Slide 19: ML methods
Learning dynamics
9
import tensorflow as tf
from keras.models import Sequential
from Taylor_Map import Drift, Diplole, Quadrupole, Sextupole
lattice = Sequential()
high-order maps for dynamics simulation (Taylor maps, Lie transform, Differential Algebra)

## Slide 20: ML methods
Learning dynamics
9
import tensorflow as tf
from keras.models import Sequential
from Taylor_Map import Drift, Diplole, Quadrupole, Sextupole
lattice = Sequential()
lattice.add(Quadrupole(length=0.1, k1=1.0))

## Slide 21: ML methods
Learning dynamics
9
import tensorflow as tf
from keras.models import Sequential
from Taylor_Map import Drift, Diplole, Quadrupole, Sextupole
lattice = Sequential()
lattice.add(Quadrupole(length=0.1, k1=1.0))
lattice.add(Drift(length=0.25)
lattice.add(Dipole(length=0.1, angle=0.01))
…
lattice.predict()

## Slide 22: ML methods
Learning dynamics
10
import tensorflow as tf
from keras.models import Sequential
from Taylor_Map import Drift, Diplole, Quadrupole, Sextupole
lattice = Sequential()
lattice.add(Imperfection()) # nonlinear model with trainable_weights
lattice.add(Quadrupole(length=0.1, k1=1.0)) # lattice design

## Slide 23: ML methods
Learning dynamics
10
import tensorflow as tf
from keras.models import Sequential
from Taylor_Map import Drift, Diplole, Quadrupole, Sextupole
lattice = Sequential()
lattice.add(Imperfection()) # nonlinear model with trainable_weights
lattice.add(Quadrupole(length=0.1, k1=1.0)) # lattice design
…
lattice.fit() # fit model of imperfections with data from BPMs
Imperfection():
simple shifts for misalignments, neural networks for considerations of nonlinear effects, etc.

## Slide 24: ML methods: control policy
Classical Control Theory or Reinforcement Learning with continuous actions
11
A computational graph in TensorFlow
control
observations
temperature, etc.
OCELOT Optimizer
RL

## Slide 25: Next steps
in terms of data acquisition and interfaces to be able to introduce implemented models into existing control environment
Build models for orbit correction with simulated data
OCELOT:
open source project for beam dynamics simulation of the whole machine in modern electron-based x-ray sources
Work with infrastructure
12

## Slide 26
Andrei Ivanov
MPY
andrei.ivanov@desy.de
Thank you