## Slide 1
We are planning two more engineering runs in TSI. A large chip for Mu3e MUPIX10 will be submitted within the first run.
The second run will be shared within many projects.
Multi purpose chip (Belle II)
CLIC
LHCB
Small pixels
Pixel readout chip
(hybrid detectors)
Counting pixels for hadron therapy
TBD

## Slide 2
We are planning two more engineering runs in TSI. A large chip for Mu3e MUPIX10 will be submitted within the first run.
The second run will be shared within many projects.
Multi purpose chip (Belle II)
CLIC
LHCB
Small pixels
Pixel readout chip
(hybrid detectors)
Counting pixels for hadron therapy
TBD
Large multi-purpose low power chip with 50µm x 50µm pixels, triggered and untriggered readout and geometry that would fit for instance to belle 2.
Pixel readout chips for medical applications (readout of CdTe sensors)
Counting monolithic pixel sensor for hadron therapy application
Pixel matrix and test structures for LHCB

## Slide 3
CLIC design with elongated pixels 25 x 300 um and the readout and periphery similar to ATLASPIX simple
10 bit leading edge time stamp and 7 bit TOT time stamp
The pixels would contain CSA and comparators that would be implemented as CMOS circuits and isolated by deep p-well.
Multi purpose chip (Belle II)
CLIC
LHCB
Small pixels
Pixel readout chip
(hybrid detectors)
Counting pixels for hadron therapy
TBD

## Slide 4
All previously mentioned sensor would be based on the pixels with large fill factor, the deep n-well filled with electronics
Since TSI can make deep p-well we can also do low fill factor sensors. We plan following test sensor:
The pixels would have size of 25 x 25 microns and in pixel electronics with CSA, comparators, time measurement and priority based readout. 10 bit leading edge and 6 bit TOT time stamp would be implemented per pixel
Multi purpose chip (Belle II)
CLIC
LHCB
Small pixels
Pixel readout chip
(hybrid detectors)
Counting pixels for hadron therapy
TBD

## Slide 5
P-substrate (200 Ohm cm)
25µm
n-well
p-well
Deep p-well
n-well
n-well
n-well

## Slide 6
Improvements of standard HVCMOS stracture are possible
Idea: reduce capacitance by reverse biasing of deep-pwell to n-well junction
N-well
P-well = 0V
N-well
Deep n-well
Deep p-well
P-substrate (200 Ohm cm)

## Slide 7
N-well
P-well = 0V
N-well
Deep n-well
Deep p-well
P-substrate (200 Ohm cm)