## Slide 1: Applications for a Laser-Driven Accelerator on a Chip
R. J. England (SLAC, Stanford)
3rd Workshop on Applications of Dielectric Laser Accelerators
Boulder CO, March 10, 2020

## Slide 2: Dielectric Laser Accelerator (DLA) Concept: Towards an “Accelerator on a Chip”
gradient
fused silica
silicon
SEM images of DLA prototypes tested at SLAC
Modelocked Thulium Fiber Laser (λ = 2µm, 10µJ, $300k)
Required lasers are MHz rep rate, low pulse energy, wallplug efficiency ~ 30%
Dielectric materials can withstand GV/m
fields and kilowatts of average power
Can be mass produced using techniques of the integrated circuit industy.
3 cm
DLA research aims to produce ultracompact nanofabricated devices for particle acceleration, powered by efficient solid-state lasers.

## Slide 3: Moore Foundation has Funded a 5-Year Accelerator on a Chip International Program (ACHIP)
3
Goals of ACHIP:
(1) An MeV class benchtop DLA accelerator in 5 years.
(2) Transverse dynamics (focusing, deflection, undulators, diagnostics)
Moore Foundation “Accelerator on a Chip” Program (started Dec 2015)
$13.5M / 5 years
6 universities, 3 partner labs
1 industry partner
The ACHIP program has been extended by Moore Foundation for an additional 2 years, continuing through 2022.
(DOE Web Feature 2015)

## Slide 4: ACHIP Institutional Organization
System integration
(Core DLA groups)
Stanford: Byer, Harris, Solgaard
Erlangen: Hommelhoff
Light Coupling
Stanford: Fan, Vučković
Electron source
UCLA: Musumeci
Erlangen: Hommelhoff
Stanford: Harris, Solgaard
Structures
Stanford: Harris, Solgaard, Byer
Erlangen: Hommelhoff
Simulations
Tech-X: Cowan
U Darmstadt: Boine-Frankenheim
Relativistic DLA experiments
SLAC: England
DESY/UnivHH: Assmann, Kaertner, Hartl
PSI/EPFL: Ischebeck, Rivkin
Associated Scientific Collaborators
Yenchieh Huang (Tsinghua)
Evgenya Simakov (Los Alamos)
Zhirong Huang (SLAC)
Kazu Koyama (Tokyo U)
Sub-Relativistic DLA experiments
Stanford: Harris, Solgaard
Erlangen: Hommelhoff
Program start: Dec. 2015
ACHIP Scientific Advisory Board:
Chan Joshi (UCLA), Tor Raubenheimer (SLAC), Reinhard Brinkmann (DESY)
Industrial affiliate Hamamatsu Corp. Japan (joined June 2017)
R. L. Byer (Stanford), P. Hommelhoff (FAU), R. J. England (SLAC), R. Assmann (DESY), R. Ischebeck (PSI)
Executive Committee:

## Slide 5: ACHIP Technical Group Organization
R. L. Byer (Stanford), P. Hommelhoff (FAU), R. J. England (SLAC), R. Assmann (DESY), R. Ischebeck (PSI)
Executive Committee:
TG 2: Relativistic Structures & Facilities
R. J. England (SLAC)
R. Assmann (DESY)
R. Ischebeck (PSI)
TG 5: Radiation Generation and Applications
Yen-Chieh Huang (NTHU TW)
Zhirong Huang (SLAC)
TG 1: Injector
K. Leedle (Stanford)
N. Schönenberger (FAU)
TG 3: Laser Sources & Coupling
J. Vučković (Stanford)
F. Kaertner (Hamburg)
I. Hartl (DESY)
TG 4: Simulation and Beam Dynamics
U. Niedermayer (Darmstadt)
B. Cowan (Tech-X)
TG 6: Integration
R. J. England (SLAC)
P. Hommelhoff (FAU)
P. Musumeci (UCLA)

## Slide 6: Concept for 1 MeV “Shoebox” Accelerator (1 Year)
...
Transverse Focus
Longitudinal Focus
Emitter
Buncher
DLA Linac with APF Focus + Velocity Taper
50-100 keV
Pulse Front Tilted Laser
1.3 cm
tip emitter +
electrostatic
lens
A single bunching/acceleration/focusing stage driven by a tilted laser pulse.
special “banana” shaped pulse needed for group velocity match

## Slide 7: High Brightness Photocathodes Tested Under the ACHIP Program...
A. Ceballos, DLA Applications Workshop, March 26 (2019)

## Slide 8: A compact prototype “shoebox” test system is now operating at Stanford University – goal of 1 MeV energy
8
Stanford “glassbox” test system
N. Sapra, et al.,
Science 367, 79 (2019)
optimized DLA components via inverse design
e-
waveguide coupled DLA
T. Hughes, et al, Phys. Rev. Appl. 9, 054017 (2018)
compact electron gun
w/electrostatic lens
Si tip emitter
splitters
couplers
courtesy T. Hirano (Hamamatsu, visiting scientist at Stanford University)
3000 e-/pulse,100 kHz rep
0.2 nm emittance
A. Ceballos, Stanford
compact e- gun
30mm
96keV

## Slide 9: Sub-relativistic Structures with Laser-Driven Focusing Have Been Recently Fabricated for Experimental Tests
First APF structure optimized for 2000 nm laser wave length and 26.478 keV electron beam Structure length required pulse front tilted (PFT) laser pulses
Structure is only for guiding as a proof-of-principle
Goal is to see a maximum laser ON/OFF contrast of 2.5:1
Additionally the contrast should scale with incident laser power
z
y
x
s
Laser
Laser
Niedermayer, et al., PRL 121, 214801 (2018)
Hommelhoff Group, FAU Erlangen, Germany

## Slide 10: Multistage Waveguide Network Design for a Dielectric Laser accelerator
• Design Study of Integrated Multi-Stage DLA Network
• Realistic Component Parameters
• Adjoint Variable (“Inverse Design”) Based Structure Optimizations
couplers
splitters
phase shifters
T. Hughes, et al. “On-Chip Laser Power Delivery System for Dielectric Laser Accelerators,”
Phys. Rev. Appl. 9, 054017 (2018)

## Slide 11: Demonstration of a waveguide-coupled DLA produced using inverse design optimization
N. Sapra, et al., “On-chip laser driven particle acceleration through inverse design,” Science 367, 79 (2019)
• First demonstration of acceleration in a waveguide-coupled DLA
• Acceleration of 1.2 keV over 30 µm (gradient of 40.3 MeV/m)
• Illustrates utility of inverse design methods to optimize over unique parameter constraints

## Slide 12: Concept for Injector + Multistage Accelerator (2-5 Year)
12
Injector/Buncher
MZI Controlled DLA Linac with APF Focusing
...
silicon
fused silica
Oscillator 1
CEP phase locked network
Master Clock
Oscillator 2
…
Oscillator N
Master Oscillator
Oscillator 3
…
50 keV 1 MeV 5-10 MeV
Thulium Fiber
Laser (2µm)
Oscillator 0

## Slide 13: Shoebox Demonstration System Parameters (1 vs. 2-3 Year Time Scale)
Parameter | Units | Near Term (1 Year) | Longer Term (2-3 Years)
Final Electron Kinetic Energy | MeV | 1 | 6
Charge Per Laser Pulse | e- | 10 | 300
Laser Rep Rate | MHz | 0.1 | 50
Electron Beam Size (X/Y) | µm | 0.05 / 1.00 | 0.05 / 1.00
Geographical Gradient | MeV/m | 100 | > 200
Total Accelerator Length | cm | 1 | 3
Electron Beam Power | µW | 1 | 3000
Values represent conservative estimates (as of March 2019) and not ultimate limitation on the technology.

## Slide 14: What are DLA’s Unique Capabilities?
• Compactness: x10-2 longitudinal, x10-4 transverse
• Efficiency: solid state lasers (> 30% wall-plug)
• Bunch Format: fC charge at MHz rep rates
• Attosecond Time Scale: intrinsic optical bunching
• Uniquely enabled by DLA?
Features of a DLA Accelerator:
“Create a matrixed list or table of all DLA related applications that have been proposed or discussed so far, both near and long-term, including industrial, scientific, and medical. Please evaluate each application in terms of area of interest (light source, HEP, industry, medicine, security, etc.), feasibility (is DLA a good match?), time scale (near-term vs. long-term), and degree to which it leverages DLA's unique capabilities.”

## Slide 15: Applications Identified by the March 2019 DLA Applications 1-Day Workshop
potential areas of industry interest
Biomedicine industry
-- Radiation therapy
Semiconductor industry
-- low-power EUV for mask/wafer
inspection/calibration
potential areas of scientific interest
Nano- or micro-beam for radiobiology and radiation chemistry
Ultrafast electron diffraction, X-ray pulses at sub-fs time scales

## Slide 16: High-Brightness DLA Beams for Ultrafast Electron Diffraction – Renkai Li (SLAC, Tsing Hua U., Beijing)
  e- probes can tackle broad range of scientific puzzles
  Imaging and energy loss spectroscopy more challenging, which require energy spread and stability
  DLAs based UED will be compact, all optical control
  Lower emittance, potentially reduced time-of-arrival jitter
  Promising sources for UED with improved probe size, q-resolution, and temporal resolution
Parameters | Values
rep. rate | SS - 180 Hz
beam energy | 2 - 4 MeV
bunch charge | 104-106
emittance | 2 - 20 nm
bunch length | <50 fs rms
Typical UED beam parameters

## Slide 17: Optical structures naturally have sub-fs time scales and favor high repetition rate operation
DLA's attosecond bunch structure raises the possibility of making attosecond radiation pulses
D. Black, et al. PRL 123, 264802 (2019)
Shönenberger, et al., PRL 123, 264803 (2019)

## Slide 18: EUV Attosecond Frequency Comb
Parameter | Unit | Value
Beam Energy | MeV | 40
Microbunch Charge | fC | 10
Undulator Period | µm | 250
Number of periods / Delay Modules | # | 10 / 100
EUV Photon Energy | eV | 50
Radiated Pulse Energy | nJ | 100
Modelocking scheme proposed could enable attosecond radiation pulses
(R. J. England, Z. Huang, FLS 2018)

## Slide 19: DLA X-ray FEL Strawman Parameter Table
* 1 “SBU” = ph/s/mm2/mrad2/0.1%BW
Parameter | Units | Value
Ebeam Energy | GeV | 1.056
Microbunch Charge | fC | 0.5
Bunches per Train |  | 150
Rep Rate | MHz | 100
Normalized Emittance | nm | 0.87
Laser Wavelength | µm | 2
Laser Pulse Duration | ps | 1
Undulator Period | mm | 0.9
Equivalent Undulator B | T | 1.6
Undulator K |  | 0.14
Pierce Parameter |  | 2.29E-04
Undulator Length | m | 0.9
Photon Energy | keV | 11.5
Gain Length | m | 0.18
Photons per Bunch |  | 6.6E+04
Photon Flux | photons/sec | 9.9E+14
Brightness | SBU* | 1.05E+21
A DLA X-ray source would be in or near the Quantum FEL regime:

## Slide 20: A miniaturized attosecond XFEL could enable revolutionary new science capabilities.
Concept for multi-axis ultrafast tomography with DLA based XFELs (K. Wootton)
• Improved access for universities
• Ultrafast (attosec) pulses
molecular movies
atomic physics
• Inexpensive solid state devices
• Portable security scanners

## Slide 21: What about protons or ions?
Parameter | Value
Proton Energy | 15 keV to 1 MeV
Beam power | 1 MW
Beam Brightness | low / unimportant
Desired Delivery Parameters (c/o: Dr. M. Thompson, Tri-Alpha)
• In principle DLA can accelerate heavier charged particles.
• Existing tabletop p+ sources not suitable for a final device, but may be useful for demonstration tests; feasibility studies needed.
• Demonstration experiments would be interesting with suitable test facilities.
Parameter | Value
Proton Energy | > 10 MeV desired
Size | Compact (< 1 meter)
Emittance | << 1 µm
Beam format | Pulsed, laser synced, high rep rate (MHz)
Preliminary Estimated Source Requirements
Reduce size/cost for colliding beam fusion reactor (CBFR).
Possible uses for plasma diagnostic measurements of ion temperature, plasma density with lower beam powers.
Motivation
Commercialization of Nuclear Fusion Summit (CNFS) – SLAC, 2017

## Slide 22: Applications Timeline
Application | Field | Time-Scale | Kinetic Energy | Species | Beam Power
Radiobiology | Science | 5 yrs | 100 keV to 5 MeV | e- | 5 mW
UED/UEM Source | Science | 5 yrs | 1-5 MeV | e- | 10 to 50 µW
Catheterized Electron Source | Medical | 5 yrs | 1 to 10 MeV | e- | 1-3 mW
Compton X-ray Source | Medical | 5-10 yrs | 10 to 60 MeV | e- | 20 to 60 mW
Low-power EUV | Industry | 5-10 yrs | 10 to 100 MeV | e- | 0.5 W
Proton/Hadron Therapy | Medical | 10-20 yrs | 70 to 250 MeV | p+ | 3-400 mW
Compact XFEL | Science | 10-20 yrs | 1 GeV | e- | 1.5 kW
Multi-Axis Tomography | Science | 10-20 yrs | 1 GeV | e- | 1.5 kW
Colliding Beam Fusion | Industry | 20+ yrs | 15 keV to 1 MeV | p+ | 1 MW
Linear Collider | HEP | 20+ yrs | 1 to 10 TeV | e-/e+ | 10 to 200 MW
AB Recommendation #11: A clear picture/diagram should be developed showing the timeline for different DLA applications and the most important beam parameters

## Slide 23: 3rd Workshop on Applications of Dielectric Laser Accelerators
Date: Tues March 10, 2020
Satellite meeting of the March ACHIP collaboration meeting.
Room reservations made at the Boulderado Hotel.
Proposed session topics: Biomedical, Attosecond science, UED/UEM, and Industrial EUV
Workshop charge: to develop performance requirements and R&D roadmap for a DLA based source in consultation with experts in relevant fields.
Due to reduced attendance on account of coronavirus, we will augment this workshop with a follow-up teleconference in the next few weeks. This will allow international colleagues to more easily contribute.

## Slide 24: Proposed Charge Questions for Each Application
What characteristics of the DLA approach make it attractive for this application area?
Are there new capabilities that would be uniquely enabled (i.e. which could not be done with a conventional accelerator system)?
What are the minimum required accelerator performance parameters for useful application of the technology?
What are the primary R&D challenges and time scale to achieve needed performace?
Google doc created at the following link to facilitate group editing:
https://docs.google.com/document/d/1pq4UM53rHdNySY4I0W1OLuavIJPqctJIrq5sWg3ZVX4/edit?usp=sharing

## Slide 25: Schedule for Today

## Slide 26: Thank you!
contact: england@slac.stanford.edu
Special thanks to K. Leedle, Z. Huang, Y-C. Huang, T. Hirano, U. Niedermayer for contributions of slides.
http://achip.stanford.edu
http://slac.stanford.edu/dla
Group photo, ACHIP collaboration meeting at DESY, Hamburg, Germany, Sept 19-21, 2018.