## Slide 1: Geant4 Electromagnetic Physics Introduction
Editors:
Michel Maire (LAPP, Annecy, France)
Vladimir Ivanchenko (CERN & EMSU, Moscow)
Sebastien Incerti (CNRS/IN2P3, France)
on behalf of the Geant4 Standard EM and Low Energy EM Physics Working groups
Geant4 tutorial MC-PAD Network Training Event 28-30 January 2010, DESY V. Ivanchenko

## Slide 2: Outline
Electromagnetic (EM) physics overview
  Introduction
  Structure of Geant4 EM sub-packages
  Processes and models
Geant4 cuts
  Cut in range and energy thresholds
How to invoke EM physics in Geant4
  EM Physics Lists
  How to extract physics?

## Slide 3: Electromagnetic (EM) physics overview

## Slide 4: Geant4 Electromagnetic Physics
Release with the 1st version of Geant4 with EM physics based on Geant3 experience (1998)
Significant permanent development in many aspects of EM processes simulation since the beginning up to now
Many years is used for large HEP experiments
  BaBar, SLAC (since 2000)
  LHC experiments ATLAS, CMS and LHCb (since 2004)
Many common requirements for HEP, space, medical and other applications
EM web page (common for Standard and Low-energy working groups):
http://cern.ch/geant4/collaboration/working_groups/electromagnetic/index.shtml

## Slide 5: Geant4 simulation of ATLAS experiment at LHC, CERN

## Slide 6: Gamma and Electron Transport
Photon processes:
  γ conversion into e+e- pair
  Compton scattering
  Photoelectric effect
  Rayleigh scattering
  Gamma-nuclear interaction in hadronic sub-package CHIPS
Electron and positron processes:
  Ionization
  Coulomb scattering
  Bremsstrahlung
  Nuclear interaction in hadronic sub-package CHIPS
Positron annihilation
HEP & many other Geant4 applications with electron and gamma beams
HEP calorimeter
Medical linac

## Slide 7: Geant4 EM packages
Standard
  g, e up to 100 TeV
  hadrons up to 100 TeV
  ions up to 100 TeV
Muons
  up to 1 PeV
  Energy loss propagator
Xrays
  X-ray and optical photon production processes
High-energy
  Processes at high energy (E>10GeV)
  Physics for exotic particles
Polarisation
  Simulation of polarized beams
Optical
  Optical photon interactions
Adjoint
  New sub-library for reverse Monte Carlo simulation from the detector of interest back to source of radiation
Utils – general EM interfaces
Low-energy
  Livermore library g, e- from 10 eV up to 1 GeV
  Livermore library based polarized processes
  PENELOPE code rewrite , g, e- , e+ from 250 eV up to 1 GeV
  hadrons and ions up to 1 GeV
  Microdosimetry models (Geant4-DNA project) from 7 eV to 10 MeV
  Atomic deexcitation

## Slide 8: Software design
Since Geant4 9.3beta (June, 2009) the design is uniform for all EM packages
  Allowing a coherent approach for high-energy and low-energy applications
A physical interaction or process is described by a process class
  Naming scheme : « G4ProcessName »
  For example, G4Compton for photon Compton scattering
  Assigned to Geant4 particle type
  Inherit from G4VEmProcess base class
A physical process can be simulated according to several models, each model being described by a model class
  Naming scheme : « G4ModelNameProcessNameModel »
  For example, G4LivermoreComptonModel
  Models can be assigned to certain energy ranges and G4Regions
  Inherit from G4VEmModel base class
Model classes provide the computation of
  Cross section and stopping power
  Sample selection of atom in compound
  Final state (kinematics, production of secondaries…)

## Slide 9: Comments
The list of available processes and models is maintained by EM working groups in EM web pages
It is shown in Geant4 extended and advanced examples how to use EM processes and models
User feedback always welcome

## Slide 10: Geant4 Cuts

## Slide 11: Example: Muon Energy Loss
Continuous energy loss
  Contribution from processes:
    Ionization
    Bremsstrahlung
    Production of e+e-
Tcut – cut energy
Transfers above Tcut are sampled
Below 200 keV – ICRU’49 parameterization of dEdx
Radiative corrections to ionization at E > 1 GeV
Total muon energy loss

## Slide 12: Geant4 Cuts
No tracking cuts by default
Unique production threshold definition via RANGE
For a typical process (G4hIonisation, G4eIonisation, …) production threshold Tc subdivides continues and discrete part of energy loss:
  Energy loss
  -electron production
By default energy loss is deposited at the step
Optionally energy loss can be partially used
  for generation of extra -electrons under the threshold when track is in vicinity of a geometry boundary (sub-cutoff)
  for sampling of fluorescence and Auger–electrons emission

## Slide 13: Effect of Production thresholds
Pb
Liquid
Ar
Liquid
Ar
Pb
500 MeV incident proton
Range threshold: 1.5 mm
455 keV electron energy in liquid Ar
2 MeV electron energy in Pb
one must set the cut for delta-rays (DCUTE) either to the Liquid Argon value, thus producing many small unnecessary d-rays in Pb,
or to the Pb value, thus killing the d-rays production everywhere
Geant3
DCUTE = 455 keV
DCUTE = 2 MeV

## Slide 14: What processes are using cuts?
Energy thresholds for gamma are used in bremsstrahlung
Energy thresholds for electrons are used in ionisation and e+e- pair production processes
Energy threshold for positrons is used in the e+e- pair production process
Energy thresholds for gamma and electrons are used optionally (“ApplyCuts” options) in all discrete processes
  Photoelectric effect, Compton, gamma conversion
Energy threshold for protons are used in processes of elastic scattering of hadrons and ions defining the threshold for kinetic energy of nuclear recoil
  New feature available since December 2009

## Slide 15: Comments
Range cut approach was established for simulation of energy deposition inside solid or liquid media
  Sampling and crystal calorimeters
  Silicon tracking
For specific user application if may be revised, for example, by defining different cuts in range for electron and gamma
  Gaseous detectors
  Muon system
Tracking cuts may be useful (saving some CPU) for simulation of penetration via shielding or for simulation in non-sensitive part of the apparatus
  Astrophysics applications

## Slide 16: How to invoke EM physics in Geant4?

## Slide 17: Physics List
Physics Lists is the user class making general interface between physics and Geant4 kernel
  It should include the list of particles
  The G4ProcessManager of each particle maintains a list of processes
There are 3 ordered lists of processes per particle which are active at different stage of Geant4 tracking:
  AtRest (annihilation, …)
  AlongStep (ionisation, bremsstrahlung, …)
  PostStep (photo-electric, Compton, Cerenkov,….)
Geant4 provided a set of different configurations of EM physics (G4VPhysicsConstructor) with physics_list library
These constructors can be included into modular Physics List in user application (G4VModularPhysicsList)

## Slide 18: EM Physics Constructors for Geant4 9.3
G4EmStandardPhysics – default
G4EmStandardPhysics_option1 – HEP fast but not precise
G4EmStandardPhysics_option2 – Experimental
G4EmStandardPhysics_option3 – medical, space
G4EmLivermorePhysics
G4EmLivermorePolarizedPhysics
G4EmPenelopePhysics
G4EmDNAPhysics
Located at $G4INSTALL/source/physics_list/builders
Advantage of using of these classes – they are tested on regular base and are used for regular validation
Combined Physics
Standard > 1 GeV
LowEnergy < 1 GeV

## Slide 19: Example - G4EmStandard Physics
G4ProcessManager* pmanager
If ( particleName == “gamma” ) {
pmanager->AddDiscreteProcess(new G4PhotoElectricEffect);
pmanager->AddDiscreteProcess(new G4ComptonScattering); pmanager->AddDiscreteProcess(new G4GammaConversion);
} else if ( particleName == “e+” ) {
pmanager->AddProcess(new G4eMultipleScattering, -1, 1, 1);
pmanager->AddProcess(new G4eIonisation, -1, 2, 2);
pmanager->AddProcess(new G4eBremsstrahlung, -1, 3, 3);
pmanager->AddProcess(new G4eplusAnnihilation, 0, -1, 4);
Numbers are process order;
  G4Transportation is the 1st (order = 0) for AlongStep and PostStep
“-1” means that the process is not active
Only PostStep
3 stages

## Slide 20: Example G4EmPenelopePhysics
Process class G4PhotoElectricEffect
Default model in g4 9.3 is G4PEEffectModel (EM Standard)
There are alternative Livermore and Penelope models
Example of the combined EM Physics Lists:
………
G4double limit = 1.0*GeV;
If ( particleName == “gamma” ) {
G4PhotoElectricEffect* pef= new G4PhotoElectricEffect();
G4PenelopePhotoElectricModel* aModel = new
G4PenelopePhotoElectricModel();
aModel->SetHighEnergyLimit(limit);
pef->AddEmModel(0, aModel); // 1st parameter - order
pmanager->AddDiscreteProcess(pef);
…….

## Slide 21: How to extract Physics ?
Possible to retrieve Physics quantities using a G4EmCalculator object
Physics List should be initialized
Example for retrieving the total cross section of a process with name procName: for particle partName and material matName
#include "G4EmCalculator.hh"
...
G4EmCalculator emCalculator;
G4Material* material =
G4NistManager::Instance()->FindOrBuildMaterial(“matName);
G4double density = material->GetDensity();
G4double massSigma = emCalculator.ComputeCrossSectionPerVolume (energy,particle,procName,material)/density;
G4cout << G4BestUnit(massSigma, "Surface/Mass") << G4endl;
A good example: $G4INSTALL/examples/extended/electromagnetic/TestEm14
Look in particular at the RunAction.cc class

## Slide 22: Let us start exercises of task 1.3
• Tutorial Material online task 1.3: http://www.ifh.de/geant4/g4course2010/task3