## Slide 1: Preparation for ZZ and recovery after access
Thomas Wamsat
July 28, 2020

## Slide 2: Topics
Magnet current during ZZ
ZZ Injector
Restart Injector after ZZ
ZZ XTL
Restart XTL after ZZ
ZZ XTD-1-3-4-7-
Restart XTD-1-3-5-7 after ZZ
ZZ XTD-2-4-10-
Restart XTD-2-4-10- after ZZ
ZZ and Restart XTD6 and XTD9
Useful hints

## Slide 3: Magnet current during ZZ
Before ZZ with magnets under current, MXL or RCs make a safety audit to ensure that there is no work near the beam pipe
Point out to the colleagues who enter the tunnel that the magnet current is on
Also the shift leaders should point that out while the ZZ team enters the ZZ door
Under this conditions ZZ with magnets under current and without attendance of MKK colleagues is permitted
Injector and XTL all magnet connections are covered
XTD1-3-5-7 and XTD2-4-10 not every magnet connection is covered sufficiently
  In XTD1-3-5-7 and XTD2-4-10 using a bike with magnets under current is prohibited

## Slide 4: ZZ areas
Injector
XTL
XTD1-3-5-7 (SASE2 branch)
XTD2-4-10 (SASE1 branch)
XTD6 (SASE2 Photon tunnel)
XTD9 (SASE1 photon tunnel)
XTD8 (empty tunnel)

## Slide 5: ZZ Injector
Save a file (sequencer)
Close beam shutter BS I1
Switch of RF
  GUN
  A1 and AH1 (with energy manager)
  Injector TDS (uncheck RF on/off)
In case of work near beam pipe, switch off and ground magnets
  Use ‘Magnet overview’ panel to switch off magnets and ask MKK for grounding (also Dump dipole will be switched off, no effect on XTL beam permission
Delete beam permission

## Slide 6
Ask MKK to unground magnets
Switch on magnets and load file values
Start Beam warning Injector
Open beam shutter BS I1
Grant beam permission
Switch on RF
  GUN (see training “GUN operation”)
  A1 and AH1 with energy manager
  Injector TDS
Restart Injector after ZZ

## Slide 7
Save a file
Use sequence “Separate Injector from XTL” to keep Injector running
Shut down RF by using “Linac Energy Manager”
Shut down TDS B2 (press STBY)
In case of work near beam pipe, switch off and ground magnets
  Use ‘Magnet overview’ panel to switch off magnets by clicking on each section and press Switch off
  Ask MKK for grounding
Switch off orbit- and longitudinal feedbacks
ZZ XTL

## Slide 8
Restart XTL after ZZ
Unground magnets
Switch on magnets and load file
Cycle all main magnets
Ask Shift leader for beam permission
Restart RF using the ‘Linac Energy Manager’
  See training “LLRF”
Use sequence “Join Injector with XTL”
Use corrector CBB.62.I1D to correct orbit and re-establish transmission
Switch on orbit FBs to re-establish transmission
Switch on longitudinal FBs successively

## Slide 9: ZZ XTD1-3-5-7 (South branch SASE2)
Save a file
Use sequence “Separate SASE2 from XTL”
In case of work near beam pipe, switch off and ground magnets
  Use ‘Magnet overview’ panel to switch off magnets by clicking on each section and press Switch off
  Ask MKK for grounding

## Slide 10: Restart XTD1-3-5-7 after ZZ
Use sequence “Join SASE2 with XTL”
Cycle special grounded magnets
In case magnets were grounded, unground, switch on and reload file and cycle main magnets
Switch on orbit FB to re-establish transmission (maybe load orbit from saved file before)

## Slide 11: ZZ XTD2-4-10 (North branch SASE1/3)
Save a file
Use sequence “Separate SASE1/3 from XTL”
In case of work near beam pipe, switch off and ground magnets
  Use ‘Magnet overview’ panel to switch off magnets by clicking on each section and press Switch off
  Ask MKK for grounding

## Slide 12: Restart XTD2-4-10 after ZZ
Use sequence “Join SASE1/3 with XTL”
Cycle special grounded magnets
In case magnets were grounded, unground, switch on and reload file and cycle main magnets
Switch on orbit FB to re-establish transmission (maybe load orbit from saved file before)

## Slide 13: ZZ XTD6 and XTD9
No magnets in this areas
For ZZ in XTD6 close BS TD6
For ZZ in XTD9 close BS TD9

## Slide 14: Useful hints
Beam warning, as requirement for beam permission, for all interlock section except the injector, can only be given when all interlock keys are locked

## Slide 15: Useful hints
Media shaft XSIN can be entered without breaking the injector interlock via door in UG4 with additional keys at Injector BKR interlock rack