## Slide 1: ECAL for the LUXE CDR
Wolfgang Lohmann

## Slide 2: Phase 1 calorimeter
LUXE needs an electromagnetic calorimeter to count the number of electrons and to measure the energy spectrum
Highly granular
Highly compact
Fiducial volume 50 x 10 x 10 cm3
Good energy resolution
Moderate timing
Moderate radiation hardness

## Slide 3: Calorimter of the LUXE experiment

## Slide 4: Phase 1 calorimeter
Ideal case:
Compact detector planes
FCAL technology (compactness)
Pad size 5 x 5 mm2
Tungsten absorber thickness
1 X0

## Slide 5: Phase 1 calorimeter
Budget contains core costs (no R&D)
Budget contains person power (to be hired for the project
(engineers, technicians)
Weigth: 50 kg
Sensor area: 6000 cm2
Readout channels: 25000
Investment: 250 k (to be detailed)
Engineering personpower

## Slide 6: Phase 1 calorimeter
Electron spectrum
Number electrons
Mechanics
Mechanics |  |  | 
 | number | price | total
tungsten plates | 100 | 70 | 7000
support frames | 1 | 4000 | 4000
sensor support structures (carbon etc) | 100 | 300 | 30000
Connectivity
fan out Kapton HV | 100 | 60 | 6000
fan out Kapton, signal | 100 | 60 | 6000
Silicon sensors
Comment from Roman: use insted of 6$ per cm2 better 10 $, would lead to roughly 60 k

## Slide 7: Phase 1 calorimeter
FE ASICs
Comment from Marek: production costs will be larger, about 100l, to be clarified
FE electronics
Comment from Roman: CMS HGCal used 140$ per PCB, would result to 14 k

## Slide 8: Phase 1 calorimeter
Power supplies
DAQ

## Slide 9: Phase 1 calorimeter
Tooling (jigs, bonding machine supplements, test stands)
Engineering person power (Hired for the project)
sum

## Slide 10: Phase 0 calorimeter
What we have so far:
option for an ECAL
Calice prototype
A dedicard demonstrator of the phase 1 calorimeter (one section of the phase 1 calorimeter
What is missing:
For 1: the Calice prototype is less compact, i.e. some simulation on the performace is needed;
Technical: who will install it, who will pay for it, how to integrate it in the LUXE readout
For 2: prefered solution, but needs investment in tungsten plates (JINR?), sensors, and FE electronics, DAQ, physics potential.

## Slide 11: Phase 0 calorimeter
Calice prototype: cost estimate to be done
One module of the phase1 calorimeter

## Slide 12: Phase 0 calorimeter
Option 3: LUXE phase 1 demonstrator
6‘‘ sensors, 10.5 x 5.5 cm2 , 5 x 5 mm2 pad size, 25 pieces
Detector planes using FCAL technology
Flame readout, 5000 channels, plus data concentrator
Tungsten plates (25) from JINR
Excellent device for high granularity and compact electromagnetic calorimeter studies

## Slide 13: Phase 0 calorimeter
tungsten plates | 20 | 70 | 1400
support frames | 1 | 4000 | 4000
sensor support structures (carbon etc) | 20 | 300 | 6000
Mechanics
Connectivity
fan out Kapton HV | 20 | 60 | 1200
fan out Kapton, signal | 20 | 60 | 1200
Silicon sensors
Comment from Roman: use insted of 6$ per cm2 better 10 $, would lead to roughly 12 k

## Slide 14: Phase 0 calorimeter
FE ASICs
FE electronics
Power supplies
prototyping, ASICs | 50 | 1000 | 50000
channels | 5000 | 1,5 | 7500
probecard for tests | 1 | 20000 | 20000
PCB and assemply | 20 | 70 | 1400
auxiliary components |  |  | 5000
Comment from Roman: CMS HGCal used 140$ per PCB, would result to 3 k
HV |  |  | 2000
LV |  |  | 2000
cables and connectors, patch panels |  |  | 5000

## Slide 15: Phase 0 calorimeter
DAQ
Tooling
sum
Receiver cards | 20 | 300 | 6000
crates | 1 | 1000 | 1000
crate computer | 1 | 1000 | 1000
racks | 1 | 2000 | 2000
Engineering person power (Hired for the project)

## Slide 16: ECAL LUXE CDR
Who may do what (phase 0):
Hopes:
Yan may find out with Roman what is a realistic way to include the Calice prototype in LUXE.
For the demonstrator some clarification is needed from TAU and UST (funding applications, personpower)