## Slide 1: Phase velocity measurement
Calibration free characterization of integrated Terahertz waveguides
Max Kellermeier
Francois Lemery, Klaus Flöttmann, Ralph Aßmann, Wolfgang Hillert
max.kellermeier@desy.de
17 August 2020

## Slide 2: Agenda
Introduction
Measurement Principle and Four term error model
Current measurement results
Discussion and Outlook
Notes: Why?
What and how?
Show results
Limits and outlook

## Slide 3: Agenda
Introduction
Measurement Principle and Four term error model
Current measurement results
Discussion and Outlook
Notes: Why?
What and how?
Show results
Limits and outlook

## Slide 4: Introduction: AXSIS
Fully Coherent Attosecond X-ray Source
Based on THz Acceleration and Inverse Compton Scattering
Frontiers in Attosecond X-Ray Science: Imaging and Spectroscopy
Notes: to outrun radiation damage effects due to the necessary high X-ray irradiance
Phase velocity here not refering to the accelerating mode but the fundamental mode
Still useful insights about the waveguide

## Slide 5: Introduction
Emerging interest in THz waveguides in the accelerator community:
  “Active devices” which are driven by external THz sources (streaking, accelerating)
  “Passive devices”: Beam-driven, acts as THz source
Due to small feature sizes  monolithically integrated coupler and waveguide preferential
How to characterize the waveguide if you cannot separate it from the coupler?
Critical quantity: phase velocity
  In case of horn coupler: Causes additional phase shift
Notes: A more general introduction
Waveguides:
  Simple funnel and tube in a solid block
  More advanced couplers like the one from Francois proposal for THz generation
  Or this fancy side couplers foreseen by our CFEL collegues for AXSIS
Phase velocity: keep phase slippage as small as possible
Relatively short waveguides  phase shift at horn matters

## Slide 6: Introduction
State of the art
Mitrofanov, O. et al. “Reducing Transmission Losses in Hollow THz Waveguides.” IEEE Trans. THz Sci. Tech, 2011.
Georgiadis, V. et al. “Characterizing the Accelerating Mode of a Dielectric-Lined Waveguide Designed for Terahertz-Driven Manipulation of Relativistic Electron Beams.” 44th IRMMW-THz, 2019.
1200 μm
575 μm
DLW exit
695 μm
S.P. Jamison, “Terahertz Driven
Particle Acceleration of relativistic beams”, 4th EAAC, 2019. (unpublished)
Notes: Mitrofanov:
  Optically generated THz
  First waveguide used as luncher, no coupler included
  Long waveguide (120 cm)  phase shift from coupling negligible
  2.2 mm diameter Ag/PS waveguide
  Single cycle pulse, using spectrogram, i.e. frequency depending on time  limited by capabilities of the transform
Group at CLARA in Daresbury applied same optical setup:
  Traces shown  Phase and power spectra extracted but haven’t seen a dispersion line so far
  My guess: Horn contribution can’t be taken out

## Slide 7: Agenda
Introduction
Measurement Principle and Four term error model
Current measurement results
Discussion and Outlook
Notes: Why?
What and how?
Show results
Limits and outlook

## Slide 8: Measurement Principle
VNA: Fixed frequency  unknown wavenumber and wavelength in waveguide
Inspired by lower frequency techniques: Trombone for impedance matching (Constant impedance adjustable coaxial line)
By varying the length of the coaxial  change circuit from “open” to “short” (180° phase)
Measured length corresponds to half wavelength  phase velocity
Short-circuit
VNA Testport
Notes: In RF field: wavevector usually beta instead of k
VNA sends out CW signal
Trombone: same principle applied in music instrument
  RF device: Denoted as phase adjusters, line stretchers
One port to VNA, one short-circuited

## Slide 9: Measurement Principle
Why not trombone?
  Current upper frequency limit: ~ 20 GHz
  Required feature sizes of transition infeasible
  Connector can cause significant effect
Transmission Method
Using phase difference between S21 and S11
But phase ambiguity
Reflection Method
Circuit does not have to be closed, only a reflecting obstacle
Obstacle movable (subwavelength scale)  measure phase difference
Notes: Two main aspects:
  Feature sizes required for a trombone mechanism infeasible at these high frequencies
  Connector can cause significant contribution, similar to horn
    At low frequencies the impedances of the connectors are matched
Generalization:
  Why short-circuit? Any reflection exploited
  Length of device fixed  change position of the origin of the reflection
Comment on Transmission technique:
  S-parameters are applied for Linear Time invariant systems  no time information
  Even though both reflection and transmission  phase ambiguity (30° vs. 390°)

## Slide 10: Four Term Error Network Model
Issue: Waveguide embedded in single block with horn  can’t be attached to VNA port (ref. plane)
Additional out-coupling horn and free space
Goal: self-calibration with measurements at different positions
Four Term Error Model
i-th measurement
Notes: But: Principle does not account for couplers and freespace propagation  multiple reflections at interfaces and interference
 Self-calibration method, denoted as 4-term error model
Illustrated here: horns , freespace, waveguide, obstacle
S-matrix for a waveguide, gamma includes the wavevector beta, k denoted as propagation factor
Doing the math:
  Reflection from each network interface is a Möbius transform
  arrive at S-parameter measured at test port
  Terms similar to a standard Open-Short-Match calibration (directivity, source match, reflection tracking)

## Slide 11: Experimental Setup and Waveguide Structure
Frequency range: 220 GHz – 330 GHz (Streaking: 267 GHz, AXSIS: 300 GHz)
Obstacles:
  Syringe + Canula as obstacle (OD = 0.72 mm, ID = 0.41 mm), on motorized stage (+/- 1 µm)
  Paper clip (OD = 0.89mm)
  New: steel welding wire
Three different waveguide structures:
  Conical horn drilled in copper monolithically
  Same, but in brass
  EDM machined in two half shelves, “split waveguide”

## Slide 12: S11 depending on position in 4-term error model
Measured:
analyzed independently for each frequency point:
Copper Waveguide 1
Notes: After measurement set: data set of S_11(f,l)
Analyzed separately for each frequency point by fitting the 4-term error model to it
Example: Real and Imaginary part versus obstacle position, for selected frequency point
Nice sine wave, but does not have to be the case in the 4-term error model
  Contributions from error term b and c can significantly distort the shape of the waveform
  Here: b and c small

## Slide 13: Agenda
Introduction
Measurement Principle and Four term error model
Current measurement results
Discussion and Outlook
Notes: Why?
What and how?
Show results
Limits and outlook

## Slide 14: Analysis based on 4-term error model
Copper waveguide
Tweaking initial parameters for least squares problem  Curve fit works
Better result than harmonic analysis (FDM)
Notes: Measurement 05
What do you see here?
In blue (behind the orange one): phase velocity computed from the 4-term error model (for each frequency point independently!)
In orange: fitting the dispersion line of the analytical solution for a metallic waveguide
In green: prediction based on the aperture measured under the microscope  a circle detection algorithm applied to the microscope image (Hough transform + accumulator)
Measurement does not fall into the error band of the prediction
  Uncertainty in radius might be too optimistic
  Hole drilled  might be larger at the outside than inside
   fit result more trusted than the microscope image

## Slide 15: Brass waveguide
Notes: Measurement 7
Same as before, with brass wvg
Measured dispersion line smoother than the copper one
Microscope image looks already cleaner

## Slide 16: Split waveguide
Measured with different obstacles
Checked reproducibility
Notes: Measurement 12
Third Last metallic waveguide
Cross section at exit and inside are more likely to be the same as EDM machined, not drilled
Prediction and Measurement match well up to a certain frequency of 280 GHz
What happened there? Verified by another measurement

## Slide 17: Multimode excitation in split waveguide,
Above failing frequency
Amplitude (a.u.)
Notes: At single frequency point: S_11(l)
Beat of two different wavelengths directly visible  Fit fails, 4-term error model does not include multiple modes
Transform to Fourier Domain (k-space) confirms the interpretation: Two wavevector components with almost equal amplitude

## Slide 18: Higher order modes in metallic waveguide
TEmn/TMmn refer to analytical dispersion relations
Using radius from microscope image:
FDM finds a lot more modes, only selected “mode 1” and “mode 2”
Notes: Measurement 12
Applying a Fourier Domain analysis using FDM  multiple dispersion lines found
FDM useful but can’t describe error terms so not as accurate as 4-term error model in general
Solid lines: Analytical modes expected from radius
TE_01 hidden behind TM_11
Apart from fundamental mode:
  Dispersion line close to TE21 but clearly separate
  TM11 matches very well
Still unclear why TE_21 is so far off

## Slide 19: Split waveguide with dielectric
Preliminary result
Truncated S11(l) due to poor signal probably due to movement of the dielectric
Notes: M.13
Capillary inserted in waveguide
3d printed capillary  far from perfect (not centered, sprues on the outside distorting the waveguide inside)
Dispersion line got pulled down (in fact, pulled down too far)
We would like to cross the speed of light

## Slide 20: Agenda
Introduction
Measurement Principle and Four term error model
Current measurement results
Discussion and Outlook
Notes: Why?
What and how?
Show results
Limits and outlook

## Slide 21: Discussion
Uncertainty in S-parameter below 1‰ (95% confidence interval)
4-term error model sufficient for modelling the studied waveguides
  Effective inner diameter for metallic waveguides
  Phase velocity below c in dielectric loaded waveguide
Limits of 4-term error model:
  Effects of transitions should be small  long waveguide section
  No reflection from behind the obstacle  obstacle not too small
    extended model includes 9 unknown terms
  Single mode excitation necessary
Improving obstacle:
  Ideal: Closed circuit, “short”, infeasible
  Set of rods of different outer diameters
Waveguides:
  Imperfect Environment (oxidation of copper) and material (standard copper)
  Dielectric layer far from acceptable

## Slide 22: Outlook
Improve obstacle
Continue uncertainty evaluation
Compare result of brass waveguide with EO sampling measurement
Continue measurements with dielectric (better capillaries)  matching phase velocity
Acknowledgements:
Francois Lemery, Thomas Vinatier, Klaus Flöttmann, Wolfgang Hillert, Ralph Aßmann, Hannes Dinter, Frank Mayet, Christian Henkel, Immo Bahns, Patrick Rauer, Markus Hünning

## Slide 23: Backup

## Slide 24: S-Parameters for Phase Velocity Measurement (Simulation)
Simple rectangular waveguide (WR-3)
Length: 11.613mm
Simulated S_21
Phase velocity from unwrapped phase

## Slide 25: Extended 9-Term Error model
Issue: canula and waveguide wall form coaxial line  additional reflection from waveguide end (interpretation after first measurements)

## Slide 26: Extended 9-Term Error model
Issue: canula and waveguide wall form coaxial line  additional reflection from waveguide end (interpretation after first measurements)
Doesn’t work!
Not even in simulation, too many unknowns (9)

## Slide 27: Poor man’s solution: Time Gating
Time Domain Gating (without free space calibration):
Transform from Frequency domain to Time Domain (incomplete time domain information, but helpful tool)
apply window (here: Kaiser instead of Hann)
transform back
Drawbacks:
Wiggles in frequency domain
Result depends on window parameters (center and span)
Frequency band must be truncated at the edges (DFT assumes a periodic signal, which the S-parameter clearly isn’t)
Phase information in bandpass transform susceptible to transform

## Slide 28: Measurement result with Time Domain Gating, I

## Slide 29: Measurement result with Time Domain Gating, II

## Slide 30: Fit dispersion curve
Comparing dispersion curves
  Measured (using time gating)
  Fit to measured data  0.50 mm
  Expected from measured aperture diagonal
  Fits from last 10 measurements (from 11.5 mm):

## Slide 31: Impact of Gate parameters

## Slide 32: 4-term error model would be better
Per-Frequency analysis
Does not rely on incomplete time domain information
But:
  error function depends on starting point
  Complex error function
  Sensitive to phase error
solving for a, c, b with pairs of measurements and back-substitution
Root finding problem

## Slide 33: Four-term error model applied
Using measurement at 10.00, 10.50, 11.00, 11.50 mm

## Slide 34: Time domain transform at different obstacle position

## Slide 35: Time domain transform of obstacle free measurements
Measurement from 2020.07.02

## Slide 36: Harmonic analysis
Comparison to time domain gating
Based on time domain gating
Based on harmonic analysis

## Slide 37: Analysis based on 4-term error model
While tweaking initial parameters for least squares problem: Found sign error
 Curve fit works
Better result than harmonic analysis

## Slide 38: Phase velocity measured with EO sampling

## Slide 39: THz traces with EO sampling

## Slide 40: Calibration coefficients
Magnitude and unwrapped phase

## Slide 41: Calibration coefficients
Real and Imaginary

## Slide 42: Uncertainty in S-parameter
Waveguide 2 (brass)
At a fixed position of the obstacle
Notes: Measurement 17

## Slide 43: Split waveguide with dielectric, S11
S11 at low frequency

## Slide 44: Split waveguide with dielectric, S11
S11 at medium frequency

## Slide 45: Split waveguide with dielectric, S11
S11 at high frequency