Snow on IceTop
Patrick Berghaus
Zeuthen Group Meeting
09-04-09

---
Deployment

---
IceTop Station

---
IT 59
IT 40
IT 26
IT 16

---
axis
Factor 3

---
DOM Launches
Source: Serap
Factor 3

---
Tank A-Tank B Coincidences

---
Tank Calibration
Muons
/EM Bkg
Integration
Range

---
snow removed

---
snow filled in

---
IceTop Simulation Scheme
gammas
electrons
muons
hadrons
TankTop: GEANT-based
surface tank simulation
too CPU-
intensive
CORSIKA air shower
simulation
Response parametrization
In dependence of particle
type and energy
Add Snow
IceTop full event simulation

---
IceTop Tank
Snow Height
snow
perlite
DOM
DOM
x2 x78
water
65cm
93cm
130cm

---
Air Shower
electromagnetic
particles (e,g)
photons
muons

---
Theoretical Track Length
30° zenith angle
particles
snow
Assumption:
Response a Track Length
Track length

---
g: 10s of MeV
Median energy after
convolution with detector
response (not plotted)
m: several GeV
e:100 MeV

---
Energy deposit is a practical parameter for signal
independent of :	particle type
particle energy
snowdepth

---
TT: Gammas
main contribution to tank signal
Highest Contribution to Signal
Cascade Effects above 1 GeV
Moderate Attenuation

---
Parametrization: Gammas
a+b cdot (ln E)^c a+b cdot (ln E)^c
   Fit Formulas:

---
- energy loss : dE/dx ~3MeV/cm (ice)
- Track length proportionality assumption fails for low energies (stopping tracks) and for short track lengths

---
TT: Electrons
Cascade Effects above 1 GeV
Stronger Attenuation

---
Parametrization: Electrons
a+b cdot (ln E)^c a cdot E^b
   Fit Formulas:

---
100MeV electrons stop in tank
Track length proportionality does not work for higher energies

---
TT: Muons
Cascade Effects small
Threshold increases

---
Parametrization: Muons
a+b cdot E^c
   Fit Formula:

---
muon energy loss in ice (ionization) dE/dx ~ 2MeV/cm
100MeV muons are stopped in 90cm ice
higher energy muons have energy loss proportional to their theoretical track length

---
MC with Snow Parametrization
Old MC
Data
New MC
Ratio New MC/Data

---
Old
New
Zenith

---
Old
New
NTanks

---
IC40:
“Hot” and “Not”
X-Axis Projection

---
IceTop Energy
IceTop vs. InIce Energy
Shift of Energy Measurement
Shift of Threshold

---
Summary
Snow has major influence on IceTop
Event rates decrease 20-25% each year
Diminished sensitivity at knee, high-E
MC promising (Snow easier to model than Ice!)

---
Zenith Angle
Increasing fraction
entering through
side walls
perlite
ice
snow

---
Shower Core x
less snow
more snow
perlite
ice
snow