## Slide 1: Development of a next generation CMOS MAPS for CBM and beyond
PD Dr. Michael Deveaux
on behalf of the MIMOSIS-team.
in collaboration with:

## Slide 2: Initial motivation: CBM
CBM
MVD

## Slide 3: The CBM-MVD, motivation of requirements
Limited detector precision spoils vertex precision.
  Needs <5µm.

## Slide 4: The CBM-MVD, motivation of requirements
Limited detector resolution spoils vertex resolution.
  Needs <5µm.
Multiple coulomb scattering must be reduced.
  Needs x< 0.3% X0.
  Detector in vacuum.
  Low power <100mW/cm²
Collision rate:
  105 Au+Au/s (11 AGeV)
  107 p+Au/s (30 GeV)
  Need high rate capability
 | CBM requirement
Spatial precision | <5 µm
Low power | <100 mW/cm²
Material budget (per station) | 0.3% X0
Calls for CMOS
MAPS

## Slide 5: Additional requirements: Beam and occupancies
Double counting in simulation (simulated sensor overlap)
Size of MIMOSIS-1
Occupancy very inhomogenious.
Strong beam fluctuations expected.
Beam halo ion impacts expected.
CBM requirements (cont.) | 
Rate capability mean (peak) | 20 (80) MHz/cm²
Ion tolerance (10 AGeV Au) | 1 kHz/cm²
J.Pietraszko, private communication
Beam intensity - SIS18
Q.Li, private communication
Curtesy
Courtesy
Beam hole:
11 mm

## Slide 6
Assumption:
Sensor has to withstand 5x106s at 100 kHz Au+Au or 10 MHz p-A.
All numbers hold for the most illuminated 1mm² of the MVD.
 | Requirement
Spatial precision | ~ 5 µm
Time precision | < 5 µs
Sensor thickness | ~50 µm
Power dissipation (full hit density) | 100 mW/cm²
Operation temperature | - 40°C to +30°C
Temperature gradient on sensor | 5 K
Radiation doses (non-ionizing) | ~ 7x1013 neq/cm²
Radiation doses (ionizing) | ~ 5 MRad
Radiation gradient on chip | 100%
HI-tolerance | 10 Hz/mm²
Rate, all hits recorded (average/peak) | 20/80 MHz/cm²
 | Requirement
Spatial precision | ~ 5 µm
Time precision | < 5 µs
Sensor thickness | ~50 µm
Power dissipation (full hit density) | 
Operation temperature | - 40°C to +30°C
Temperature gradient on sensor | 5 K
Radiation doses (non-ionizing) | ~ 7x1013 neq/cm²
Radiation doses (ionizing) | ~ 5 MRad
Radiation gradient on chip | 100%
HI-tolerance | 10 Hz/mm²
Rate, all hits recorded (average/peak) | 20/80 MHz/cm²
approx.

## Slide 7: R&D strategy
MIMOSA-26
On-pixel discrimination.
Speed-up x20
Low power x0.2
In collaboration with:
Depleted MAPS
Rad. hard. >10x ?
In collaboration with:
MIMOSIS
CBM specific:
Beam halo tolerance
~80 MHz/cm² rate
Beam fluctutation

## Slide 8: R&D strategy
Sensor must handle beam
fluctuations in time.
Size of MIMOSIS-1
Sensor must handle occupancy
gradients in space.
Solution:
Discriminator on 27x30µm² pixel.
(5 µs readout time)
Multiple data concentration steps. (early averaging of Poisson fluctuations)
Elastic output buffer.
(max. 3x nominal beam for 50µs)
8 x 320 Mbps links (switchable).
(GBTx compatible)
Triple redundant electronics.
(Become HI-tolerant)
I2C slow control.
Sensor must handle 100kHz Au+Au
MIMOSIS block diagram

## Slide 9: MIMOSIS – R&D schedule
MIMOSIS-0 (2018)
Demonstrate pixel concept.
Demonstrate readout concept.
MIMOSIS-1 (2020)
Add buffer structure.
In beam tests.
SEE hardening 1/2
MIMOSIS-2 (2021e)
On-chip pixel grouping.
Final pixels.
SEE hardening 2/2
MIMOSIS-3 (End 2022e)
Final sensor
We are here
All submissions:
Additional CE18 test structures
to study specific design questions.
MIMOSIS-0
MIMOSIS-1

## Slide 10: First Prototype: MIMOSIS-0
MIMOSIS-0
32 columns of 504 pixels.
Priority encoder (data driven).
Up to 40V depletion voltage.
No data buffers yet.
MIMOSIS-0
1 mm
Pulse injection
DC-pixel
(Inspired by ALPIDE)
AC-pixel
up to 40V HV top bias
Decoupling capacitor
Back bias possible.
P-Well bias (ALPIDE) possible

## Slide 11: MIMOSIS-0: Pulse tests
Pulse injection
55Fe (1640 e)
Rather small time walk & jitter
Signal
~850e
M.I.P ~850e (MPW 25µm epi)

## Slide 12: MIMOSIS-0: Pulse tests
After optimizing trim voltages:
Time walk + jitter < 1µs, pixel busy (analog) ~3µs.
AC pixel (not shown) 30% slower than DC pixel
Might reach time accuracy < 1µs (target frame readout time 5µs)
400
(individual pixel)

## Slide 13: First Prototype: MIMOSIS-0
1 mm
X-ray
Test with test-pulse:
FPN < 12 e ENC, temporal noise <<6 e ENC
Threshold ~120 e (Threshold/Noise = 8)
Very uniform response.
Signal: 850e MPV
Computed estimate.
M.I.P. 25µm-epi.
No charge sharing.

## Slide 14: Results: MIMOSIS-0
Rad tolerance > 3 MRad (after 1 year room temperature annealing)
Handling dose gradients appears feasible.
B. Arnoldi-Meadows, CBM progress report 2019
Manipulation error?
Room temperature

## Slide 15: MIMOSIS – 1 : 1st full size sensor
MIMOSIS-1, 60µm thick
 | MIMOSIS-1 goal
Time precision | < 5 µs
Pixel | 1024 x 504
Pixel size | 27 x 30µm²
Pixel variants | 2 x AC – 2 x DC
Epi layers | 6 options (4 relevant)
HI tolerance | Hardened
MIMOSIS-1, 60µm thick
3 x
W. Snoeys et al., DOI: 10.1016/j.nima.2017.07.046
H. Pernegger et al., https://doi.org/10.1016/j.nima.2018.07.043
M. Munkeret al., DOI: 10.1016/j.nima.2019.02.049
M. Dyndal et al.,10.1088/1748-0221/15/02/p02005

## Slide 16: MIMOSIS – 1 : 1st full size sensor
Response to 55Fe
MIMOSIS-1, 60µm thick
MIMOSIS-1 test system
(Lockdown edition)
First results look promising – stay tuned.
Fixed Pattern Noise: 9 - 17 e ENC
Thermal noise: 3 - 5 e ENC

## Slide 17: Summary and conclusion
MIMOSIS is a CMOS MAPS
Highest spatial precision.
Low power (<<100 mW/cm²).
<5 µs time precision.
Advanced radiation tolerance.
20/80 MHz/cm² recorded rate (average/peak).
The MIMOSIS-1, first full size sensor is being tested
Confident to match design goals.
GSI joined R&D aiming for future trackers (CBM-MVD, FAIR upgrade).
MIMOSIS will be made available to interested partners.
H. Darwish, M. Deveaux, C.J. Schmidt
J. Baudot, G. Bertolone, A. Besson, R. Bugiel, S. Bugiel, Z. El Bitar, G. Claus, C. Colledani, A. Dorokhov, G. Doziere, M. Goffe, A. Himmi, C. Hu, K. Jaaskelainen, F. Morel, H. Pham, M. Specht, I. Valin, M. Winter, Y. Zhao
B. Arnoldi-Meadows, B. Linnik, P. Klaus, M. Koziel, Q. Li, J. Michel, C. Müntz, Q.Yang, P. Sitzmann, J. Stroth

## Slide 18
Backup

## Slide 19: Signal estimate
Assumptions:
25µm expitaxial layer, minimum ionizing particle
Deep substrate does not contribute (pessimist)
Marginal charge sharing (fully depleted pixel)
Data : H. Bichsel, Rev. Mod. Phys.,Vol. 60 (1988), No. 3, P-663 699
Target:
Mean value: 1430e
FWHM: 1158e
Corresponding ROOT-Landau:
Landau (MPW,sigma) => Landau(850,293)
=> MPW=850
MIMOSIS-0 threshold

## Slide 20: MIMOSIS-0 Threshold scan

## Slide 21: Integration concept of the MVD
Vacuum operation requires actively cooled device.
Use cooling support from diamond to move heat out of acceptance
Put heat sink and FEE outside acceptance
CBM acceptance
Outside acceptance
Beam
hole
rout

## Slide 22: Integration concept of the MVD
M. Deveaux
22
Discri
Sensor
Discri
Sensor
GBTx data
concentrator
LV-re-
gulator
MVD Prototype (mock up)