## Slide 1
T. Dritschler, M. Caselle, L. Ardila, S. Chilingaryan,
A. Ebersoldt, J. Hurst, N. Karcher, A. Kopmann, O. Sander, T. Stockmann(*)
(Commercial) DMA technologies to realize a flexible DAQ system for Tera-Scale experiments
Karlsruhe Institute of Technology (KIT)
(*)Forschungszentrum Jülich
Notes: <Foliennummer>

## Slide 2
Challenges for modern DAQ Systems
Advancements in Detector Technologies lead to highly complex DAQ systems
This complexity results in heterogeneous systems with many different components
Complex data paths and heterogeneous architectures
Detector
Readout
Event building
Processing
Storage
ASICs?
FPGAs?
CPUs?
GPUs?
Optical
Links?
PCIe?
InfiniBand?
Ethernet?

## Slide 3
Challenges for modern DAQ Systems
Development and maintenance of complex DAQ systems is expensive and time consuming
Complex data paths and heterogeneous architectures
Detector
Readout
Event building
Processing
Storage
Using commercially available standards and „off-the-shelves“ components might mitigate these efforts
Can we design scalable and maintainable DAQ using mostly commercial components?

## Slide 4
Buffer
Kernel Space
Application Space
System Bus
Data transfer inside of conventional computing systems
CPU involvement in data movement

## Slide 5
Place
Buffer
Kernel Space
Application Space
System Bus
Data
Place
Fetch
Fetch
Place
Data arrives and is placed in device buffer
CPU Fetches data from buffer
CPU Places data into Driver memory
CPU Fetches data from Driver
CPU Places data into application space
Data transfer inside of conventional computing systems
CPU involvement in data movement
Data
Fetch
Place
Fetch
Repeat for each Data!

## Slide 6
DMA
Engine
Kernel Space
Application Space
System Bus
Data
CPU „reserves“ memory in application space (Pinning)
CPU configures the device’s DMA engine, effectively „Mapping“ the pinned memory to the device
Data arrives and is placed right into destination memory
Pin
Configure
Map
Direct Memory Access (DMA) enabled data transfer
Freeing up CPU and reducing copy efforts
Enables microsecond latencies at full interconnect bandwidth!
To Network

## Slide 7
RDMA enabled GPGPU computing
Efficient use of GPUs for On-Line and In-Line data processing
System Bus
DMA
Engine
Data
DMA is possible for GPU memory as well
Analogous to main memory DMA
Pin → Map → Place
Significantly reduces latency!
IO Device
IO

## Slide 8
InfiniBand, the ‚de facto‘ standard for RDMA
[...]
Commercial High-Speed, Low-Latency data transfer
© Mellanox
Support both: InfiniBand AND Ethernet!

## Slide 9
Next generation RDMA capable computing accelerators
Closing the gap between networking and computing
Commercially available components
Software Programmable
Low development effort
Easy to upgrade to newer generations, once they become available
(R)DMA Capable
Optimized for Machine Learning and AI applications!
Xilinx ALVEO SmartNIC:
Up to 1.1M LUTs
Up to 100Gbps Ethernet
Nvidia EGX A100:
Ampere GPGPU,
200Gbps Network,
Ethernet + InfiniBand
© Xilinx
© Nvidia

## Slide 10
Communication between heterogeneous components
One protocol for all the most common components?
Ethernet is one of the most common commercially available interconnects
Ethernet ✓
Ethernet ✓
Ethernet ✓
PC / CPU
GPU
FPGA
Network Infrastructure
Ethernet ✓
Is there a way to benefit from RDMA using Ethernet?

## Slide 11
RoCE (RDMA over Converged Ethernet)
RoCE uses UDP packets and encapsulates InfiniBand “instructions” into the UDP payload
Soft- and Hardware implementations available!
Enabling RDMA benefits for conventional Ethernet networks

## Slide 12
KIRO: KIT RDMA Programming Library
Integrating RMDA capabilities into software
© Mellanox
Clone it on Github!
https://github.com/ufo-kit/kiro
KIRO Server/Client:
Unidirectional data transfer from Server to Client (Clients “Pull” from Server)
Fixed-Size memory segment
Supports multiple connected clients per server
KIRO Messenger (Beta):
Layers bi-directional point-to-point messaging on top of KIRO
Messengers can connect to multiple peers
Fully RDMA enabled arbitrary sized memory exchange (“Push” and “Pull”)
Works for both: InfiniBand and RoCE!

## Slide 13
Novel DAQ architecture using commercial HPC Components
High-performance distributed ML for physics experiments
Ethernet fabrics
(hundreds Gb/s)
Detectors
On-line data path (by commercial devices)
…
FPGA
AI
ETH
…
FPGA
AI
ETH
…
FPGA
AI
ETH
Modular readout
Ethernet
…
Versatile DAQ optimized for detector and AI applications
High-performance ML inference on modern programmable hardware platforms
Novel heterogeneous FPGA/GPU architecture based on emerging Ethernet protocols
Fast Feedback
HPC
GPUs
AI
Alveo
AI
HighFlex
AI

## Slide 14
Machine Learning Application Example
PANDA Tracking and Event Selector
Forward Tracking Stations
1 & 2, 3 & 4, 5
3&4 inside 2 Tm dipole field
Graph Neural Network
In Total:
Connection of all hits from one layer with all hits in next layer
6 charged tracks
Track finding efficiency 96%
Most probable connections survive
Waleed Esmail

## Slide 15
Machine Learning Application Example
PANDA Tracking and Event Selector
PANDA online event selector
Best network: CNN
Efficiency improvement for different physics channels CNN vs. Classical method
Peiyong Jiang
Software trigger selects physical interesting channels from background for data storage
All data points above 100% efficiency vs. conventional approach → Indicates Neural Network performs better accross all metrics
100%
Heterogeneous system
Unifiable communication
Proposed for PANDA DAQ

## Slide 16
Heterogeneous FPGA – GPU architecture for beam physics
High-performance distributed ML for physics experiments
Ethernet fabrics
(hundreds Gb/s)
FPGA
AI
ETH
FPGA
AI
ETH
FPGA
AI
ETH
Modular readout
HPC
GPUs
AI
Alveo
AI
HighFlex
AI
Versatile DAQ optimized for detector and AI applications
High-performance ML inference on modern programmable hardware platforms
Novel heterogeneous FPGA/GPU architecture based on emerging Ethernet protocols
Detectors
…
…
…
Beam diagnostics
Synchrotron
Accelerator
KAPTURE
KALYPSO
…
Ethernet
Fast Feedback
On-line data path (by commercial devices)

## Slide 17
Hardware implementation
Reinforcement Learning on modern programable device
Deep Deterministic Policy Gradient (DDPG)
Actor consists of four fully-connected dense layers, each layer consists of 64 neurons using a rectified linear unit (ReLU) as activation function in FPGA
Actor
Critic neural network and the policy gradient are implemented as bare-metal application on ARM processor
Critic
As seen in: „Accelerated Deep Reinforcement Learning for Fast Feedback of Beam Dynamics at KARA“ A. Ebersoldt

## Slide 18
Control of the complex beam with ML
Machine Learning toward Autonomous Accelerators
RF System
action
THz detector
KAPTURE
HighFlex card
AI deployed in the FPGA
Closed feedback loop at KARA:
    Detection of signals with THz detectors and KAPTURE @ 500 MPulse/s
    Data processed by Reinforcement Learning on FPGA
    FPGA action as special RF signal modulation is sent to the kicker cavity
  Goal: total latency of control feedback loop << 1 ms
Target applications: KARA, FLUTE, ARES and more
Status: first beam control on FPGA developed within AMALEA  will continue in ACCLAIM (Helmholtz Innovation fund)
MicroTCA
A. Ebersoldt
Feedback
Ethernet

## Slide 19
Digital
Conversion
RF
FPGA
~
DAC
ADC
Up-conversion
4 … 8 GHz
Down-conversion
±400 MHz
2
4
Baseband frequency comb generation
Digitization &
signal processing
1
5
3
Storage / Backend
Server
|a|
…
|a|
…
Application: RoCE in FPGA for the ECHo experiment
ECHo Experiment to measure the Neutrino mass
Jonas Hurst, Nick Karcher, Oliver Sander

## Slide 20
RoCE
Master Thesis: „Entwicklung eines breitbandigen Datentransfers (DMA) für die Messdatenakquise“ (Jonas Hurst, Nick Karcher, Oliver Sander)
Xilinx Zynq US+
(64bit ARM + FPGA)
Development Board
Application: RoCE in FPGA for the ECHo experiment
Xilinx ERNIC IP Core implementation and integration
KIRO

## Slide 21
Conclusion
Application of industrial RDMA standards for modern DAQ
Computing Accelerator integration → Full support for HPC and on-line processing
Readily available Hard- and Software → Drastically reduces development efforts
Single, commercial components → Easy maintenance and easy upgrades to newer versions
Highly versatile → Unify communication between all components: CPU, GPU, FPGA
Benefits:
Drawbacks:
Integration into existing infrastructure requires (complex) retooling
Difficult to deploy and operate from within virtualized software environments
Full performance can only be reached when using dedicated networking hardware