## Slide 1
Error Tolerances and Girder Errors from a beam dynamics point of view
S.M.Liuzzo, ESRF, Grenoble, 11th May 2021
The message of this presentation is, for an HMBA-like upgrade project:
Girder-Girder == Magnet-Magnet
IF ANY, USE MEASURED SURVEY DATA INSTEAD OF GIRDER-GIRDER ERRORS

## Slide 2: Tolerance estimates objective
TARGET
Septum
>10h
Touschek Lifetime
@ 200mA uniform, 5pm
Injected
beam
2 main parameters to achieve,
Absolute values depend on facility layout.
-10mm (-8.1mm @INJECTION)
~100% Injection Efficiency
Also :
Emittance variation < 2pm
Feasible correction strengths
Orbit < 100um rms
etc…

## Slide 3: Liftime and dynamic apertures vs error sources
10h
17h
DA=-10mm
Lifetime = 10h
A CLUSTER is crucial for this analysis. Each error set to analyze requires 1CPUx4h
CAoPAC Workshop l GSI, Darmstadt 10-13 March 2015 l S.M.Liuzzo
How tolerances were defined
How to determine the ”tolerance” ?  DRAW A LINE (relative impact of each error), RESCALE globally.
The line where I should have placed it.
The line where I should have placed it.
Sext. Alignment do more on DA than on TLT ;
Moderate gradient are irrelevant compared to high gradient ;
Etc. etc.

## Slide 4: Comparable tolerance table
DQ (combined function dipoles) behave as quadrupoles concerning errors. Evident the impact on vertical dispersion compared to the other quadrupoles (defocussing quadrupoles).
Quadrupoles have large impact on orbit and horizontal dispersion, also in this case, lifetime and DA are strongly affected. QF6 and QF8 are dominant.
Sextupoles have the largest impact on DA, they are also the strongest source of beta-beating and emittance as expected.
Octupoles influence is limited compared to quadrupole and sextupoles, nevertheless they do have an impact on DA. Their effect on lifetime is very small.
Rotations up to 100urad have impact on the various parameters but limited.
How tolerances were defined
In RED
The worst crossing of the “line” for each performance parameter

## Slide 5: Tolerable random errors
Each error, on each magnet family, is studied individually looking at the dependence of DA, lifetime, emittances and all relevant parameters vs error amplitude.
Required: | DX | DY | DS | DPSI | DK
 | mm | mm | mm | mrad | 10^-4
DL | >100 | >100 | 1000 | 500 | 10
DQ, QF[68] | 70 | 50 | 500 | 200 | 5
Q[DF][1-5] | 100 | 85 | 500 | 500 | 5
SFD | 70 | 50 | 500 | 1000 | 35
OF | 100 | 100 | 500 | 1000 | 
Sextupoles and high gradient quadrupoles are the most relevant limitations, nevertheless, this alignment specifications are currently achievable.
(DX=DY=60mm, 84 mm between two magnets).
How tolerances were defined

## Slide 6: Girder Errors
Girder displacements and rotations
Girder displacements and rotations
+ random errors Quad. and Sext.
4 girders, BPMs are moved with the girder.
l 30-31 May 2014 l S.M.Liuzzo
How GIRDER
tolerances were defined

## Slide 7: Dynamic aperture @S3 septum vs errors for s28A + RDT correction
-20%
l WP1 ESRF upgrade l May 2014 l S.M.Liuzzo
26/07/2013
How GIRDER
tolerances were defined
All is NOT the sum of each error

## Slide 8: error values for a reduction of 20% of Hor. Dynamic Aperture @S3
No influence on emittances
Strong impact off quadrupole errors
RDT correction
How GIRDER
tolerances were defined

## Slide 9: Girder Errors
(g) Stands for girder errors,
no (g), are quadrupole and sextupole individual misalignments
10h
17h
Hor. DA @ QFI, X0.81 to scale at S3,
8mm required at S3, 10mm accepted at QFI
How GIRDER
tolerances were defined
In terms of DA girders and magnet alignment approx. sum up. In terms of lifetime, magnets+girder have a stronger impact.
Girders+Magnets
Girders+Magnets
GOOD
BAD
Girders only
girders

## Slide 10: Summary Table of Girder Errors
(g) Stands for girder errors, no g, are quadrupole and sextupole individual misalignments
How GIRDER
tolerances were defined
Commissioning-like correction sequence to get these data
Cluster, Average over several (10) error seeds.
Computing cluster

## Slide 11: The measured position of the lattice
nominal
current
How GIRDER
tolerances were excluded
This is where the machine is. Let’s use this information!
ESRF 1994-2018
EBS 2019-?? We placed EBS where the old SR used to be. Everyone is happy.

## Slide 12: Survey errors PLUS random errors
Random Gaussian DX DY in quadrupoles and sextupoles on top of the survey errors.
The blue curve represents the current ESRF storage ring position.
The x symbols are the interpolated positions on this curve for the S28A lattice.
BPM are positioned on the same curve.
DX and DZ and girder rotations are applied.
Errors are ramped in steps of 20% up to the nominal value.
Added random errors to account for unknown magnetic center position
l ESRF Upgrade l June 2014 l S.M.Liuzzo
How GIRDER
tolerances were excluded

## Slide 13: Long range errors
Error “waves” applied to the lattice: DX, DY, Rotations for quad and sext.
Correction performed for each frequency and amplitude set as:
Open trajectory correction
Orbit correction
RDT correction
storage ring survey data
simulated 1st harmonic,
Simulations performed on the OAR asd cluster, 8h-600cpu
26/07/2013
How GIRDER
tolerances were excluded

## Slide 14: Long range errors: error envelope function
Impact of error “waves” on horizontal orbit
At a wavelength of L/128~6m
30um errors amplitude give
30 um residual orbit distortion.
At a wavelength of L/2~422m
7mm errors amplitude give
30 um residual orbit distortion.
26/07/2013
How GIRDER
tolerances were excluded
SLOW, LARGE VARIATIONS HAVE LIMITED IMPACT ON THE OPTICS

## Slide 15: Emittance, dispersion and beta-beating vs wavelength
How GIRDER
tolerances were excluded

## Slide 16: Simulated survey errors current positions (from ALGE group)
Simulated survey errors about the current position of the lattice.
Rotations are random, but for a 21urad systematic outward tilt.
Data provided in 320 points for the current lattice.
26/07/2013
How GIRDER
tolerances were excluded
50 cases
WHERE WILL THE SR BE
if we remove it and reinstall it?
horizontal
Longitudinal (electrons path)
vertical
DATA from ALIGNMENT GROUP

## Slide 17: Dynamic aperture and lifetime
The above curves are interpolated to set the errors in the S28A lattice.
-10mm (-8.1mm @S3)
Lifetime: 16.6h
range:[16.4 17.1]
26/07/2013
MEASURED SURVEY + simulated alignment errors
SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
TARGET
nominal
current
On the blue curve
How GIRDER
tolerances were excluded

## Slide 18: Additional Random errors
-10mm (-8.1mm @S3)
Lifetime goes from 16.6h to about 12h with many lost seeds and increasing range.
As above + RANDOM ERRORS SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
Increasing random errors
How GIRDER
tolerances were excluded
TARGET
Additional random errors are still required to describe the error on the position of the magnetic centers of the magnets.

## Slide 19: Simulated survey errors nominal positions (from ALGE group)
Simulated survey errors about the nominal position of the lattice.
Rotations are random, but for a 21urad systematic outward tilt.
Data provided in 320 points for the current lattice.
PREVIOUS
How GIRDER
tolerances were excluded
horizontal
Longitudinal (electrons path)
vertical

## Slide 20: Dynamic aperture and lifetime
The above curves are interpolated to set the errors in the S28A lattice.
-10mm (-8.1mm @S3)
Lifetime: 16.7h
range:[16.6 17]
IDEAL SURVEY SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
TARGET
nominal
current
On the red curve
How GIRDER
tolerances were excluded

## Slide 21: Additional Random errors
-10mm (-8.1mm @S3)
Lifetime goes from 16.7h to about 13h with many lost seeds and increasing range.
IDEAL SURVEY + RANDOM ERRORS SET IN THE LATTICE
AND TESTED FOR DA/LIFETIME AFTER CORRECTION
How GIRDER
tolerances were excluded
TARGET
Increasing errors
Additional random errors are still required to describe the error on the position of the magnetic centers of the magnets.

## Slide 22: In practice
We have no specific beam dynamics interest in the girder-girder tolerance themselves.
Those are not precisely defined among different groups and may lead to lack of understanding.
From beam dynamics, we can say that: large, slow, smooth, variations of position are not detrimental.
From a beam dynamics point of view, as long as magnet-magnet tolerances (actually, single magnets rms position errors) are achieved at every location in the machine, including between magnets standing on neighboring girders, we will get the foreseen Dynamic Aperture and LIFETIME.
We let the alignment group decide how to achieve this requirement.
For ESRF-EBS It worked extremely well, largely exceeding expectations/simulations.
Expected magnet-to-magnet
60-70 mm
From steerers/orbit data
Achieved magnet-to-magnet
25-40 mm
rms DX DY
alignment
In order to model the lattice at the location where it will be installed, we included in all “predictive” (DA, LT, IE,etc) simulations the Simulated Survey Position provided by the alignment group.
This may be usefull also for maximum correctors strength evaluation, and/or definition of Beamlines alignment strategies.
Conclusion

## Slide 23: Tolerable random errors
Each error, on each magnet family, is studied individually looking at the dependence of DA, lifetime, emittances and all relevant parameters vs error amplitude.
Required: | DX | DY | DS | DPSI | DK
 | mm | mm | mm | mrad | 10^-4
DL | >100 | >100 | 1000 | 500 | 10
DQ, QF[68] | 70 | 50 | 500 | 200 | 5
Q[DF][1-5] | 100 | 85 | 500 | 500 | 5
SFD | 70 | 50 | 500 | 1000 | 35
OF | 100 | 100 | 500 | 1000 | 
Sextupoles and high gradient quadrupoles are the most relevant limitations, nevertheless, this alignment specifications are currently achievable.
(DX=DY=60mm, 84 mm between two magnets).
GIRDERS
Survey simulations or SAME AS worst case MAGNET-MAGNET
To answer the question:
What girder-girder tolerances did you use?
Conclusion
60
Many simulations for 1 number needed

## Slide 24: conclusions
The definition of alignment tolerance can be done in a quasi deterministic way, to give relative impact on final parameters of each source of errors. Finally this is NOT directly usefull for alignment. Unless some specification is really demanding, everything will be alignment to the minimum value found: one single number.
Running Girder-to-girder simulations is also not really useful. For compact machines girder-to-girder is the same as magnet-to-magnet. Using simulated Survey data is more realistic, simpler and efficient.
Large, slow, SR position variations are not an issue for beam dynamics. Magnet to magnet is what really counts.
For upgrade project using the measured positions of the SR and hypothetical positions after dismantling and reinstallation, shares well the contribution of alignment and magnet center fiducialization error sources. Simulations of the measured survey may be included in the model simply, sparing a lot of time and effort, and simplifying the communication among colleagues.

## Slide 25: BACKUP

## Slide 26: Comparable tolerance table
This table provides a deterministic way to compare error impact on lattices.
It is used also to asses the performances of correction schemes and correction algorithms
Further reduction of this data is needed to provide a tolerance table.
How tolerances were defined

## Slide 27: definition of a List of tolerable errors
Compare magnet groups for the same error
Compare error sources for the same magnet group
Tolerated errors
beta beating = 1%
Hor. Disp. = 1mm
How tolerances were defined

## Slide 28: error amplitude giving 30um orbit after correction vs wavelength
Amplitude is X, Y and rotation about s (rad) simultaneously

## Slide 29: Comparison of various Error Sources to obtain 30 um orbit

## Slide 30: Comparison of various Error Sources (other parameters)

## Slide 31: Girder to girder: an historical exchange after >2 years of simulations
Dear Alignment group colleagues,
we would like the girders to have an alignment error of
78.656 mm rms in the X plane
73.421 mm rms in the Y plane
Thank you
Best regards
Beam Dynamics people
Dear Beam Dynamics colleagues,
What do you mean?
2 girders one at the injection and one on the opposite side of the SR should be aligned within 75 mm?
We think it would be better to meet and discuss.
Could you give us the tolerated alignment envelope over 10cm, 1m, 10m, 100m, 1km?
By the way, X for us is the longitudinal direction.
Thank you
Best regards
Alignment people
Dear Alignment colleagues,
Indeed, we would appreciate a meeting on the topic.
Best regards
Beam Dynamics people
In purpose missing “Thank you”

## Slide 32: Girder to girder: an historical exchange after >2 years of simulations
Dear Alignment group colleagues,
we would like the girders to have an alignment error of
78.656 mm rms in the X plane
73.421 mm rms in the Y plane
Thank you
Best regards
Beam Dynamics people
Dear Beam Dynamics colleagues,
What do you mean?
2 girders one at the injection and one on the opposite side of the SR should be aligned within 75 mm?
We think it would be better to meet and discuss.
Could you give us the tolerated alignment envelope over 10cm, 1m, 10m, 100m, 1km?
By the way, X for us is the longitudinal direction.
Thank you
Best regards
Alignment people
Dear Alignment colleagues,
Indeed, we would appreciate a meeting on the topic.
Best regards
Beam Dynamics people
In purpose missing “Thank you”
Lesson learnt:
TALK TO YOUR COLLEAGUES BEFORE RUNNING YEARS OF SIMULATIONS

## Slide 33: Girder to girder: an historical exchange after >1month of simulations
Dear Alignment group colleagues,
we would like the girders to have an alignment error in the transverse plane with
L/1-L/8 wavelengths and up to 2mm amplitude on a closed trajectory.
Thank you
Best regards
Beam Dynamics people
Dear Beam Dynamics colleagues,
What do you mean?
What do you mean by “wavelength”?
We think it would be better to meet and discuss.
Could you give us the tolerated girder-to-girder alignment envelope over 10cm, 1m, 10m, 100m, 1km?
What about the longitudinal direction, X?
Thank you
Best regards
Alignment people
Dear Alignment colleagues,
Indeed, we would appreciate a meeting on the topic.
Beam Dynamics people
In purpose missing “Thank you”
In purpose missing “best regards”

## Slide 34: Girder to girder: an historical exchange after >1month of simulations
Dear Alignment group colleagues,
we would like the girders to have an alignment error in the transverse plane with
L/1-L/8 wavelengths and up to 2mm amplitude on a closed trajectory.
Thank you
Best regards
Beam Dynamics people
Dear Beam Dynamics colleagues,
What do you mean?
What do you mean for “wavelength”?
We think it would be better to meet and discuss.
Could you give us the tolerated girder-to-girder alignment envelope over 10cm, 1m, 10m, 100m, 1km?
What about the longitudinal direction, X?
Thank you
Best regards
Alignment people
Dear Alignment colleagues,
Indeed, we would appreciate a meeting on the topic.
Beam Dynamics people
In purpose missing “Thank you”
Lesson learnt:
speak the same language or
find an interpret or
first ask the right question.
In purpose missing “best regards”