## Slide 1
Sapphire sensors for LUXE Gamma Beam Profiler

## Slide 2
Gamma Beam Profiler Station (1 sensor per station)
Sapphire Sensor
Support plate
(fixed)
Piezo motors
Flex Kapton cables
Patch panel
Connection plate
(movable)
Coaxial cables (Kapton ø1.2 mm)
Sensor frame
Connectors
~2-3 m
or ~30 m
to Control
room

## Slide 3
Min 2 cm
Floor
~2.5 m
Beam
X
Y
Cables to Control room
Patch-box
Station cables
Gamma Beam Profilometer
+Shielding box
with thin windows
for the beam
(2x Kapton 5 μm)

## Slide 4
Q-545.240
Drive force 7 N
Travel range 26 mm
Incremental sensor with nanometer position resolution
Maximal velocity 8 mm/s
Minimal incremental motion 6 nm
Bidirectional repeatability 200 nm
Cable length 2 m
Q-545.240
Q-Motion® Linear stage, piezoelectric inertia drive, 26 mm travel range, linear encoder, 1 nm resolution, 7 N drive force, dimensions 45 × 63 × 15 mm (W × L × H)
www.pi.ws
https://www.physikinstrumente.com
Physik Instrumente (PI)
Physik Instrumente (PI) GmbH & Co. KG
Auf der Roemerstrasse 1 76228 Karlsruhe Germany

## Slide 5
Q-545.240

## Slide 6
All connectors from
SAMTEC
Pitch 1.27 mm
100 Kapton ø1.2 mm
Coaxial cables

## Slide 7
R/O electronics (or Patch-panel 2)
Signal inputs

## Slide 8
SAMTEC micro-pitch
Patch-panel 1
For flex Kapton cables

## Slide 9
SAMTEC micro-pitch
Flexible Kapton cables