## Slide 1: General Info
M. Bruschi (INFN Bologna)

## Slide 2: News
INFN Bologna and Padova groups belong now to the LUXE collaboration
A space in CONFLUENCE where to place GBP files is now available
  https://confluence.desy.de/display/LUXE/Gamma+Beam+Profiler
  Mail to uco@desy.de for access to the area
  Confluence documentation only in German!
  Is this an acceptable repository for our files or should we create a space in other platforms (Google docs, Sharepoint ... other ideas?)
Our next meetings will be on Thursdays at 14:00 (TBC)

## Slide 3: Readout Electronics
It is a rather straightforward design
  Plenty of signal: ~30 pC/BX (peak on upstream detector)
  Low rate: 10 Hz
Array of Sample-and-Hold capacitors
  Control logic for switching and multiplexing the outputs to read them out
Read-out card: commercial solution existing
  Modular reading system FERS-5200 developed by CAEN based on CITIROC
  64 channels per card (13-bit dynamic range)
INFN Bologna will design and built a patch panel (PP) to distribute the detector signals to plugged-in readout cards
  6 M.U. requested to INFN BO in 2022 for the PP design

## Slide 4: Readout system
DT5215 Concentrator Board for FERS-5200
A5202 64 Channel Citiroc unit for FERS-5200

## Slide 7: Electronics Noise (assuming CR-RC with t=50 ns)
IL < 1 nA
CT<3.5 pF+2 pF
RS< 10 MOhm
t~ 50 ns
ENCP~3.8E-3 fC
ENCS~3.5 fC (??)
Peak signal on upstream detector ~ 30 pC (13-bit dynamic range)

## Slide 9: HV System
SY5527LC - 4 Slot LOW COST Universal Multichannel Power Supply System
A2519CA - SYx527 L.V. channels 15V 5A (50W) - DB37 - Individual Floating - Current Controlled (8 ch)
A7038 32/48 Channel 1 kV/100 µA Common Floating Return Boards

## Slide 10: Very low-noise electronics to test sapphire
Strip capacitance: 1.84 pF
MIP signal:22 eh/um
Thickness: 100 um
CCE: 50%
Total signal: 1100 el
Total noise: 12.4 el
Starting kit:
5 CUBE (400 euros/piece)
1 Bias Board 8CH
(800 euros/piece)
https://www.xglab.it/products/cube/

## Slide 11: Test Beam Needs
1 MIP in 100 um Sapphire : 2200x27 eV= 60 keV
LUXE Max Energy release in downstream detector per BX: 25 GeV
Number of MIPS per BX (LUXE) per strip: 4.2 x 105
1 Year running LUXE ~ 35 weeks
Test beam duration ~ 1 week
Electron test beam intensity needed (per strip) ~ 35 x 4.2 x 105 ~ 1.5 x 107 /s
MC standalone simulation needed to plan test beam

## Slide 12: Today’s program
Discussion
  Status of the Delivery from DESY to Padova and Tomsk
  Samples received by Padova from University
    Report about first tests
  PCB support for the detectors
    Design/production (INFN Bologna experts started working on this)
  Specifications for detector mechanics
Test Beam planning
Update on MC simulation
Others?

## Slide 13: Backup

## Slide 14: Questions from the Padova group
detector:
  the minimum distance between metallization and edge of the PCB is 0.2 mm we wonder whether there is any reason to be so close to the edge or if it wouldn't be safer to keep of the order of 1mm gap.
  it would help to have alignment crosses obtained with the metallization on the strip side of the detector, in a few positions where there is no metallization on the other side, so that the transparency of the sapphire makes it possible to see the corresponding markers on the PCB.
  what is the minimum thickness of the metallization that can be deposited ?
PCB:
  the current baseline electronics (EASIROC chips) seems to provide an AC coupling to the strips; in this case it would seem opportune to implement a polarization of the strips in the PCB: is there any reason why it has not been foreseen ?
  it would seem beneficial to have all the the pads used for gluing the detector connected to the HV line and not just the bottom one
  as mentioned for the detector, alignment markers could be included in the PCB design to match the ones on the detectors

## Slide 15: Specifications for mechanics
Absolute reproducibility: 100 um ( this is the accuracy of the measurement provided by the survey group, I can't see reasons to do better than this, but maybe I'm overlooking something)
max. relative motion accuracy, within total motion in one direction < 2mm: 2 um (this is the requirement for the gamma beam scan)
min. motion range: 2 cm
max. mass to be moved: 200g + vertical stage mass in the horizontal direction
min. top movement speed: 1 mm/s possibility to switch off the liner stages ( this may reduce the noise, servomechanisms usually stay active to keep the positions)

## Slide 16: TDR GBP
Scientific motivation
Detector Description
  Sapphire detectors
  Mechanics
  Readout Electronics
  Slow Control
Performances
  test
  MC simulation
Costs, Resources

## Slide 17: Todo List for TDR
Detector performances using full G4 and realistic beam conditions
  improved (not final) mechanical structure description
  digitization
  linearly polarized laser beam
Finalize conceptual design of
  mechanics
  readout electronics
Planned:
  Quality tests and first lab tests on sapphire detectors
  Uniformity of response using radioactive source
The level of advance of the planned points strongly depends on the economical support which will be given by the funding agency from now to the end of the year
  Experiment and GBP presented yesterday (May 18th) at INFN CSN1
  Internal Reviewing procedure will be started this year aiming, if succesfull, to financial support from 2022

## Slide 18: Today’s discussion
Quality tests
  Labeling scheme?
  Wafer thickness (~10 points)
  Weight (~0.8–1.2 g for 2” 100-150 μm thick wafers)
  Optical tests (to be discussed)
  Probe station tests (UV, Röntgen, source)

## Slide 19
How to study charge carriers lifetime by optical methods?
Ideas are welcome!
Röntgen pumping – visible light reflection
Optical-Pump/THz-Probe Spectroscopy
Double photon absorption – UV (~200 nm) light?
Something else?
Why optical? Allows to check wafers without metallization,
electrical contacts etc.

## Slide 20: Electrical methods?
Electrode with holes
HV
Sapphire
sample
Pump

## Slide 21: Probe station + pumping
HV
Sapphire
sample
Pump
Sensitive region

## Slide 22: Cable attenuation
30 m
Vin=1.6 Volt, 10 ns
Vout=0.68 Volt, ~ 100ns
The readout logic is based on peak stretcher or sample and hold
Probably a signal loss of factor ~ 2-2.5 should be considered (worsening of S/N must be measured)
The cost from the company is appealing:
750 euro (64 channels, 30 m)  total of 4500 euros for 3+3 cards (High Speed Interconnection company)

## Slide 23: Method verification with Lorentz-Cauchy
Full G4 simulation from Kyle’s studies
FWHM (1st plane):30 npixx=0.150 mm
gX=FWHM/2=0.075 mm
X (mm)
gx=0.075 mm
sx(gaus)=0.111 mm
FWHM (gaus)=0.260 mm=52 npixx
D=6.7 m
D=11.8 m
Extrapolation to D=11.8 m  gx=0.130 mm

## Slide 24: To be discussed at the next meeting on 05/10
inputs for the design of the mechanics
Quality test procedures for the sapphire wafers
Readout electronics positioning
Number of stations necessary (in the CDR they are 2, can we drop one with the new beam line?)
MC digitization
Others?

## Slide 25: Questions for mechanics

## Slide 26: Table of Risks
The table has been updated for the meeting with PRC
The table can be still changed
Please read carefully and send your comments

## Slide 27: Timeline
The table has been updated for the meeting with PRC
Please read carefully and send your comments

## Slide 28: Clean Room
LUXE TC asked for the need of a clean room
Apparently the situation is now frozen at DESY due to COVID emergency
  How do we deal with this for the first tests at DESY on the delivered wafers?
The situation should change from 2023 (spaces will be allocated for us probably in XS1)
In any case we should formulate very soon a plan for our needs (area, facilities ...)

## Slide 29: Test Beam
Tests will start in 2022
A plan should be made and start to contact the TB facilities
ELBE/FRASCATI/XFEL/RAL
Probably some inputs will come from today’s discussion

## Slide 30: GBP collaboration tasks
Detector
  Procurement (DESY, U. TOMSK, INFN PD)
  Production (TOMSK)
  Design and Integration (DESY, BELFAST, PD, BO, TOMSK)
  Tests
    Characterization in the lab (DESY, PD, BELFAST –laser tests at RAL-)
    CCE uniformity (DESY, PD, TOMSK)
    Test Beam (DESY, BO, PD, TOMSK, BELFAST)
Mechanics (PD)
  Design (DESY, PD System Eng.)
  Production
  Tests, Commissioning
Electronics (BO)
  Design
  Production
  Tests, Commissioning
Data Acquisition (milestones in the readout talk)
Slow control
  HV,LV
  Table movements (PD)
  Calibrations (BO)
Data Quality (DESY, PhD)
MC
  Detector performances (PD –PhD-, BELFAST)
    Stand Alone
    LUXE
Data Analysis (DESY, PhD, BELFAST)

## Slide 31: Some thoughts about the measurement

## Slide 33: Precision on x
With Ng=107 (conservative) sw|min=1.8 mm
Simulation must be improved
  Full simulation
  Electronics noise
  Charge collection effects
There is margin to keep sw|min <5 mm (sx/x<2.5%) once all the systematic effects will be included

## Slide 34: An alternative approach
How is the beam width defined ?
For a gaussian beam shape the beam width could be defined as
  profile standard deviation : s
  profile FWHM:
  Area/Amplitude:
In general: beam width
If the X and Y distributions belong to the same class of distribution
  the proportionality factor cancels in the ratio
In this case, following the Area/Amplitude definition
And since A(x)=A(y), finally
Measuring the ratio of the peak amplitudes in the
X and Y strips will provide the value of x
The measurement could be in principle precise and many
systematics effects should cancel out
This could be tested with the full G4 simulation

## Slide 35: Cross check
Gaussian values (x,y) generated according to sX=0.375 mm
Agreement found with standalone MC distribution (10E7 gammas with E=5 GeV generated)
  Compatible values found for chi2, parameters, and error on parameter
X (mm)

## Slide 36: Method verification
Generated Y distribution with sY=2 sX
Fit with parabolic function around the maximum
Simulation: 10E7 gamma, 5 GeV
  (2.0%)
Simulation: 10E9 gamma, 5 GeV
  (0.25%)
Y (mm)
X (mm)
The method works if beam is gaussian and sx > 0.375 mm

## Slide 37: Method verification with Lorentz-Cauchy
Full G4 simulation from Kyle’s studies
FWHM (1st plane):30 npixx=0.150 mm
gX=FWHM/2=0.075 mm
X (mm)
gx=0.075 mm
sx(gaus)=0.111 mm
FWHM (gaus)=0.260 mm=52 npixx
D=6.7 m
D=11.8 m
Extrapolation to D=11.8 m  gx=0.130 mm

## Slide 38: Further studies
A beam of Lorentz-Cauchy (LC) shape will be assumed
  gx=0.130 mm
  gy=0.260 mm
Fitting with parabola one gets
Fitting with LC in an interval
Fitting with LC in an interval
If the beam shape is LC the binning we have chosen is not enough for reconstructing beam widths (systematic of 2%)
Fitting with LC in an interval and strip width =50um

## Slide 39: Comments
If the beam shape is more LC than gaussian (and if gmin~0.130 mm) it looks like the strip pitch 100mm is not enough
In any case, to reconstruct the beam profile we will need to know very precisely which distribution should be used
In general, we would like to measure position and width with a method weakly dependent on theoretical assumptions (ideally, by using only the content of the strip with highest release of charge)
A detector with pitch 20 mm would allow to measure for each BX
Dx,y < 5.8 mm
Dx/x ~ 1%

## Slide 40: Wrap-up
The results obtained with this study should be redone with full MC simulation
  Realistic beam parameters are fundamental to design the detector
If the results are confirmed
  Can the distance by the two X-Y detectors be reduced to zero (from the actual ~2cm) and a second pair of detectors being added (at 2 cm distance)?
  The first XY station will have 200+200 strips of 20 mm pitch
  The second XY station will have 200+200 strips of 100 mm pitch
    It will be used to position correctly the first station and to cross check results and tails behavior
Other things to be discussed
  Position of the electronics
  Baseline detector
  Test procedures (see next slide)

## Slide 41: List of discussion arguments for the round table (proposed by Mauro)
delivery of wafers to the labs: when and how
wafers test:
  thickness measurements
  uniformity with pair production by UVC radiation ?
  light absorbance ?
  surface characterization with an Atomic Force Microscope
  do we need jigs to manipulate the wafers ?
wafers cut and metallization process
  pads/test points besides strips ?
  minimum tests performed at TOMSK before the detector are shipped
detector handling and shipment, schedule
characterizing the detectors in the lab: what to do, how, test setup
(if enough time) first ideas for test to be done on a beam