## Slide 1: Ecal modifications

## Slide 2: hypothesis
Max of the shower in layer 7
Max of the energy is 600 MIP/mm2
The positrons are mainly distributed over x and not over y
The peak is between 70mm up to 105 mm
~70mm
~105mm

## Slide 3: modifications
Have a non symmetric ecal :
  Different types sizes of pads :
    Production of pixelized sensors with pads 0.5 x 5 mm2 (0.5mm in x)
    For the layers where energy is deposited bigger than E ( we have to decide), the two first sensors are pixelized sensors, the rest are standard sensors
    For the layers with energy deposited smaller than E, standard sensors
  Different amplification :
    For the pixelized sensors, we connect a low gain preamplifier
    For the standard sensors, we connect a high gain preamplifier
No need to modify the ADC