## Slide 1
To do list for the TDR
(my opinion)
Wolfgang Lohmann

## Slide 2: Simulations
There are 4 scenarios with different positron numbers per bunch
gg phase 0 (less than one positron per BX)
gg phase 1 (a few per BX)
eg phase 0 (a few 1000 per BX)
eg phase 1 ( up to 106 per BX)
My conclusion is that we need different operation regimes for low and high number of positrons (still to be defined what is ‚low‘ and ‚high)

## Slide 3: Simulations
First topic: define the dynamic range for each of the scenarios
First step:
When this is fixed (Jakub should confirb that the readout can tackle it)
A few general performance plots should be repeated:
Energy resolution with 9 bit digitisation
Positron spectrum reconstruction with 9 bit digitisation
Considering background
Second step:
Apply the Mykyta-Chan algorithm for a given scenario with appropriate dynamic range settings and 9 bit digitisation, with and without background. Determine number and spectrum of positrons
Since currently MC simulations are not available for all scenarios strat with one available, and develop the analysi schain.

## Slide 4: Hardware
For sensors:
Characterisation of the different prototyps (dark current vs. HV, depletion voltage for Si)
Connectivity scheme to FE boards
Tests with FE connected (capacitive coupling needed?)
First testbeam results (minimum screenshots for signals)
FE and DAQ:
Status of submission for new FLAME
DAQ concept

## Slide 5: Simulations
Mechanics:
Box concept fixed, artists drawings
Tungsten plates, prototypes, quality tests done
FE istallation concept
Cablage and services will be a common chapter, but we should define what we need.