## Slide 1: GBP Report

## Slide 2: News
A formal statement from the DESY Directorate on the laboratory's support for the project is expected on August 5th
Decision levels for projects with costs > 250 k€
  CD0: Inclusion in the list of opportunities
  CD1: Inclusion in the DESY roadmap
  CD2: Inclusion in the investment plan
  CD3: Submission for evaluation by scientific committees
  CD4: Start of project
CD0 level expected (but could also be CD1, given the prospect of installation in 2024)
PRC recommendation for swift start of TDR to be completed by end 2021

## Slide 3: TDR layout for the GBP section
Introduction
Principle of measurement
Chose of Saffire as detecting material
Proposed detector
  Electronics
  Mechanics
  TDAQ
  Slow Control
MC studies
  Systematics uncertainty
(Detector performances on test beam or lab)
Detector calibration and monitoring strategy
Timescale, Resources, Personpower and internal organization
Writing should start in September
Status of MC simulation should be improved by then
Laser linear polarization should be
available by end of August
Skeleton will be implemented in OVERLEAF and section editors assigned
TDR editor must be decided

## Slide 4: News
CDR has been updated with new Fig 6.1 (now it includes properly GBP)
  https://desycloud.desy.de/index.php/s/SQcJXckeZ7iRk26
From: Yan Benhammou Sent: 22 July 2021 12:50 To: Marco Bruschi Cc: Yan Benhammou; Louis Helary Subject: Re: Gamma beam profiler readout
Dear Marco,I checked and :
- you can connect to an external clock (NIM/VSDL) so it could accept the TLU signal
- the software is under windows. There is two ways to communicate: ethernet or USB. I think that it will be easy to encapsulate the ethernet frames within a EUDAQ component. It could be more difficult with the USB port but still doable.
Good News for the use
of CAEN FERS 5200 system

## Slide 5: News
ELBE TB experts must be contacted (Marco, Sergej)
No news from Bologna on the support PCB
  Only comment: 40 um tracks spacing  60 um
  August is a bad month: news on this item expected toward the end of August
The date of the next meeting has to be decided
  If no urgent matters, I propose August 26th

## Slide 6: Backup

## Slide 7: The maximum dose absorbed by a material
The maximum dose D absorbed by the detector exposed to radiation for a time T is
(1)
where A is the peak energy per time unit released on a surface dS and the other symbols definition is evident
In case of a gaussian beam profile of ET total energy per unit of time
which, plugged in (1) gives
(2)

## Slide 8: Maximum GBP dose in LUXE
Equivalent to a total dose D1y per year of LUXE run
This dose is actually one order of magnitude less than the one reported in the CDR (where beam width was ~ 100 um)
  we should keep in any case 10 MGy as target for our tests

## Slide 9: Total dose in a test beam
From (2) it follows that, in order to irradiate the detector with the same dose of the experiment one should run for a time T’
(3)
where the test beam characteristics are primed
From (3), assuming T=107 s

## Slide 10: Frascati
Beam spot: 1cm x 1mm
Beam Intensity: 1010e/s @ 60 keV (MIP energy release) = 6 105 GeV/s
~ 300000 s ~ 3.5 days

## Slide 11: HZDR (Helmoltz Zentrum Dresden Rossendorf)
Beam spot: 4 mm diameter  12.6 mm2
20 MeV electrons  dE/dx ~ 7.2 MeV/cm (Al2O3) ~ 70 keV (dz=100 um)
Max Beam current 0.1 mA  After collimator: 0.03 mA  2 1014 e/s 1.4 1010 GeV !
In this condition: T’MIN~ 20 s !
A beam current of 25 nA would allow to measure in 1 day

## Slide 12: Detector current vs beam current at ELBE
0.03 mA  2 1014 e/s  ~ 2 1014 x 70 keV/27 eV x 0.5 cce x 1.6 10 -19
About 40 mA ~ uniformly distributed on 12.6 mm2 (40 strips)
HV = 200V  8 Watt on the detector !
The CAEN A7038 3 has 100 uA max Current and 500 pA Current monitor resolution
  This constraints the beam currents in the range (0.125E-3,0.25) uA
The max detector current in LUXE: 250 GeV/27 eV x 0.5 cce x 1.6 E-19 ~ 740 pA
  is this acceptable with the A7038 32/48 ratings ?
  Mod A1561H can read 50 pA (but 20 uA max current) : https://www.caen.it/products/a1561h/

## Slide 13: Test structures on sapphire wafer (tbd)
23x22 mm
23x10 mm
Per 2-inch wafer:
2 Standard strip sensors
2 Test structures
Configuration of electrodes
on the test structure could be
different from the nominal one.
Number of strips, width, pitch
are to be discussed ASAP.

## Slide 14: Test Beam plans (2022 and beyond)
Radiation hardness study (1-2 sensors) (ELBE). Beam requirements: ~ 2 mm beam spot, e- ~ 10 MeV, intensity ≥ 105 /bunch. Measure the sensor response vs time for the stable beam conditions until several MGy accumulated local dose. Control HV current (beam on/off). For several doses perform HV scan. Displace sensor wrt the beam and repeat measurements. Different producers
Scan of metallized sapphire sensors for response uniformity study (ELBE/FRASCATI): all sensors before final installation. Beam requirements: ~ 2 mm beam spot, e- ~ 10 MeV, intensity ≥ 105 /bunch. Measured variables: signals from strips, current in the HV circuit. At several positions measure dependence of signal size on HV.
Study of profiler performance in the narrow electron beam (DESY) Required beam spot size ≤ 0.1 mm. Sensor inclination wrt the beam allows to simulate elliptic spot shape. Make the detailed scan in the direction perpendicular to the strips and find reconstructed beam parameters. Use also previously irradiated detectors. Use the movable beam
Repeat performance study at the photon beam (Facultative) (spontaneous emission U1/U2 beamlines XFEL). Energetic photons (i.e. Bremsstrahlung) would be useful, and this option is being investigated
Beginning of 2022
Individual strip readout not necessary
<1 week
Spring of 2022
Individual strip readout necessary
<=1 week
End of 2022
Individual strip readout necessary
GBP movable table necessary
1 week

## Slide 15: First comments about readout PCB
So far the PCB expert in Bologna has only pointed out to me that isolation between tracks of 40 um is very challenging and not only does it limit the number of companies able to do it, it also increases costs.
As a first remark, he says that maybe even just 60 um (if possible per type of signal) would be much better.
More about this in the following days

## Slide 16: Repository for documents
I put the relevant documents and their list (excel table) in a local Dropbox directory
  https://www.dropbox.com/s/fp3zru83xj46a4n/GBP_repository.xlsx?dl=0
Kyle is taking care to store and maintain his MC analysis codes in confluence
  https://confluence.desy.de/display/LUXE/Gamma+Beam+Profiler
  Please cross check all this material and send your comments