## Slide 1: The RF of PETRA IV.
Stefan Wilke, DESY MHF-e
25th ESLS rf meeting Hamburg, 8th/9th nov 2021

## Slide 2: We miss him so much.
Michael Ebert (+ 2021-03-06)

## Slide 3: The RF of PETRA IV.
- Lots of activities at DESY
- Short view on the present RF-system at P3
- CDR P4
  main parameter of the machine
  RF parameter
  active 3rd harmonic RF
- RF at DESY IV
- Tests of P4 RF components in P3
Overview

## Slide 4: Lots of activities at DESY.
24/7 operating of XFEL, PETRA3, DESY2, FLASH
FLASH2020+: new undulators, new rf-modules Operation from 2025
KALDERA: A high-power laser for plasma accelerators. Operation from 2026
Some major competitions to PETRA IV

## Slide 5: The existing RF system.
PETRA III
RF parameters
frequency: 499.664 MHz
harmonic number: 3840
20 MV cavity voltage
12 × 7 cell nc cavities
RF power: up to 4 × 800 kW (2 Thales and 2 Philips klystrons)
ELWIS: modular control system based on PXI crates (Windows, LabVIEW, TINE)
transmission line to the other side
tunnel

## Slide 6: PETRA IV.
The future from 2028 (Dark time: 2026-27)

## Slide 7: PETRA III vs PETRA IV.
mostly reuse of the
old tunnel segments
of PETRA 1 from 1976
Thanks to
Michael Bieler

## Slide 8: Some main parameters in comparison.
 | PETRA III | PETRA IV (CDR)
Energy / GeV | 6.08 | 6.08
Circumference / m | 2304 | 2304
Revolution frequency / kHz | 130.121 | 130.121
Beam lines | 26 | 30
Number of bunches (timing-, brightness mode) | 40, 480 | 80, 1600
Beam current / mA | 100, 120 | 80, 200
Bunch current / mA | 2.5, 0.25 | 1, 0.125
Emittance (hor./vert.) / pm rad | 1300 / 10 | <50 / 10, <20 / 4
Energy loss (ID closed) / MeV per turn | 5 | 4.024
Momentum comp. factor | 0.001127 | 0.00001485
RF voltage / MV | 20 | 8 + 2.4
Synchrotron frequency / kHz | 6 | 0.421
RF frequencies / MHz | 499.6 | 499.6 + 1500
Harmonic number | 3840 | 3840

## Slide 9: PETRA IV RF.
fundamental
Parameters for the PETRA IV fundamental RF system:
500 MHz single cell nc cavity
HOM damped
reuse of plungers and couplers
see presentation
‚Plunger Refurbishment‘
(Nils-Oliver Fröhlich)
Main (fundamental) RF frequency | 499.65 MHz
Total voltage main RF | 8 MV
RF voltage per cavity | 476 kV
Transit Time Factor | 0.7
RF voltage per cavity seen by the electrons | 333 kV
Cavity wall loss | 16.3 kW
Quality factor (unloaded) | 29600
Cavity coupling factor | 3.0
Shunt impedance Rs=V²/(2P) | 3.4 MΩ
Loaded quality factor | 7400
Number of main RF cavities | 24
Synchronous phase | 30.2
Synchrotron frequency | 421 Hz
Total wall loss in cavities | 392 kW
Total beam loading power | 800 kW
Nominal transmitter power per RF station | 110 kW
Beam tube aperture | 74 mm
Length of cavity (flange to flange) | 500 mm
Main (fundamental) RF frequency | 499.65 MHz
Total voltage main RF | 8 MV
RF voltage per cavity | 476 kV
Transit Time Factor | 0.7
RF voltage per cavity seen by the electrons | 333 kV
Cavity wall loss | 16.3 kW
Quality factor (unloaded) | 29600
Cavity coupling factor | 3.0
Shunt impedance Rs=V²/(2P) | 3.4 MΩ
Loaded quality factor | 7400
Number of main RF cavities | 24
Synchronous phase | 
Synchrotron frequency | 421 Hz
Total wall loss in cavities | 392 kW
Total beam loading power | 800 kW
Nominal transmitter power per RF station | 110 kW
Beam tube aperture | 74 mm
Length of cavity (flange to flange) | 500 mm

## Slide 10: two frequencies.
Bunch length:
- without a 2nd RF-system: 5 ps (1.5 mm)
- with an additional RF-system (3rd harmonic): 65 ps (ca. 20 mm)
So the single bunch current could be increased
The required harmonic RF voltage for a flat potential at the bunch transition is
n: order of the harmonic (PETRA IV: 3) U0: energy loss per turn (4.0 MeV) Vrf: voltage of the fundamental RF system (8.0 MV) qe: elementary charge (1.602 * 10-19 C)
This gives an optimum value for the harmonic voltage of VHHC,opt. = 2.26 MV. With some safety margin, the system is designed for VHHC = 2.4 MV.
lengthen the bunch with a second active RF-system
corrected: 23 ps (7 mm)
corrected:
60 ps (18 mm)

## Slide 11: PETRA IV RF.
third-harmonic
Parameters for the PETRA IV third-harmonic RF system:
3rd harmonic RF frequency | 1498.995 MHz
Total RF voltage | 2.4 MV
RF voltage per cavity | 100 kV
Cavity wall loss | 3.3 kW
Quality factor (unloaded) | 17000
Loaded quality factor | 2700
Total wall loss in cavities | 71 kW
Cavity coupling factor | 5.3
Shunt impedance Rs=V²/(2P) | 1.5 MΩ
Number of RF stations (cavity/SSA) | 24
Nominal transmitter power per RF station | 10 kW
Beam tube aperture | 46 mm
Length of cavity (flange to flange) | 313.6 mm
Collaboration ALBA/HZB/DESY
Development of a 3rd harmonic HOM damped cavity
1/3 scaled and optimize from 500 MHz
see presentation tomorrow (Jesús Ocampo)
In addition there are some ideas of alternatives
see presentation of Peter Hülsmann

## Slide 12: RF System Design.
A worst case scenario (200 mA beam current):
Only 5 of the 6 systems (each a group of 4 SSA/Cav) running
and in addition a failure of one sub-system (SSA/Cav).
This brings the cavities to their limit.
µTCA crate
More details see presentations tomorrow
(Frank Maschewski, Arvid Eislage)
Each of the 24 cavities is powered by its own Solid State Amplifier (SSA) and we want to control them in 6 groups of 4 pairs of cavity/SSA.

## Slide 13: RF implementation in PETRA IV.
new tunnel segment and new hall: 24 + 24 cavities and 24 + 24 SSA
tunnel

## Slide 14: DESY IV.
Booster parameters:
Circumference: 316.8 m
Harmonic number: 528
Repetition rate: 2 Hz to 5 Hz
Momentum compaction: 3.30 × 10−3
Beam energy at 6 GeV 700 MeV
Energy loss per turn 4.04 MeV 0.748 keV
A new machine (DESY IV) in the same tunnel as
the existing and remaining DESY II.
RF:
9 (grouped in 3 locations) 5-cell 500 MHz nc cavities
each powered by a SSAs
Frequency | 499.65 MHz
Total RF voltage | 12 MV
RF voltage per cavity | 1.3 MV
Cavity wall loss | 59 kW
Quality factor (unloaded) | 29500
Cavity coupling factor | nyd
Shunt impedance Rs=V²/(2P) | 15 MΩ
Number of RF 5-cell cavities | 9
Beam tube aperture | 120 mm
Cavity length (flange to flange) | 1800 mm

## Slide 15: Tests of P4 RF components in P3.
One prototype SSA and one prototype HOM damped 500 MHz single cell cavity
Delivery SSA: July 2022
Delivery cavity: March 2022

## Slide 16: Thank you for lending your ears.
Additions or questions?
Sailing vessel (four-masted barque) „Peking“ back in Hamburg 2020-09-07

## Slide 17
Stefan Wilke
DESY, MHF-e
stefan.wilke@desy.de
049/40/8998-1836