## Slide 1: F and Q Measurements on Normal Conducting HOM Damped Cavity
Shivaji Pande
On behalf of DLS RF Group

## Slide 2: RF at Diamond Light Source
3GeV 300mA third generation synchrotron light source
Diamond has been operating for users since January 2007

## Slide 3: Storage Ring RF
One high voltage power supply supports four IOTs which are then combined
Superconducting cavity supported by Air Liquide cryogenic plant
Space for three cavities in RF straight, usually two operational
Two extra EU HOM damped cavities installed in 2017-2018

## Slide 4: New storage ring RF configuration
Third HOM Damped cavity is ready to be installed in Straight 15
Has been conditioned
For ease of conditioning / reduce reflected power, b = 1
For operation in the ring, b = 5
Is kept under vacuum
Straight 15
3rd NC Cavity

## Slide 5: Diamond II upgrade - RF Requirements
Power required for 300mA with all IDs 460kW
Total voltage required 2.7 MV
Number of cavities | 6 | 7 | 8 | 9
Optimal cavity coupling | 3.8 | 4.3 | 4.7 | 5.2
Individual cavity voltage | 450 kV | 386 kV | 338 kV | 300 kV
Generator power per cavity | 104 kW | 85 kW | 73 kW | 63 kW
Power dissipated per cavity | 27 kW | 20 kW | 15 kW | 12 kW
Power dissipated in all cavities | 164 kW | 140 kW | 123 kW | 109 kW
Operation with 8 normal conducting cavities
  Reduces voltage per cavity to conservative level
  Minimises running costs
  Gives acceptable total wall power losses
  Allows redundant operation should one cavity fail
  Enables cavities to fit in storage ring

## Slide 6: Location of Amplifiers and Cavities
Diamond-I RF is concentrated in one area
  Amplifiers in RF hall
  Cavities in single RF straight
Diamond-II cavities can be distributed in pairs around available mid-section straights
  New beamline can be installed in present RF straight
  Seven mid-section straights are available
  Installation of most new amplifiers is possible with no impact on operating RF
Available mid-section straights

## Slide 7: R/Q Data
Requirement from Acc Phys Group for the HOM data for Diamond II Upgrade
Cavity is available for measurements
Unavailability of bead pull setup at Diamond
Measure f, Q and b for the HOMs
Estimate f, RSH, and Q with CST Studio
As R/Q is constant, estimate RSH from measured Q
Observation : Qmeas << QCST
Data for 100MHz band from 450 – 1100 MHz
Data for 200MHz band from 1.1 to 2.5GHz

## Slide 8: Measurements
Coupler adjusted to b = 5
Pickup
VNA
Cavity waiting to be installed in the ring
S11 fundamental mode
S21 fundamental mode

## Slide 9: CST Model
Coupling coefficient on the model
b = 5

## Slide 10: CST Eigen Mode - R and Q Estimated
The Volume losses depend upon ferrite tand and so Q

## Slide 11: CST – Total, Surface and Volume losses

## Slide 12: CST Eigne mode - R/Q and Q
Only 3 HOMs with 10W < R/Q < 50W
And
27 HOMs with R/Q > 1W

## Slide 13: Measurements : S11 (dBMag)

## Slide 14: S21 (dBMag)
Each colour represents measurement with 10k points

## Slide 15: Measured S21 600 – 700MHz
TE111 Modes
TM011 Modes

## Slide 16: Measured S21 700 – 800MHz

## Slide 17: S21 800-900MHz
TE2xx Mode
HOM Waveguide Mode

## Slide 18: Mode @ 855 MHz
Q = 4356

## Slide 19: Mode @855 MHz Cut @ Z = 0
Z = 0 mm
E
H
HOM Waveguide Mode
Eigen Mode solver

## Slide 20: Mode @855 MHz Cut @ Z = 49.5mm
Z = -49.5 mm
E
H
Z = 49.5 mm
E
H
HOM Waveguide Mode
f = 860.793 MHz

## Slide 21: Mode @855 MHz Cut @ X = 0
X = 0 mm
E
H
HOM Waveguide Mode
Eigen Mode Results
 | E Mode | Freq Domain | Measured
f (MHz) | 860.793 | 860.783 | 855.14
Q | 5936 | 5971 | 4350
R/Q | 0.35 | 0.39 | Not measured
Field is much stronger in HOM waveguide than the cavity volume

## Slide 22: Determination of R|| and R
The shunt impedance for the monopole modes defined on axis
The transverse impedance for the dipole / deflecting modes defined r0 off-axis
Where P = power loss, k = 2/ and r0 is radial offset where the integral is calculated.

## Slide 23: R||/Q for the Monopole Modes
Mode | Freq FD | Freq meas | Q FD | QL meas | R// FD | R///Q FD | Desig’n | b FD | b meas | Q0meas | Qm/QFD | R//eff (W)
2 | 0.500497 | 0.49971 | 3.45E+04 | 5.40E+03 | 7.83E+06 | 227.11 | TM010 | 5.061732 | 4.964 | 32175.78 | 9.33E-01 | 5.03E+03
9 | 0.663948 | 0.66165 | 1.93E+04 | NM | 8.78E+05 | 45.58 | TM011L | 0.511616 | 0.01506 | NM | NM | NM
12 | 0.69697 | NM | 1.53E+04 | NM | 7.78E+05 | 50.82 | TM011L | 0.424802 | NM | NM | NM | NM
15 | 0.764009 | 0.7602 | 8.51E+03 | NM | 5.11E+04 | 3.00 | TM011L | 0.211519 | 0.014286 | NM | NM | NM
23 | 0.86078 | 0.85514 | 5.97E+03 | 4350 | 2.36E+03 | 0.40 | HOMWG | 0.125879 | 0.255754 | 5462.53 | 9.15E-01 | 3.98E+03
30 | 0.971305 | 0.9749 | 6.78E+03 | 2010 | 2.84E+03 | 0.42 | HOMWG | 0.015004 | 0.329489 | 2672.273 | 3.94E-01 | 7.92E+02
88 | 1.321991 | 1.32202 | 1.98E+04 | 150 | 5.72E+03 | 0.29 | TM021 | 0.446763 | 0.01 | 151.5 | 7.67E-03 | 1.15E+00
124 | 1.508321 | 1.508 | 1.23E+04 | NM | 5.12E+04 | 4.16 | TM012 | 0.101294 | 0.01 | NM | NM | NM
130 | 1.53231 | 1.53203 | 1.62E+04 | 1600 | 7.51E+04 | 2.64 | TM012 | 0.123449 | 0.005 | 1608 | 9.94E-02 | 1.59E+02
138 | 1.5669 | 1.573 | 1.82E+04 | 400 | 1.79E+04 | 0.99 | TM212 | 0.268038 | 0.01 | 404 | 2.22E-02 | 8.90E+00
139 | 1.577681 | 1.57934 | 2.52E+04 | 1070 | 3.29E+04 | 1.31 | TM212 | 0.051364 | 0.01 | 1080.7 | 4.30E-02 | 4.60E+01
146 | 1.589114 | 1.5882 | 1.57E+04 | 200 | 2.38E+04 | 1.51 | TM212 | 0.10438 | 0.01 | 202 | 1.28E-02 | 2.57E+00
277 | 1.916443 | 1.9214 | 2.04E+04 | 180 | 3.12E+04 | 1.53 | TM221 | 0.258744 | 0.01 | 181.8 | 8.93E-03 | 1.61E+00
290 | 1.953699 | 1.95878 | 2.53E+04 | 300 | 5.32E+04 | 2.10 | TM2X2 | 0.197813 | 0.04 | 312 | 1.23E-02 | 3.69E+00
439 | 2.265918 | 2.25564 | 2.15E+04 | 300 | 5.78E+03 | 0.27 | TMX22 | 0.258732 | 0.9 | 570 | 2.65E-02 | 7.95E+00

## Slide 24: R^/Q for Dipole modes with r0 = 3mm
Mode | Freq F Domain | Freq measured | Q F Domain | QL measured | R// 3mm | R^(W/m) 3mm | R^/Q 03mm | b measured | Q0meas | Designation | Qm/QCST | R^/Q eff 03mm | R^ eff 03mm
3 | 0.630569 | 0.62895 | 23520 | 100 | 24890.63 | 2.09E+08 | 8896.285 | 0.064309 | 106.4309 | TE111D | 0.004525 | 40.25679 | 9.47E+05
4 | 0.631993 | 0.6311 | 21780 | 200 | 76471.5 | 6.41E+08 | 29450.19 | 0.056433 | 211.2866 | TE111VD | 0.009701 | 285.6947 | 6.22E+06
5 | 0.634288 | 0.63414 | 21440 | 500 | 205932.3 | 1.72E+09 | 80265.79 | 0.171999 | 585.9995 | TE111VD | 0.027332 | 2193.83 | 4.70E+07
6 | 0.645022 | 0.6433 | 20057 | NM | 8491.189 | 69789810 | 3479.574 | 0.038685 | NM | TE111 | NM | NM | NM
8 | 0.647364 | 0.64688 | 23799 | 300 | 219.1689 | 1794853 | 75.41715 | 0.086655 | 325.9965 | TE111 | 0.013698 | 1.033057 | 2.46E+04
14 | 0.759483 | 0.74641 | 8795 | NM | 30356.29 | 2.12E+08 | 24092.57 | 0.118624 | NM | TM111VD | NM | NM | NM
21 | 0.846087 |  | 7055 | 150 | 4092.96 | 25646070 | 3635.42 |  | 150 | TM111VD | 0.021262 | 77.29454 | 5.45E+05
22 | 0.84776 |  | 8246 | 150 | 248.5997 | 1554627 | 188.5219 |  | 150 | TM111HD | 0.018191 | 3.429334 | 2.83E+04
23 | 0.86078 | 0.85514 | 5971.4 | 4350 | 645.8229 | 3977573 | 666.1039 | 0.255754 | 5462.53 | HOMWG | 0.914782 | 609.3399 | 3.64E+06
25 | 0.899576 | 0.891211 | 11764 | 230 | 15.46077 | 91115.34 | 7.745269 | 0.01 | 232.3 | TM110HD | 0.019747 | 0.152943 | 1.80E+03
26 | 0.90327 |  |  | NM | 12.1172 | 71118.59 | 5.828914 |  | NM | TM110VD | NM | NM | NM
34 | 1.02917 | 1.03016 | 22007 | 260 | 6710.924 | 34569450 | 1570.839 | 2.02 | 785.2 | TMXXX Hybrid | 0.03568 | 56.04684 | 1.23E+06
39 | 1.046574 | 1.04214 | 12860 | 350 | 21812.72 | 1.1E+08 | 8591.392 | 0.561798 | 546.6293 | TM112~VD | 0.042506 | 365.1871 | 4.70E+06
41 | 1.060609 | 1.06566 | 16380 | 770 | 41374.59 | 2.07E+08 | 12622.83 | 0.260417 | 970.5211 | TM112 VD | 0.05925 | 747.9074 | 1.23E+07
53 | 1.106478 | 1.10908 | 7711 | 600 | 19932.29 | 95502110 | 12385.18 | 0.01 | 606 | TM112Offcentre | 0.078589 | 973.3393 | 7.51E+06
128 | 1.522945 | 1.5183 | 13630 | 600 | 22490.83 | 78292390 | 5742.858 | 0.01 | 606 | TM112D | 0.044461 | 255.3318 | 3.48E+06

## Slide 25: R^/Q for Dipole modes with r0 = 30mm
Mode | Freq F Domain | Freq measured | Q F Domain | QL measured | R// 30mm | R^(W/m) 30mm | R^/Q 30mmOF | b measured | Q0meas | Designation | Qm/QCST | R^/Q eff 30mm | R^ eff 30mm
3 | 0.630569 | 0.62895 | 23520 | 100 | 5414.048 | 455184.6 | 19.35062 | 0.064309 | 106.4309 | TE111D | 0.004525 | 0.087564 | 2.06E+03
4 | 0.631993 | 0.6311 | 21780 | 200 | 111144.7 | 9323414 | 428.033 | 0.056433 | 211.2866 | TE111VD | 0.009701 | 4.152325 | 9.04E+04
5 | 0.634288 | 0.63414 | 21440 | 500 | 202367.1 | 16914210 | 788.7619 | 0.171999 | 585.9995 | TE111VD | 0.027332 | 21.55849 | 4.62E+05
6 | 0.645022 | 0.6433 | 20057 | NM | 8422.405 | 692244.7 | 34.51387 | 0.038685 | #VALUE! | TE111 | NM | NM | NM
8 | 0.647364 | 0.64688 | 23799 | 300 | 5382.203 | 440768 | 18.52044 | 0.086655 | 325.9965 | TE111 | 0.013698 | 0.253691 | 6.04E+03
14 | 0.759483 | 0.74641 | 8795 | NM | 31358.56 | 2188953 | 248.8804 | 0.118624 | #VALUE! | TM111VD | NM | NM | NM
21 | 0.846087 |  | 7055 | 150 | 4610.314 | 288877.6 | 40.9494 |  | 150 | TM111VD | 0.021262 | 0.870646 | 6.14E+03
22 | 0.84776 |  | 8246 | 150 | 6397.146 | 400047.8 | 48.51181 |  | 150 | TM111HD | 0.018191 | 0.882461 | 7.28E+03
23 | 0.86078 | 0.85514 | 5971.4 | 4350 | 706.6784 | 43523.77 | 7.288705 | 0.255754 | 5462.53 | HOMWG | 0.914782 | 6.667577 | 3.98E+04
25 | 0.899576 | 0.891211 | 11764 | 230 | 1355.683 | 79894.82 | 6.791468 | 0.01 | 232.3 | TM110HD | 0.019747 | 0.134109 | 1.58E+03
26 | 0.90327 |  |  | NM | 188.0674 | 11038.1 | 0.904688 |  | #VALUE! | TM110VD | NM | NM | NM
34 | 1.02917 | 1.03016 | 22007 | 260 | 8331.794 | 429189.1 | 19.50239 | 2.02 | 785.2 | TMXXX Hybrid | 0.03568 | 0.695837 | 1.53E+04
39 | 1.046574 | 1.04214 | 12860 | 350 | 30234.09 | 1531530 | 119.0833 | 0.561798 | 546.6293 | TM112~VD | 0.042506 | 5.061775 | 6.51E+04
41 | 1.060609 | 1.06566 | 16380 | 770 | 41445.8 | 2071684 | 126.4456 | 0.260417 | 970.5211 | TM112 VD | 0.05925 | 7.491949 | 1.23E+05
53 | 1.106478 | 1.10908 | 7711 | 600 | 18958.6 | 908368.4 | 117.8016 | 0.01 | 606 | TM112Offcentre | 0.078589 | 9.257913 | 7.14E+04
128 | 1.522945 | 1.5183 | 13630 | 600 | 9887.411 | 344188.8 | 25.24674 | 0.01 | 606 | TM112D | 0.044461 | 1.122489 | 1.53E+04

## Slide 26: Comparison with BESSY Results
Freq measured | R^/Q eff 03mm | R^ eff 03mm (W/m) | R^/Q eff 30mm | R^ eff 30mm (W/m)
0.62895 | 40.25679 | 9.47E+05 | 0.087564 | 2.06E+03
0.6311 | 285.6947 | 6.22E+06 | 4.152325 | 9.04E+04
0.63414 | 2193.83 | 4.70E+07 | 21.55849 | 4.62E+05
0.6433 | NM | NM | NM | NM
0.64688 | 1.033057 | 2.46E+04 | 0.253691 | 6.04E+03
0.74641 | NM | NM | NM | NM
 | 77.29454 | 5.45E+05 | 0.870646 | 6.14E+03
 | 3.429334 | 2.83E+04 | 0.882461 | 7.28E+03
0.85514 | 609.3399 | 3.64E+06 | 6.667577 | 3.98E+04
0.891211 | 0.152943 | 1.80E+03 | 0.134109 | 1.58E+03
 | NM | NM | NM | NM
1.03016 | 56.04684 | 1.23E+06 | 0.695837 | 1.53E+04
1.04214 | 365.1871 | 4.70E+06 | 5.061775 | 6.51E+04
1.06566 | 747.9074 | 1.23E+07 | 7.491949 | 1.23E+05
1.10908 | 973.3393 | 7.51E+06 | 9.257913 | 7.14E+04
1.5183 | 255.3318 | 3.48E+06 | 1.122489 | 1.53E+04
Frequency(MHz) | Quality | R/Q(W) | Impedance(k W) | R/Q(W) | Impedance(k W /m)
 |  | measured on axis |  | measured @ 3 cm off axis | 
619.68 | 918 | 0.36 | 0.33 | 0.28 | 22.0(H)
620.126 | 1079 | 0.14 | 0.15 |  | 
625.832 | 770 | 0.5 | 0.38 | 0.69 | 44.8(H)
639.39 | 556 | 0.32 | 0.18 |  | 
643.925 | 557 | 2.82 | 1.57 |  | 
654.575 | 168 | 6.02 | 1.01 |  | 
679.95 | 334 | 32.05 | 10.72 |  | 
812.508 | 284 | 0.61 | 0.17 |  | 
1024.224 | 1016 | 0.22 | 0.22 | 0.91 | 48.4(V)
1029.465 | 1085 | 0 | 0 | 0.78 | 43.3(H)
1037.66 | 1213 | 0.002 | 0 | 0.95 | 58.6(V)
1040.318 | 1578 | 0.04 | 0.07 |  | 
1041.307 | 485 | 0 | 0 |  | 
1057.539 | 772 | 0.59 | 0.46 | 0.82 | 31.8(V)
1083.7 | 748 | 0.12 | 0.09 | 1.31 | 45.2(H)
1338.864 | 479 | 0.77 | 0.37 |  | 
1384.696 | 511 | 0.18 | 0.09 | 1.18 | 23.1(H)
1511.12 |  | noisy | noisy | 0.58 | 15.2(V)
1533.813 | 664 | 0.83 | 0.55 | 1.3 | 29.7(V)
1539.625 | 686 | noisy | noisy |  | 
1578.385 | 1628 | 0.72 | 1.17 |  | 
1583.331 | 684 | 0 | 0 |  | 
1591.087 | 583 | noisy | noisy |  | 
2284.448 | 649 | 0.85 | 0.55 |  | 
2321.303 | #DIV/0! | 0 |  |  | 
2596.775 | 817 | 0.02 | 0.02 |  | 
2662.078 | 551 | 0.69 | 0.38 |  | 
 F. Marhauser, E. Weihreter; Impedance Measurements of the HOM-Damped 500 MHz Metrology Light Source Cavity; Report bessy-034-january-2007

## Slide 27: Computation from Wake Potential

## Slide 28: Comments?
R^ is prone to an error due to choice of the offset?
A factor of 10^2 in R^ depending upon choice of radial offset of 3mm and 30mm
Is the defining equation for R^ valid in the vicinity of axis or anywhere in the beam tube aperture?
Colleagues at DESY planning for the perturbation measurements
Eagerly wait for the results!

## Slide 29: Thanks for your attention