## Slide 1: Test beam

## Slide 2
Full test beam is from the 1/11 to the 15/11
The ECAL will have the second week : 8/11-15/11
Need to have a safety course (usually on the Monday 13:00) to be able to access the area.
  Louis is checking if possible to get the course with zoom on the 1/11 : Marcel doesn’t seem to like this solution

## Slide 3: Proposition for the TB mechanics
If we need more W planes, we install it before the stack
3 Detectors
W planes
beam

## Slide 4
Detectors to test | Number of sensors
GaAs with traces | 2
GaAs without traces | 2
CALICE sensors (standard gluing) | 2
CALICE sensors (ACF gluing) | 2+2
DAQ rate : 200-600 Hz.
Let’s suppose :
200 Hz
3 different tungsten configurations
3 points per sensor
10 sensors
Detectors to test | Number of sensors | Type of test | Number of event per point | Time per point
GaAs with traces | 2 | Cross talk/signal | 1 M | 1.5h
GaAs without traces | 2 | signal | 500k | 50min
CALICE sensors (standard gluing) | 2 | signal | 500k | 50 min
CALICE sensors (ACF gluing) | 2+2 | signal | 200k | 20min

## Slide 5: schedule
Day one : 2 GaAs traces + GaAs no traces. 3 points x 3 tungsten configuration = 9 points x1.5 h = 13.5h
Day two : 1 GaAs no traces + 2 CALICE. 3 points x 3 tungsten configuration = 9 points x 50 minutes ~ 9 hours
Day three : 2x 2 CALICE sensor with ACF. 3 points x 1 tungsten configuration = 3 points x 20 minutes = 2 x 1 hours = 2 hours
This take into account the set up modification :
Opening of the mainframe to add tungsten planes : 2 hours
Opening of the mainframe to replace sensors : 4 hours