## Slide 1: DQ/SC monitoring +few words about trigger

## Slide 2: SC monitoring (no DAQ data)
Current/voltage of sensors : 1 plot (with current and voltage) x number of HV power supplies on the same plot (looks like we will start with 2 PS)
Current/voltage of FEBs : 1 plot (with current and voltage)x (number of FEBs || number of layers) on the same plot.
FEB temperature : 1 plot with the temperature of all the FEBs.
FPGA temperature/current ?
Humidity/temperature in the frame ?
ASIC status ?
Between 3 and 6 plots

## Slide 3: DQ monitoring
Dead channels : 1 histo
Ped values (mean and sigma) : 1 histo
Signal values as a function of XY for each planes (20 x 2D histos)
Projection of signal in X, Y and Z (3 x 1D histo)
Multiplicity

## Slide 4: trigger
Problem : the trigger has to be synchronize with the DAQ in order to use the power pulsing feature. If FEBs on all the time (no power pulsing), power used is between 2mW to 4mW.
Triggers:
  Electron beam : needed and no problem because given frequency (1Hz) (generated by the TLU)
  Electron-laser interaction : needed and no problem because given frequency (0.1Hz) (generated by the TLU)
  Pedestal inter electron packet : needed and no problem (generated by the FPGA and not by the TLU)
  Cosmic: needed on the surface and problem (42W to 84W for the ECAL). (can be generated by the TLU or NIM modules)