## Slide 1
Overview on GSI
Heavy Ion Accelerator Facility
ARD ST3 Annual Meeting September 2022
HZB Berlin, 7th of September 2022
Peter Forck, GSI
on behalf of the GSI Accelerator Department
For peace
and freedom
Solidarity
with Ukraine

## Slide 2
The GSI Accelerator Facility
Fragment
Separator
Ion sources
SIS: Emax=2 GeV/u
 =95%
Storage rings:
ESR
CRYRING
UNILAC: Emax=12 MeV/u =16%
Fix-
target Exp.
UNILAC: all ions p – U
Energy: 3 – 12 MeV/u
Pulse operation: 50 Hz, max. 5 ms
Up to 20 mA current
Synchrotron, Bρ=18 Tm, dB/dt up to 10 T/s
Emax p: 4.7 GeV & U: 0.9 GeV/u
Achieved e.g.: Ar18+: 1·1011
U28+: 3·1010 & U73+: 1·1010
Radioactive beams
Nuclear Physics
Atomic & Plasma Physics
Bio Physics
ESR: Bρ=10 Tm
CRYRING, Bρ=1.4 Tm

## Slide 3
Beam Time Schedule Feb.-June 2022: Exemplarily for March
3 ion
sources
LINAC
users
Synchr.
users
Storage
rings
proton beam
light ions Li&C
medium & heavy ions U
LINAC rf power increase
for U beams
Ion | H | Li | C | O | Ar | Fe | Ni | Au | Pb | Bi | U
Current [mA] | 1 | 0.005 | 0.045 | 1 | 3 | 0.05 | 0.025 | 0.025 | 0.5 | 0.015 | 0.5
LINAC beam current in front of synchrotron

## Slide 4
Beam Ability 2022
Features:
LINAC with 50 Hz pulsing, max. pulse length 5 ms
‘parallel’ operation,
i.e. each LINAC pulse can have different source and target
Synch SIS18 is filled by LINAC, typical cycle time  3 s
Storage ring might have hours storage times
Chart: Beamtime 2022
| Beam on Target | Interruption | Setup
 | 0.75111 | 0.14072 | 0.10817
Proton beam
(mainly behind SIS)
Li&C
rf cond.
Many ions & targets
Operation weeks in 2022
February
June
168h=1week
equivalent time for
beam-on-target
March: previous slide

## Slide 5
UNILAC at GSI: Overview
MEVVA
MUCIS
PIG
RFQ IH1 IH2
Alvarez DTL
HLI: (ECR,RFQ,IH)
Transfer to
Synchrotron
2.2 keV/u
β = 0.0022
120 keV/u
β = 0.016
11.4 MeV/u
β = 0.16
RFQ, IH1, IH2
Gas Stripper
U4+
U28+
Alvarez DTL
Single Gap Resonators
All ions, high current, 5 ms@50 Hz, 36&108 MHz
Foil Stripper
To SIS ↑
Constructed in the 70th, Upgrade 1999,
 Injector for FAIR ion operation
1.4 MeV/u
β = 0.054
10mm
frf = 36 MHz
frf = 108 MHz
U73+

## Slide 6
UNILAC: Built for heavy ion acceleration, e.g. 1st LINAC part 238U4+ i.e. A/q=238/4=59.5
For protons 1H+: Reduce of rf-voltage by factor 60, But: Outside of amplifier regulation
Proton Generation by molecular Ions
Ion source
CH3+ acceleration
Use of HSI heavy ion beam capabilies to acclerate hydro-carbon compounds
Dissociation of CH-compounds + stripping
H+ , 3 emA
C6+ , 6 emA
Gas target at 1.4 MeV
A. Adonin, R. Hollinger, et al.
CH3+ , 1 mA
10mm

## Slide 7
Proton Beam Dynamics with low Voltage & large Phase Offset
ALVAREZ Rf-voltage < 1V (s  -30°)?
  s  -57° (Urf  1.5V) 
  s  -65° (Urf  2.0V) 
  s < -65° (Urf > 2.0V) 
pros and cons of large negative phases:
  smooth rf-operation  
  slightly reduced transmission 
  emittance blow up 
  longitudinal phase space? 
see also: A. Rubin, et al.
Brilliant beam acceleration at longitudinal phase advances far beyond 90°, LINAC 2020
Simulations on operation of the new UNILAC post-stripper with intense proton beams: longitudinal phase advances below and beyond 90°. Acc. Sem., GSI, 2020
reduced synchr. phase?
Reference phase
Achievement:
3 mA before SIS18, sufficient for actual users
Typical emittance reached
(High current 50 mA by planned proton LINAC)
UNILAC: Built for heavy ion acceleration, e.g. 1st LINAC part 238U4+ i.e. A/q=238/4=59.5
For protons 1H+: Reduce of rf-voltage by factor 60, BUT: Outside of amplifier regulation

## Slide 8
Gas Stripper for efficient Change of Charge State: Hardware
UNILAC: Ion source high current, low charge state e.g. 238U4+
 1st LINAC part 238U4+ up to 1.4MeV/u (=5.5%)  gas stripper 238U4+  238U28+
 2nd part of LINAC 238U28+ up to 11.4 MeV/u (=15.5%)
However, only  15 % for q=28+ depending on gas and pressure
High pressure super-sonic gas jet required, inlet p = 120 bar, light molecules deliver small jet
Contradictory requirements: high density  good stripping, low density  lower straggling
Pulsed inlet to reduce gas load inn vacuum chamber

## Slide 9
Gas Stripper for efficient Change of Charge State: Results
distance
ion source
behind stripper
synchr.
emittance [mm mrad]
beam current [emA]
distance
ion source
behind stripper
synchr.
emittance [mm mrad]
beam current [emA]
N2
H2
Results:
Higher yield of 238U28+
for pulsed H2 jet
Lower emittance
due to lower straggling
Talk by Simon Lauber: Novel beam dynamics for heavy ion acceleration

## Slide 10
The GSI Accelerator Facility: Synchrotron
Fragment
Separator
Ion sources
SIS: Emax=2 GeV/u
 =95%
Storage rings:
ESR
CRYRING
UNILAC: Emax=12 MeV/u =16%
Fix-
target Exp.

## Slide 11
GSI Heavy Ion Synchrotron: Overview
Important parameters of SIS-18
Circumference | 216 m
Inj. type | Multiturn
Energy range | 11 MeV → 2 GeV
Acc. RF | 0.8 → 5 MHz
Harmonic | 4 (= # bunches)
Bunching factor | 0.4 → 0.08
Ramp duration | 0.06 → 1.5 s
Ion range (Z) | 1 → 92 (p to U)
injec-
tion
extrac-
tion
acceleration
Important parameters of SIS-18
extrac-
tion
injec-
tion
acceleration
Dipole, quadrupoles,
transfer line
rf cavity,
quadrupoles, dipoles
commissioning 1991
Ion (Z) | 1 → 92 (p to U)
Circumference | 216 m
Inj. type | Multiturn
Injection energy | 11 MeV/u
Max. final energy |  2 GeV/u
Ramp duration | 0.1 → 1.5 s
Acc. RF | 0.8 → 5 MHz
Harmonic | 4 (= # bunches)
Bunching factor | 0.4 → 0.08
Beam current | 10 µA to 100 mA

## Slide 12
Slow Extraction: Principle and Micro-Structure
Slow extraction for tex = 1 … 10 s frequently used:
Gentle excitation of a beam third order resonance
Beam physics: Extraction as ‘slow losses’
Particle crosses
stability-boarder sequentially
Exponential amplitude growth
 50 … 1000 turns
reaching septum and is extracted
Problem: Sensitivity to any
unintended resonance condition, e.g.:
Change of tune:
unintended quadrupole current ripples
Sextupoles: non-linear fields
Ion’s amplitude growth per turn
 Ttransit & xstep
Stored beam phase space at electrostatic septum
x
x’
ele.-stat. septum
thickness
last spiral step xstep
after 3 turns
transit time Ttransit
extr.
channel
shrinkage of
by tune scan
Qm (t)  n  1/3
 0
unintended quadrupole current ripple
 tune ripple
 bursts extracted
Example: C6+ at 300 MeV/u at GSI
2 s extraction
called ‘spill’
10 ms time window
Spiky structure is one major problem for users as it increases the detector dead time

## Slide 13
Possible mitigation:
Smaller horizontal emittance by crossing
shortly a coupling resonance Qx= Qy+1
 Significant improvement
Slow Extraction: Micro-Structure Improvement
Duty factor, i.e. normalized fluctuations
Other methods also tested related to
linear and non-linear beam dynamics
Part of EU-project IFAST-REX with
Collaboration: CERN, GSI, Medical Ion Therapy Centers
10 ms time window
10 ms
window

## Slide 14
The GSI Accelerator Facility: Storage Rings
Fragment
Separator
Ion sources
SIS: Emax=2 GeV/u
 =95%
Storage rings:
ESR
CRYRING
UNILAC: Emax=12 MeV/u =16%
Fix-
target Exp.

## Slide 15
Physics:
Momentum transfer by Coulomb collisions
Cooling force results from energy loss in the cold, co-moving electron beam
Cooling time: 0.1 s for low energy highly charged ions, 1000 s for high energy protons
Also Stochastic Cooling available at ESR
Electron cooling: Superposition ion and cold electron beams with the same velocity
e.g.: 220 keV electrons cool 400 MeV/u ions
electron
temperature
kBT  0.1 eV
kBT║  0.1 - 1 meV
Example:
Electron cooler at ESR Umax = 300 kV
Electron Cooling: Improvement of Beam Quality

## Slide 16
Physics:
Momentum transfer by Coulomb collisions
Cooling force results from energy loss in the cold, co-moving electron beam
Cooling time: 0.1 s for low energy highly charged ions, 1000 s for high energy protons
Also Stochastic Cooling available at ESR
Electron cooling: Superposition ion and cold electron beams with the same velocity
e.g.: 220 keV electrons cool 400 MeV/u ions
electron
temperature
kBT  0.1 eV
kBT║  0.1 - 1 meV
Electron Cooling: Improvement of Beam Quality
Example:
Electron cooling at ESR: 108 proton
at 400 MeV
t = 650 s
p/p0 = 310 -5
p/p0
= 410 -4

## Slide 17
Deceleration of Highly Charged Ions
SIS
stripper/ production target
400 MeV/u
UNILAC
FRS
ESR
4 MeV/u
HITRAP
Injection to trap  cooling to 4 K
4-10 MeV/u
CRYRING@ESR
4 MeV/u … 100 keV/u
400–X MeV/u
Slow ions are stored and well controlled
Energy range 10 MeV/u to sub eV/ion
105 to 107 highly charged ions. e.g. U91+
linear decelerator
ring decelerator
11.4 MeV/u
Slow, highly charged ions
Stripping at high energy
to provide sufficient collisional energy
Deceleration: Emittance increase
(Ideally: Conservation of normalized norm)
Cooling required
Atomic physics: Ion far away from charge equilibrium
UNILAC
SIS
FRS
ESR
CRYRING@ESR
HITRAP

## Slide 18
Deceleration: Au78+: 145  30  10 MeV/u followed b fast transfer to CRYRING
dipole field strength
high voltage of electron cooler (electron energy)
beam current
electron current (300/100 mA)
   30 10 MeV/u
Achievements:
Optimization of complex beam manipulation
Intensity below 107
Particle loss less than 20 % from 145 to 10 MeV/u
Challenges:
Beam instabilities by large space charge
Lifetime limit by residual gas coll. (p=10-11 mbar)
electron cooling is applied at all three plateaus
28 s
ESR Deceleration Cycle 2022
28 s
beam current

## Slide 19
The low Energy Storage Ring CRYRING
Parameter | Value
Circumference | 54.17 m (ESR/2)
Vacuum pressure | 10-11-10-12 mbar
Ion energy | < 300 keV/u - 14 MeV/u
Rigidity for ions | 0.054 - 1.44 Tm
Magnet ramping | 1 T/s (4 T/s, 7 T/s)
Stand-alone operation | local ion beam (300 keV/u, q/A > 0.25)
Beam injection | multiturn and fast
Beam extraction | slow and fast
17 m
CRYRING: Significant improved ring from University Stockholm
Injection from ESR or local source, acceleration and deceleration, electron cooling
Beam time 2022:
Beams from ESR
Beam from local source
Atomic physics and material investigations
Extracted beams
Talk by Lorenzo Crescimbeni:
Extreme sensitive current measurement

## Slide 20
The FAIR Facility
Future Facility for Anti-proton and Ion Research FAIR:
Brilliant future as Brillance = Beam Current / Emittance
SIS100:
Low charge states e.g. U28+
 factor 10 more ions
High energies e.g. for U92+
Radioactive beam production:
100-fold better trans.& separation
Anti-proton production & cooling
Novel investigation for up to 30 GeV
Fix targets:
Nuclear-, atomic-, plasma-,
bio-physics & & material science

## Slide 21
The FAIR Facility
Future Facility for Anti-proton and Ion Research FAIR:
Brilliant future as Brillance = Beam Current / Emittance
Problems due to sanctions
against Russia
(financial and in-kind)
Significant delays expected
(under considerations….)
2028
2026
approx. 2030
after 2030

## Slide 22
Conclusion:
GSI: One of the most versatile accelerator facilities in the world
Challenging operation with interesting accelerator physics and technologies
FAIR as a ‘natural’ extension in progress
Status May 2022
The FAIR Facility: Present Status
Thank you for your attention! Do you have questions?