## Slide 1
ARES operation meeting, Monday 18th July
by the ARES shift crew

## Slide 2
Summary of KW 28
 | Monday 11th July | Tuesday 12th July | Wednesday 13th July | Thursday 14th July | Friday 15th July
Achievements | * Tunnel open for maintenance day | * Putting ARES back on track (see below) * AA shift: work on quadrupoles misalignment, agent-based beam optimization (centering/focusing), automated beam/quad alignment | * Dispersion measurement along the beamline for dispersion closure in the BC * EAQZM3 readback deviation fixed by MPC * Gun solenoid can cycle again (accuracy adjusted) | * AA shift: Measuring quadrupoles misalignments, testing agent user interface * Position feedback studies on SH.E2 | * Comparison momentum measurement LE dipole vs PCB steerers * Trying a momentum measurement comparison PDE dipole vs PCB steerer * Taking one last point for TWS1 compression curve
Perturbating events | * High voltage event in the power distribution | * DIO.0 cannot be switched on * PHAROS off with errors * Power supply of EAQZM1 needed to be exchanged | - | * Automated beam/quad alignment crashed over lunch | * LI.R3 camera is unstable (crashed several times when using it alone) * Discrepancy ASTRA/experiment for off-crest momentum
Notes | - | - | - | * MEA work brought improvement for quad alignment | * Might look at LI.R1 calibration

## Slide 3
AA shifts

## Slide 4
Dispersion studies

## Slide 5: Discrete horizontal position feedback on SH.E2
Feedback off
Feedback on
GUN_VC: x vs. y (µm) as reference
SH.E2: x vs. y (µm)
SH.E2: x vs. time (px)
PID parameter tuning tool
Measure beam position on screen, correct with upstream steerer
Tried only horizontal direction so far
rms position jitter reduced from 13.88 µm (1.41 px) to 5.48 µm (0.56 px)  factor 2.5 improvement
rms laser position jitter on virtual cathode: 4 µm (7 px)
Using ARDLMCHM2 as actuator (5 minute datasets)

## Slide 6
LE dipole momentum measurement: 3.8513 +/- 0.0002 MeV/c
Slight discrepancy when measuring on LI.R1  Might be worth to check again calibration (when time allows it)
Momentum discrepancy (around 3-2.5 MeV/c at max.) observed between ASTRA predictions and experimental measurements for off-crest settings in TWS (namely anything different from triple on-crest).
Might be due to TWS field incorrect modeling in ASTRA input or not yet understood PDE features  Try to investigate the latter one with comparison PDE/steerer for momentum measurement.
Conclusion not possible because errorbars are of 3-4 MeV/c with the PCB steerer measurement.
Dipole/steerer momentum measurement
 | LI.X1 | LI.R1 | LI.R2
CVG1 | 3.825 +/- 0.050 | 3.915 +/- 0.051 | 3.88 +/- 0.23

## Slide 7: Schedule
Week 29
Date | Shift leader
18.7. | Florian (Tunnel open)
19.7. | Hannes/Willi
20.7. | Willi
21.7. | Hannes
22.7. | Thomas
If you want to learn or join the shift: please give the shift leader a call (BKR 2840 / SINBAD Box 2454)