## Slide 1: Basic-AMC – A Cost-Effective Module for Divertor Bolometer Diagnostics

## Slide 2: What is the „Basic-AMC”
A double-width AMC module with PCI Express x2
Low dependency on special components
A minimal hardware platform for „simple” FPGA designs
RTM support, front-panel GPIO
Easily upgradeable FPGA
MMC and board features customized for your application, e.g.:
  Low-noise power supply for RTM
(and why you
might want it)
http://thedoghousediaries.com/5627

## Slide 3: The Module Overview
User area
System area
Edge connector
LVCMOS I/O
Debug UART over USB

## Slide 4: Hosted FPGA Modules
Feature | Basic-AMC (2020) | Basic-AMC V2 (2022)
FPGA module standard | TRENZ 3x4 (200 pins) | TRENZ 4x5 (260 pins)
Selected module and its features | TE0714 (104 EUR) XC7A50T QSPI FLASH | TE0712 (280 EUR) XC7A100T QSPI FLASH 1 GB DDR Memory SI5338 PLL Ethernet PHY 1-Wire EEPROM
FPGA migration options | Only migration to XC7A35T | 12 alternative modules available

## Slide 5: TRENZ FPGA Modules

## Slide 6: The Divertor Bolometer Use Case

## Slide 7: FPGA Firmware for Divertor Bolometer
PCIe gen.2 x2 (3x DMA)
DDR3 memory interface
4 CORDIC computers
4 arbitrary function generators
16 quadrature modulators
32 FIR filters of 480 taps each
Many diagnostic features
Firmware upgrade

## Slide 8: Basic-AMCv2 now support Firmware Update via IPMI

## Slide 9: Firmware Update Process
Remote PC
MCH
Update over IPMI
Firmware on the AMC board can be updated remotely without any programmer connected to the PC

## Slide 10: HPM.1 Support
Ask for a payloads that can be upgraded
Control of the upgrade process
Firmware activation, test and rollback

## Slide 11: Basic-AMCv2 MMC Memory Structure
Cold Reset
BOOTLOADER
#1 Firmware
(Active)
#2 Firmware
(Empty space)
BOOTLOADER
#1 Firmware
(Active)
#2 Firmware
(Empty space)
Start the application

## Slide 12: MMC Update Process
BOOTLOADER
#1 Firmware
(Active)
#2 Firmware
Storing a new program…
Firmware update request
IPMI
HPM.1
Upload and store new firmware
Remote PC with access to the MCH

## Slide 13: MMC Firmware Compression
LZ77 algorithm was chosen for firmware compression
This yields a
shorter update process
73%

## Slide 14: MMC Update Process
BOOTLOADER
#1 Firmware
(Inactive application)
#2 Firmware
(Currently active application)
BOOTLOADER
#1 Firmware
(Currently active application)
Upload process finished
#2 Firmware
Just received firmware
Switch application and restart

## Slide 15: MMC Firmware Rollback
BOOTLOADER
BOOTLOADER
#1 Firmware
Inactive
Upload process finished
BOOTLOADER
#2 Firmware
Faulty firmware
#1 Firmware
Inactive
#2 Firmware
Faulty firmware
#1 Firmware
Active
#2 Firmware
Faulty firmware

## Slide 16: AMC Payload Firmware Update via HPM.1
Request to update FPGA firmware
MMC
With
HPM.1 support
Program FPGA memory via SPI
Remote PC with access to the MCH
FPGA

## Slide 17: Conclusion
If there's something weird And it don't look good Who you gonna call? (Ghostbusters)
Department of Microelectronics
and Computer Science (DMCS)
+48 42 631 27 20
secretary@dmcs.pl
When in need of platform for:
  Cost-effective RTM carrier
  Unusual data concentrator
  Process control over PCIe
  Timing, event or all-purpose IO
New modules are under design
Contact us
We will customize the Basic-AMC for you
Lodz
University
of
Technology