## Slide 1: DESY MMC Solutions
New Features and more Modularity for an optimal AMC Management
Sven Stubbe, Patrick Huesmann, Carsten Dülsen
Hamburg, 8th December, 2022

## Slide 2: DESY MMC Solutions
Overview
MMC Mailbox
Implementation in MMC Firmware
Implementation in SoC Firmware
UART Forwarding to IPMB-L
Conclusion
New Features and more Modularity for an optimal AMC Management

## Slide 3
Overview
Management in MicroTCA
System perspective
  MicroTCA Carrier Management Controller (MCMC)
  Enhanced Module Management Controllers (eMMCs)
    (interfaced via IPMB-0: IPMB-A, IPMB-B)
  Module Management Controller (MMC) (interfaced via IPMB-L)
AMC perspective
  IPMI parsing / message generation
  Provide FRU information
  Event handling: sensors, thresholds, alerts
  RTM control
  Payload management (e.g. FPGAs/SoCs, FMCs)
DMMC-STAMP: drop-in solution for AMC MMC
  Manufactured and provided by DESY
DMMC-STAMP System on a Module

## Slide 4
Overview
DESY MMC Solutions
DMMC-STAMP SoM
  Pre-programmed firmware
  Tiny: 25.5 x 29.5 x 2.3 mm
DMMC-SDK
  MMC firmware customization
  DESY MMC Software Library
  Example implementations (e.g. DAMC-FMC2ZUP)
Open Source Tools and Templates
  AMC and RTM Altium Designer Templates
  mmcterm: serial over IPMB
  bin2hpm: convert bitfiles for IPMI upgrade
  frugy: generating FRUs
  IPMI tools (e.g. in-system firmware update)
DMMC-STAMP
DMMC-STAMP-BoB
DMMC-SDK
Altium Design Templates (incl. DMMC-STAMP)
Useful tools on GitHub

## Slide 5
Overview
DMMC-STAMP System on a Module
RTM
MCU GPIO
CPLD GPIO
FPGA1
FPGA2
FMC
Programmable building blocks:
  ARM Microcontroller
  Lattice CPLD
Features for payload SoC interfacing by using customized firmware

## Slide 6
MMC Mailbox
Information Exchange between SoC OS and MMC
Communication channel between AMC Management and SoC Processing System (Application)
  Monitor system health information
  Use on-board sensor data in application (e.g. for ADC/DAC calibration)
  Use DMMC-STAMP unique ID as MAC address
  Use connected FRU data in application
  Application shutdown before turning off the payload power
  User specific functionality
  {…}
Additional Communication

## Slide 7
MMC Mailbox
Implementation on DMMC-STAMP Side
Introduce 2-KB CPLD BRAM as „MMC Mailbox“
  Access from MCU via SPI register space
  Access from SoC via I2C
  Defined register space
EEPROM Emulation
  Interface the CPLD BRAM
  Emulate a Microchip 24C02 EEPROM
Define a locking mechanism to avoid a competing register access
  Registerflag
Add software functionality to DMMC-STAMP MCU
  Continuous upgrade of mmc information to mailbox
  Handling of payload shutdown sequence

## Slide 8
MMC Mailbox
Implementation on SoC Side
Add I2C master to PL BSP section
Modify device tree to support the „mmcmailbox“ driver
Add mailbox driver and mailbox software to meta-techlab-bsp layer
  Read MMC information from mailbox on request
  Provide high-level API to be interfaced by user application
  Poll mailbox register to get noticed about a Hot-Swap handle event

## Slide 9
MMC Mailbox
Memory Layout

## Slide 10
MMC Mailbox
Embedded Linux Shutdown Sequence
see talk by Patrick Huesmann today, 12:00 am
,

## Slide 11
UART Forwarding to IPMB-L
Remote Access of the PS
Improve UART multiplexing to remote access the PS by using mmcterm
  System recovery in case of failure (e.g. network issues and ssh does not work anymore)
  No need for USB cables anymore

## Slide 12
UART Forwarding to IPMB-L
SoC PS implementation
Use Cases
  Remote Access
  System Recovery

## Slide 13
Conclusion
New Features and more Modularity
Mailbox feature for communication between MMC and SoC
  Deploy (critical) system information
  Graceful shutdown of Linux OS
  Application specific need
PS UART forwarding to IPMB-L
  Additional PS access channel (next to Ethernet and USB)
  Very useful for remote access in case of a system failure
Modular firmware/software implementation
  Library based approach
  Fully integrated with the DMMC-SDK
  Clear separation to custom application part

## Slide 14: Thank You!
Deutsches Elektronen-Synchrotron DESY
MicroTCA Technology Lab
Notkestraße 85
22607 Hamburg
Sven Stubbe
Head of MicroTCA Technology Lab
+49 (0)40 8998-1870
sven.stubbe@desy.de