## Slide 1: ARES Operation Meeting
Summary of week 31 / 2022
Willi Kuropka, on behalf of the ARES crew

## Slide 2: Summary of week 31
 | Mon. 01.08. | Tue. 02.08. | Wed. 03.08. | Thu. 04.08. | Fri. 05.08.
Achievements | STRIDENAS test Adjusting FL section screen station | Optimizing dispersion measurements BC commissioning | Dispersion measurements Wire scanner quad scan BC collimator commissioning | AutoAcc shift STRIDENAS beam test | Wire scanner quad scan STRIDENAS beam test
Difficulties |  |  |  |  | Network issues with a number of doocs servers not reachable – solved by MCS

## Slide 3: Dispersion measurement along ARES
BC fits ASTRA model well, so far

## Slide 4: BC shape collimator
All apertures are within reach of the mover, when beam centered on BC.E1
600um,400um,200um slit shapes
Mover steps vs. transmission

## Slide 5: Wire scanner quad scan
preliminary results!
Normalized Emittance = ( 30.351885923301104 pm 5.247839472533824 ) nm
Normalized Emittance = ( 35.07576484833951 pm 14.634820132716161 ) nm

## Slide 6: Stridenas beam profile measurements
~70 fC
~150 fC

## Slide 7: Plan for the week
Today: Tunnel door at 25d gets door closing mechanism, maybe FL section wire scanner replacement
More wire scanner quad scans
Bunch compressor commissioning
STRIDENAS beam test

## Slide 8: Schedule
Week 32
If you want to learn or join the shift: please give the shift leader a call (BKR 2840 / SINBAD Box 2454)
Date | Shift Leader
08.08. | Tunnel open
09.08. | Hannes
10.08 | Willi
11.08. | Hannes
12.08. | Willi
13.08. | 
14.08. |