## Slide 1
PALMIERI Innovative aPproAches in technoLogy and beaM dynamIcs for futurE RecIrculating SRF accelerators
Status of PALMIERI:
Test small Nb3Sn and NbTiN systems for existing cavities here: Nb3Sn and NbTiN HOM antennas for MESA cavities

## Slide 2
MESA Enhanced ELBE-type Cryomodules
Cryomodule (2 XFEL Cavities @ 12.5 MV/m)
LHe/LN2 supply box
MCTL (LHe, GHe, LN2)
Concern: Heating of the HOM-Antenna
Changes:
Sapphire windows at HOM feedthrough
Strip line in HOM cable for cooling

## Slide 3
MESA Enhanced ELBE-type Cryomodules
Only 1.25 W
heat deposition in
1.8 K LHe bath
per HOM coupler
in cryo budget
1.8
11.4
T / K
Picture: T. Stengler
Thermal calculations at HOM antenna:
  → Provide optimised thermal connection design to RI
  → Limitation by heat input from cable, need for heat sink

## Slide 4
Simulation for MESA HOM Coupler
HOM antenna coating with
 Better HOM damping and higher
1.8 K
11.4 K
Power stored in HOMs:
N: #beams; q: bunch charge; k: loss factor;
I: average beam current
30% of outcoupled by HOM feedthrough
100 mW load
I [mA] | q [pC] | [mW] | [mW]
1 | 7.7 | 30.8 | 10
10 | 77 | 3080 | 1000
I [mA] | q [pC] |  | 
1 | 7.7 | 30.8 | 10
10 | 77 | 3080 | 1000
Picture: T. Stengler

## Slide 5
Goal for HOM Couplers
Goal:
Prevent quench of whole CM
How:
Antenna coating with Nb3SN and NbTiN
on Nb/Cu Antennas
Property | Nb | Nb3Sn
[K] | 9.2 | 18.3
(0K) | 1.4 | 34
[nm] | 39 | 5.7
[nm] | 27 | 65-89
Property | Nb | Nb3Sn
 | 9.2 | 18.3
 | 1.4 | 34
 | 39 | 5.7
 | 27 | 65-89
1.8 K
11.4 K
100 mW load
Picture: T. Stengler

## Slide 6
Goal for HOM Couplers
Coated
Antennas
Current HOM Antennas fulfil ERL at 1 mA
10 mA need enhanced HOM feedthrough
Ongoing CST Simulation
(Help from W. Ackermann from TEMF)
Beam current
[mA]
1
10
DESY

## Slide 7
Refurbishment of ALICE module
MESA Enhanced ELBE-type Cryomodules (MEEC):
Helium port (Joule-Thomson valve)
Faster DESY/Saclay tuner (higher beam currents)
 diameter of Helium tank changed
“New” HOM antennas
Cavity contamination leads to field emission @7 MV/m
 Clean room treatment!
Delayed through long maintenance of the HPR this summer

## Slide 8
HOM Feedthroughts
Design from RI (left)
Cyocera feedthrough with flange and antenna tip
25 mm tip length
Bakeout at max 300C
DESY Design (right)
29.56 mm tip length

## Slide 9
Timeline
 behind schedule: first cold test planned spring 2023
cold test with coated antennes end of 2023

## Slide 10
Outlook
Production of the first OFHC antennas
Studies of a bakeout at 400C/600C in HH
HPR treatment in March
First cold test in April
First cold test with coated antennas end of 2023