## Slide 1
Towards a
portable & standalone
DAQ for MIMOSIS
Oliver Keller (FAIR)
GSI Detector Lab
o.keller@gsi.de
9.02.2023

## Slide 2
Status Quo: Readout System from IPHC
National Instruments PXIe crate
    NI FlexRio FPGA module PXIe-7975/PXIe-7962
    NI 6587: 20 x 1 Gbit/s I/O channels (LVDS)
Data taking divided in acquisitions
    about 10-30 k frames until RAM buffer full
    then data written to disk
    dead time in between acquisitions
    additional trigger channel for scintillator
Two main variants
    Lab setup for single chip characterization
    Test beam setup for 6 MIMOSIS chips in telescope configuration
Dedicated software drivers & GUI in C++/LabView for Windows
    Developed by IPHC team: G. Claus, M. Goffe, K. Jaaskelainen, M. Specht

## Slide 3
Status Quo: Readout System from IPHC
Lab setup
Test beam setup
M. Goffe/G. Claus

## Slide 4
For SEE testing at GSI Micro-Beam, June 2022
Raspberry Pi 4
    main remote controller
    I2C slow control master
ULX3S board
  Lattice ECP5 FPGA:
    22 LVDS I/O pairs up to 400 MHz
    up to 5 Gbit/s SerDes (5G version)
  provides to MIMOSIS-1:
    40 & 320 MHz clocks
    slow control sync
  various debug & monitoring capabilities
Python library for slow control:
  github.com/ozel/Mimosis1-slow-control
First DAQ prototype at GSI
Raspberry
Pi 4
ULX3S FPGA & custom MIMOSIS
adapter boards
MIMOSIS chipboard IPHC

## Slide 5
Readout of 1-2 MIMOSIS chips per FPGA board at 2.5 Gbit/s Ethernet
    MIMOSIS output: 320 Mbit/s on either 1, 2, 4 or 8 channels in parallel
    Either 1 MIMOSIS at full speed or 2 at reduced channel count
    Current MIMOSIS 6-plane telescope: 2 channels per chip/plane
Ethernet I/O: Pixel data and slow control via UDP/Etherbone
    1 Gbit/s Ethernet for reduced data rate (max. 2 channels)
    2.5G Ethernet becoming consumer mainstream, new sweet spot
    frame buffering and data reduction/filtering requires additional RAM
Implementation using LiteX open FPGA cores: https://github.com/enjoy-digital/litex
    IP/UDP stack, 1-10G Ethernet, DDR RAM controller, debugging infrastructure etc.
Portable MIMOSIS DAQ - Features

## Slide 6
Current ULX3S-based prototype (~150 EUR)
    Ok for developing the basics
    100 Mbit/s Ethernet added via Pmod module
    good enough for S-curve scans
    rare but persistent signal integrity problems on certain differential input lines @160 MHz
Next step: Butterstick board (~300 EUR)
    on-board 256 MB DDR3 RAM and 1Gbit/s Ethernet
    3 extension connectors: SYZYGY standard (‘Zmod’)
      30 diff. I/O pairs (incl. 4 SERDES channels)
      34 single ended I/Os
      dual SFP+ module for multi-gigabit Ethernet
Re-use new MIMOSIS-1 chipboard from GU-IKF
    based on FPC cables
    if possible: rearrange FPC pinout in 2nd revision
Portable MIMOSIS DAQ - FPGA Hardware

## Slide 7
Encapsulating output of one MIMOSIS in 1-2.5G Ethernet data stream
    can be directly received on a modern PC
    keep software/operational requirements and dependencies as low as possible
Continuous recording of full pixel data streams from several MIMOSIS
    telescope use case: 6 planes x 8 x 320 Mbits/ ~ 15.4 Gbit/s
    fits well within 40 Gbit/s Ethernet
    40G Ethernet card + switch: ~3 kEUR
High-Speed Ethernet data recording
    Linux PF_RING kernel driver with modern Intel systems
    allows continuous Ethernet packet dump
      direct data copy to disk, no dead time
    system requirements:
      Intel 10G/40G/100G Ethernet card
      Intel Xeon CPU (> 2.5 GHz)
      recent SSD disk (typically ~30 Gbit/s write speeds)
Portable MIMOSIS DAQ - Data Backbone
Ethernet Switch
6 x 2.5G
1 x 40G

## Slide 8
stack of 2 MIMOSIS IKF chipboards via SYZYGY extensions on Butterstick FPGA board
focus on high speed pixel recording as opposed to chip testing & debugging
  skip most of proximity board’s circuitry
use start/sync feature of MIMOSIS-2 for synchronized data recording
include sync connector for telescope trigger and logic unit (AIDA TLU)
three of these setups from a 6-plane telescope
FPCs provide spatial flexibility, e.g. side-by-side:
Towards a compact dual layer stack readout
FPC cables

## Slide 9
Python scripts for now
  good enough/efficient for chip testing/waver probing
  autonomous, scripted s-curve scans? => IKF
Corryvreckan
  attractive telescope analysis software with large community
  allows flexible merging across frame time boundary
  supports heterogeneous telescopes composed of various chips
  dedicated module for analysis of MIMOSIS data:
    https://gitlab.cern.ch/okeller/corryvreckan/-/wikis/home
  Online monitor reads live data while recoding to disk
    => testing/debugging!
Dedicated interactive GUI required at some point
  Jupyter/Bokeh good candidates
Portable MIMOSIS DAQ - Software

## Slide 10
Current main use cases of MIMOSIS DAQs:
    chip testing & evaluation in beam telescope => IPHC DAQ
    chip testing & wafer probing for CBM-MVD production => IKF DAQ
    gather experience for mCBM & CBM DAQ, test with GBTx
EURIZON user interests:
    integration in EuDET telescope @DESY
    V. Pugatch research on ion beam dose
    MIMOSIS neutron detector
Pixel hit rate requirements?
    full MIMOSIS data rate required?
How many MIMOSIS chips at once?
Spatial chip arrangements?
o.keller@gsi.de
MIMOSIS DAQ Outlook
M. Mager