## Slide 1
WP2.1: Preparation of the Silicon Tracking System for CBM/FAIR
[FAIR, EKUT], Task Leader: [Johann Heuser, FAIR/GSI]
WP2.2: Developments for the data acquisition chain, for data
preprocessing and computing for mCBM and CBM at
FAIR [WUT, FAIR], Task Leader: [Wojciech Zabolotny, WUT]
WP2.3: Development of software packages for simulation and
data analysis, participation in physics performance
studies for CBM experiment at FAIR [FAIR, Wigner RCP]
Task Leader: [Ilya Selyuzhenkov, FAIR/GSI]
WP2.4: Development and construction of beam monitors, target
chamber and beam pipe for the CBM experiment at FAIR
[FAIR, NPI CAS] Task Leader: [Peter Senger, FAIR/GSI]
WP2.5: Development of new PSD detector for CBM [NPI CAS]
Task Leader: [Andrej Kugler, NPI CAS]
Participants: FAIR, WUT, Wigner RCP, NPI CAS, EKUT
WP2 Heavy Ions
Instrumentation for the CBM experiment at ESFRI landmark FAIR

## Slide 2: Silicon Tracking System (STS) for CBM/FAIR
STS = main CBM detector for charged-particle trajectory measurement
installed in dipole magnet’s gap
thousands of high-tech components
STS
target
beam pipe
2.5
25
MVD
STS
beam
WP2.1
The CBM experiment
J. Heuser for the STS group

## Slide 3: New dipole magnet – improved STS
dipole magnet under construction 2022 in Russia – not available any more
unavailability of the original dipole magnet requires new acquisition effort (tender ongoing)
this opens opportunity for geometrical changes:
  larger magnet gap
  to fit a somewhat enlarged STS detector
    with enhanced modular integration
    and upgrade perspectives
Highlights from WP2.1 efforts:
New modular STS has been developed
Physics performance simulations are being done
Pre-series STS module assembly has been achieved
WP2.1

## Slide 4: New modular STS
Old “monolithic” STS:
monolithic construction
once assembled no access
maintenance, replacement, upgrade only by full disassembly
very tight space constraints
New “modular” concept:
modular setup
units U00 – U03 can be moved separately from the rest U04 – U07
additional rail system
completely independent systems
Internal designs are kept!
Unit/station layout and all detector and module designs remain the same.
Outer frames and cabling are adapted.
Overall space requirements change:
  height + 3 cm
  width + 30 cm
  expressed in the new magnet specifications gap: 2000 x 3300 x 1470 mm l/w/h
2820 mm
1425 mm
1219 mm
1219 mm
3214 mm
1450 mm
WP2.1

## Slide 5: Modular STS – performance simulation studies
new dipole magnet:
field maps prepared by CBM Collaboration
enlarged gap
simulation geometry
physics performance remains high!
primary particles, B = 0.5 T
primary particles, B = 1 T
momentum resolution
efficiency [%]
p/p [%]
efficiency [%]
p [GeV/c]
p [GeV/c]
p [GeV/c]
WP2.1

## Slide 6
Pre-series production of STS modules
Pre-series assembly of STS modules has been achieved:
10 modules assembled:
test results during module assembly in clean room:
    all in specs, (<< 3% missing channels, noise ~ 1000 e)
mounting on ladder structures ongoing
Application from 2023 in J-PARC E16 experiment (Japan) for its upgrade with a silicon tracking layer
 New WP2.1 MS7 Production Readiness (M36): will be reached
 New WP2.1 D2.2 System engineered (M48): will be reached
equivalent noise charge [e]
channel number
WP2.1

## Slide 7: Development of the GERI+GBTxEMU based readout chain
Status in 2022
  Cooperation with JINR group stopped after February 24th
  Only WUT staff left involved in firmware development (Marek Gumiński and Piotr Miedzik as the project’s staff, Michał Kruszewski, Krzysztof Poźniak and Wojciech Zabołotny as volunteers)
  Tests planned in JINR in April 2022 were impossible. Development tasks related to application in BM@N experiment were suspended (abandoned in fact?)
  The package was reoriented for preparation of GERI+GBTxEMU based readout chain for mCBM, CBM and other experiments cooperating with FAIR
  GBTxEMU part completed (only maintenance, functionality adjustment, bug corrections needed)
Developments for the data acquisition chain, for data preprocessing and computing for mCBM and CBM at FAIR
WP2.2
W. Zabołotny, M. Gumiński, P. Loizeau WUT, FAIR

## Slide 8: Structure and status of the GERI firmware
WP2.2

## Slide 9: GBT-FPGA
Serial communication interface developed for HEP readout chips https://gitlab.cern.ch/gbt-fpga
FEC encoding and latency determinism for FEB control
Synchronisation of FE boards
Up to 4.8 Gbps throughput for experiment data readout
WP2.2

## Slide 10: Versatile DMA engine
Core part implemented in HLS
Compatible with PCIe-connected FPGAs and AXI-based MPSoCs
Efficient memory management even in standard Linux. Starting and stopping acquisition in multiple boards without rebooting.
Full utilization of multiple cores in host machine
Described in a paper accepted for publication, preprint available at https://www.preprints.org/manuscript/202301.0328
The design is open-source and available at https://gitlab.com/WZabISE/hls_dma
WP2.2

## Slide 11: Efficient data concentrator
Solves the problem of efficient high-speed data concentration from multiple low-width words to a single high-width word required by the DMA system.
Optimal in a sense that does not require high-speed local clock, and ensures that the “holes” are eliminated from the output stream even if they present in the input streams.
Design based on so-called Beneš network (technology from 60’s but applied to the new problem).
Efficient implementation in FPGA.
Paper describing the solution is in preparation.
The design will be open-sourced after the publication.
WP2.2
New Deliverable: D2.4 “Functional tests of the developed readout solution” (report at M48)

## Slide 12
Development of common software packages for simulation and data analysis, participation in physics performance studies of the CBM & mCBM experiments at GSI/FAIR
Ilya Selyuzhenkov, FAIR/GSI [GSI/FAIR, Wigner RCP]
mCBM data taking started in 2019
CBM operation planned for > 2028
WP2.3

## Slide 13: Scientific/technical highlights - I
Goal: Make readout chain „online ready“
Implement „algo“ classes in cbm::algo namespace.
Smallest (algorithmically) possible detector unit (parallelizable).
ROOT-free, optimize for speed, separate monitoring.
Online software for CBM
Unpacking:
Translate detector messages to universal format.
In cbm::algo: One unpacker per timeslice component.
Completed: STS, MUCH, TOF, Tzero
Ongoing: TRD
Triggering:
„Time cluster trigger“ algorithm in cbm::algo.
Shift „sliding window“ through digi stream.
Trigger when digi count exceeds threshold.
Dominik Smith, Volker Friese
WP2.3

## Slide 14: Scientific/technical highlights - II
Monte-Carlo studies for new CBM Forward detector
Spectator fragments detection for beam momenta pbeam = 3.3−12 AGeV/c
Operation at beam intensities up to 10^9 Au ions per second
Reaction plane determination with an accuracy better than 40 degree
Determination of collision centrality classes with an accuracy better than 10%
Simulations
DCM-QGSM-SMM model with fragments
Geant4
Operational background from Beam paprticles and detector materials (beam pipe, etc)
Lukas Chlad, Ilya Selyuzhenkov
WP2.3

## Slide 15: Scientific/technical highlights - III
Hypernuclei production in 0-10% central Au+Au collisions
ΛN interaction strength from measurements
ΛΛ interaction strength estimated from:
    ΛΛ=ΛN
    ΛN=k*ΛN , k<1
The energy dependence and expected yields
are comparable with other calculations
Gábor Balassa & György Wolf [WUT]
WP2.3
The deliverables remain unchanged
D2.5 Simulation results for selected observables - Month 24 (achieved)
D2.6 Physics performance for major observables - Month 48

## Slide 16: WP2.4: Beam detectors and beam pipe for CBM Peter Senger, FAIR/GSI
Applications and requirements:
Measure start time of reaction (T0) with precision of 50 ps (RMS) at beam intensities up to 10⁷ ions/s
Beam quality monitoring: position (< 50 μm resolution), halo, time structure, …
Part of fast beam abort system
Low material budget and in-vacuum operation
T0 and HaloBAS detector stations will employ pcCVD diamond technology
Detector stations installed in vacuum, in front of the CBM target
Conceptual design report: Ready in Q3 2023
T0 and beam detectors for CBM A. Rost FAIR

## Slide 17: Sensor technologies
Diamond for heavy ions
Profit from a long experience with HADES:
High purity sc/pcCVD material,
Radiation damage well known
Low Gain Avalanche Diode technology for MIPs
Profit from R&D for HADES, S-DALINAC and Medical application:
New sensor technology
Successfully used as T0 in HADES production beam-time
HADES LGAD sensor (FBK) 2 cm x 2 cm, 96 ch, 50 μm thick
pcCVD diamond sensor: 10 mm x 10 mm x 80 μm, 16 stripes (300 μm) on each side
WP2.4
Pro: Radiation hard
Cons: small samples, price
Pro: large sample, price
Cons: radiation hardness
A. Rost FAIR

## Slide 18: T0 detector demonstrator
T0 diamond interface PCB with pneumatic drive
New 10 mm x 10 mm x 80 μm
16-channels pcCVD diamond sensor
T0 demonstrator used in mCBM beam-times in summer 2022
Readout-system based on PADIX discriminator and GET4 TDC
Used for online beam monitoring during the beam-time
→ Beam-time data is currently being analyzed
Next steps:
Preparation of 16+16 ch. (both side read-out) pcCVD T0 demonstrator for the upcoming mCBM campaigns 2023/2024
Preproduction of the CBM HaloBAS + T0 stations and test with α-source in the laboratory
WP2.4
A. Rost FAIR

## Slide 19
19
STS section
RICH / MUCH section
Downstream section
Downstream section
Variable position of PSD
TRD
Variable position of TOF
B.M.
Target chamber
Acceptance window
O-Ring groove
Design of the STS team (Johann M. Heuser, et al.)
Beam pipe for CBM: Components
WP2.4
J. Kollarczyk
A. Kugler
A. Senger FAIR

## Slide 20
20
STS section
RICH / MUCH section
Downstream section
0
Downstream beam pipe with deflection:
Centre of rotation
2,5°
Zero deflection
Extreme deflection
1,24°
Turn by 180°
Change of polarity
Deflection in the range of <0°; 2.5°> in a single polarity
B.M.
1,26°
Beam pipe for CBM: Bending concept
WP2.4
J. Kollarczyk
A. Kugler
A. Senger FAIR

## Slide 21
21
Downstream beam pipe with bending mechanism:
Latest approach
Need of further research
Beam pipe for CBM: Bending mechanism
WP2.4
J. Kollarczyk
A. Kugler

## Slide 22
22
Cylindrical downstream beam pipe:
Stability demonstration
Vacuum conditions
Thickness = 3 mm
Length = 3 350 mm
Strain measurements
Inner vacuum: 10-5 mbar
Beam pipe for CBM: Prototype tests
WP2.4

## Slide 23: Implementation of beam pipe design into simulation environment
Petr Chudoba, Eoin Clerkin
Delivered:
An extenisve simulation beampipe geometry solution capable of handling beam energies from 3 → 12 AGeV and ranges through the entire length of the CBM detector subsystem, consisting of the following pseudo-independent but integrated parts:
  Downstream cylinderical section
  Bellow assembly mechanism
  Conical RICH/MUCH section
  STS backwall flange
  Toroidial beam window and upstream section.
  Target/MVD chamber.
Isolated beampipe geometry
Integrated with other CBM subsystems
WP2.4
Milestones and deliverables:
M10: Technical design of beam monitors, target chamber and beam pipe for CBM: Month 36
D2.7: Design of beam monitors, target chambers and beam pipes: Month 12 (achieved)
D2.8: Beam monitors, target chamber and beam pipe for CBM constructed: Month 48

## Slide 24: Software integration - Geometry
aims to be flexible to fit all requirements put on the FWall
starting with 3 sizes of cells
for study purposes use very fine granularity (1x1 cm2) without any hole
  this will be used to set minimum criteria on final design to meet the reaction plane resolution
  also with this setup we can determine what size of hole might be optimal in order to not lose the heavy fragments (keeping in mind also limits coming from irradiation of the material)
WP2.5:
Development of new PSD detector for CBM
L. Chlad
A. Kugler

## Slide 25: Software integration - simulation chain
TRANSPORT using Geant engines - store information of energy loss
of charged tracks within active material (scintillator)
DIGITIZATION before we will know outcome of material study with Geant 4 physics list and test beamtimes only simple summing of energy deposition within cell is possible
HIT RECONSTRUCTION for now ideal case is used = copy digi level
WP2.5
L. Chlad
A. Kugler

## Slide 26: Hardware status
plastic scintillators for testing to be obtained from Nuvia company
preparation of read-out electronics based on RICH read-out (TRB5sc + DiRich concentrator boards)
SiPMs main criteria is time resolution + radiation hardness (review of recent progress in the field is ongoing)
WP2.5
L. Chlad
A. Kugler
New Deliverable D2.10: Feasibility studies of new projectile spectator detector for CBM: Month 36
New Deliverable D2.11: Technical design of new projectile spectator detector for CBM: Month 48.