## Slide 1: FLARE 1st Project Meeting: Laser Heater and Results from recent beamtimes
Christopher Gerth,
21.02.2023, DESY Hamburg

## Slide 2
FELs at DESY
Time
3.4 km
17.5 GeV
2.5 GeV
600 MeV
130 MeV
SASE1 / SASE2
0.05 – 0.4 nm
SASE3
0.4 – 4 nm
FLASH1 / FLASH2
4 – 60 nm
SC-linac
PETRA3
FLASH
European XFEL

## Slide 3
Why Laser Heater: Micro-bunching Instability
Spectrum shows peak around 5 - 10 um.
TDS time resolution
Fourier Transforms to wavelengths
Gun solenoid IS = -320A σt = 168±3 fs
Gun solenoid IS = -315A σt = 167±4 fs
Long. Phase Space with TDS
PhD Minjie Yan
Random charge density modulations at the gun can be amplified => during bunch compression => due to longitudinal space charge
This micro-bunching instability can drastically degrade the lasing process => SASE but especially external seeding processes
Current Profiles
Micro-bunching

## Slide 4
100
Factor of microbunching gain
Microbunching Instability at FLASH: Proposal and Simulations
Simulations:
Charge Q = 250 pC, peak current at gun I0 = 15 A,
Compression C = 70, final peak current If = 1000A
O.2 – 1 mm
10 – 20 keV
…
How to cure the microbunching instability:
2003
2021

## Slide 5
LH Undulator
Screen
Screen
LH Chicane
Laser
D4
D3
D2
D1
Laser Diagnostics
D4
D3
D2
D1
BC1 Chicane
Laser Heater
FLASH Shutdown 2021/2022 – Installation of the Laser Heater

## Slide 6
Laser Heater Installation: LH Laser Beamline
FLASH2020+ LH laser beamline:
Use relay-imaging (2 lenses) => better pointing stability => TEM stabilisation system
DN100 for easier transport (compared to XFEL) => relaxes steering through beamline
FLASH
Injector
LH table
LH undulator

## Slide 7
7. Outlook <= Slide from kick-off Meeting
A) LH commissioning shifts
Before 25.10.
  Transport through LH Laser beamline with TEM mirror system to In-coupling Table ✅
  Commission Laser Safety system ✅
  Prepare DOOCS servers and panels for LH Laser and equipment on In- and Out-coupling Stations ✅
One shift 25.10. (access to tunnel): prepare spatial overlap e-beam & LH laser beam
  Transport LH laser from In-coupling table to Out-coupling Station
  Commission equipment (diagnostics, motors, etc.) on In- and Out-coupling Stations
  Adjust OTR stations OTR4/5LAHE to see LH laser on CHROMOX screens (MDI required)
Two shifts 25.11. and 27.11.: Achieve temporal overlap e-beam & LH laser beam
  Adjust coarse timing with PD with LH laser pulse and LH Undulator radiation
  Achieve temporal overlap by employing various diagnostics (OTR, BCM signal, PolariX)
  Measurement of induced energy spread vs. LH laser peak power
  Study stability and reproducibility of temporal overlap

## Slide 8
Laser Heater Installation: In- and Out Coupling Tables (25.10.22)
LH Laser
Out-Coupling
ca. 90 x 90 cm2
LH Undulator
LH Laser In-Coupling
180 x 90 cm2
3.2 m
LH Laser Beamline
Tunnel wall
OTR5
OTR4
LH Chicane
D1
D2
D3
D4
V4
H4
V5
H5
Q5
D1
D2
Vacuum chamber height only 8 mm!!!

## Slide 9
7. Outlook <= Slide from kick-off Meeting
A) LH commissioning shifts
Before 25.10.
  Transport LH Laser through beamline with TEM mirror system to In-coupling Station ✅
  Commission Laser Safety system ✅
  Prepare DOOCS servers and panels for LH Laser and equipment on In- and Out-coupling Stations ✅
One shift 25.10. (access to tunnel): prepare spatial overlap e-beam & LH laser beam ✅
  Transport LH laser from In-coupling table to Out-coupling Station ✅
  Commission equipment (diagnostics, motors, etc.) on In- and Out-coupling Stations ✅
  Adjust OTR stations OTR4/5LAHE to see LH laser on CHROMOX screens (MDI required) ✅
Two shifts 25.11. and 27.11.: Achieve spatial and temporal overlap e-beam & LH laser beam
  Adjust coarse timing with PD with LH laser pulse and LH Undulator radiation
  Achieve temporal overlap by employing various diagnostics (OTR, BCM signal, PolariX)
  Measurement of induced energy spread vs. LH laser peak power
  Study stability and reproducibility of temporal overlap

## Slide 10
Laser Heater Commissioning (Nov. 2022)
LH Diagnostics: Instrumentation
Spatial Overlap: Beam size/position of LH laser and e-beam => OTRs LAHE
Temporal Overlap: Coarse (~ns) and fine timing (~ps) of LH Laser and e-beam
  Induced energy spread in a dispersive section => OTR in BC1
OTR
OTR
LHU
OTR in BC1
OTRs LAHE
LH chicane had to be switched on and LH undulator to be closed
=> Beam mismatch => No transmission through the machine

## Slide 11
LH Chicane Commissioning
e-beam
Magnets: Four TCA-40 Steerers (in MEA storage)
Need geodetic and magnetic measurements (MEA)
4 separate PS to correct B-field variations
1st dipole and Mirror Mover in MPS to protect the mirror
Nom. beam axis
Dipole magnet
TCA-40,
offset = 30 mm
34
30
23
35
17
12
17
Chicane offset
Laser Beam
Top view
TCA-40
Dipole magnet
Beam in Nov. 2022

## Slide 12
Spatial Overlap: OTR Stations with Chromox Screens
LH Laser
Out-Coupling
ca. 90 x 90 cm2
LH Undulator
OTR5
OTR4
LH In-Coupling Chicane
D1
D2
D3
D4
V4
H4
V5
H5
Q5
D1
D2
BPM5
BLM4.U
BLM5
e-beam
e-beam
LH laser
LH laser
Nominal
e-beam rms ~ 0.3 mm
Nov. 2022:
e-beam rms ~ 0.5 mm
LH Laser rms ~ 0.6 mm
Jan. 2023:
LH chicane in operation
Correction of LH chicane
Re-matching of e-beam
e-beam rms ~ 0.1 mm
LH Laser rms ~ 0.6 mm
LH laser beam expander for adjustment of spot size not in operation yet
Requires more experience

## Slide 13
Laser Heater Commissioning
Temporal Overlap: Fine timing (~ps) of LH Laser with
  Induced energy spread in a dispersive section => OTR in FL0CBC1
LHU
OTR in BC1
e-beam width
Optimized beam for minimum beam width:
Accelerator settings
Focusing with Quadrupol
time
e-beam rms width
Increased energy spread = Temporal overlap
First heating of e-beam: 25/11/22 at 23:58

## Slide 14
Gap Scan at OTR FL0CBC1 – Jan 2023
Data from scantool: Gaussian fit to horizontal beam profile
Detuning between the LH undulator resonance wavelength and LH laser wavelength
=> “free parameter” is the e-beam energy: 140.7 MeV compared to 143 MeV (or ~ +0.4 mm gap)

## Slide 15
Gap Scan at OTR FL0CBC1 – Nov 2022
Data from Nov 2022 unscaled

## Slide 16
Gap Scan at OTR FL0CBC1 – Nov 2022
Data from Nov 2002 divided by 1.6
=> Heating with high LH laser power is not Gaussian

## Slide 17
Laser Heater Commissioning: Jan 2023 (2 shifts)
LH Diagnostics: Modelling
Temporal Overlap: LH Laser and e-beam
  Induced energy spread in a dispersive section => OTR in BC1 => Results by Dmitrii
  Measurement of integrated radiation intensity => photodetector in NIR (1–5 μm) at 28g => next slides
  Transverse Deflecting Structures
    Induced Slice energy spread with TDS in a dispersive section => LOLA or PolariX
    Measurement of MBI structures => LOLA / PolariX => next slide and results by Philipp
LOLA
PolariX
28g
OTR in BC1

## Slide 18: LH Commissioning
MBI studies with LOLA and PolariX
LOLA
LH off
Strong MBI
LH low intensity
MBI washed out
LH full intensity
e-beam „blown up“
PolariX
FEL lasing
Bunch „optimized“ for MBI
MBI: micro-bunching instability  unwanted bunching
More results of MBI study by Philipp Amstutz …
LOLA
Non-Gaussian
heating

## Slide 19
InGaAS Detector
28g
1) Machine Setup for Seeding bunches
Timing Scan
2) Compression scan

## Slide 20
LH Commissioning: Effect on FEL process
1) LH full intensity: e-beam „blown up“ => SASE destroyed
Timing Scan
No overlap
overlap
2) Optimize LH laser power for FEL

## Slide 21
Backup Slides

## Slide 22
LCLS
2004: Design: https://journals.aps.org/prab/abstract/10.1103/PhysRevSTAB.7.074401
2010: Commissioning: https://journals.aps.org/prab/abstract/10.1103/PhysRevSTAB.13.020703
FERMI@Elettra
2014: Commissioning: https://journals.aps.org/prab/abstract/10.1103/PhysRevSTAB.17.120705
PAL-XFEL
2017: Commissioning: https://www.sciencedirect.com/science/article/pii/S0168900216311214
LCLS
FERMI
PAL-XFEL
LH undulator in a small chicane (easy for in- and out-coupling of the LH laser beam (TiSa: ~800 nm))
R52 of 2nd part of LH chicane is used to ‘smear out’ the energy modulation
Risk of residual density modulation in BC that is not smeared out completely => ‘trickle’ heating (see LCLS 2010)
A look to Laser Heaters at other Facilities

## Slide 23
3. FLASH Laser Heater: Analytical Calculations
Matched laser and e-beam size
Different laser beam sizes
Note: FLASH has largest g and sL
Other facilities have huge overhead in laser power
Not much overhead in laser power:
more challenging for finding timing overlap
Peak power of 2 MW requested
LH Laser delivers > 6 MW
15 – 20 keV

## Slide 24
5. Laser Heater Commissioning
LH Diagnostics: Instrumentation
Undulator Gap: Resonant wavelength => Spectrometer in BC1
Spatial Overlap: Beam size/position of LH laser and e-beam => OTRs LAHE
Temporal Overlap: Coarse (~ns) and fine timing (~ps) of LH Laser and e-beam
  (Typical at other facilities: TDS in the injector)
  Induced energy spread in a dispersive section => OTR in BC1
  Induced Slice energy spread with TDS in a dispersive section => LOLA or PolariX
  Measurement of integrated radiation intensity => photodiode in NIR (1–5 μm) at 28g
  Measurement of MBI structures => LOLA / PolariX
OTR
OTR
LHU
OTR in BC1
Spectrometer
LOLA
PolariX
28g
OTRs LAHE