## Slide 1: Polimi experience towards development of new Front-end solutions for next generation of EuXFEL detectors
Carlo Fiorini
Politecnico di Milano and INFN, Milano, Italy
Workshop on “Future Detectors for the European XFEL”, Hamburg, 18th of Sept. 2023

## Slide 2: OUTLINE
Front-end design for the DSSC readout ASIC
Front-end design in 65nm for low noise readout (of UV sensors)
‘Predictive’ Gain-Switching approach
Possible contribution to FE designs for future EuXFEL detectors

## Slide 3: The DSSC readout ASIC
POLIMI contributions

## Slide 4: Charge preamplifier for the DSSC readout ASIC (1)
Selectable feedback capacitor:
60 fF to 360 fF;
Selectable resistor: 7, 10, 15 kΩ;
Dynamic range: 256 or 2560 photons;
Energy range from 0.5 to 3 keV;
CSA current consumption of 120 µA.

## Slide 5: Charge preamplifier for the DSSC readout ASIC (2)
A control loop is been implemented during the programming phase
The loop exploits the CSA output stage;
The loop programs the CSA output voltage to the same Filter virtual ground voltage (Offset Compensation).
Programming phase

## Slide 6: Electronics noise vs. Integration time (courtesy M.Porro)
Mini-SDD
Front-end
f=4.5 MHz
f=1.125 MHz
f=2.25 MHz
gain = 7 ADU/3 keV = 2.333 ADU/keV
50.2
40.3
43.1
T=-20 °C
Noise vs. T int @ 2.25 MHz
Spectral resolution @ 3keV + Au Ma (2.123keV)
DEPFET
Front-end

## Slide 7: Pixel Readout in 65nm (MIRA ASIC)
Pixel readout channel
Sum.
CSA
Disc.
C1
C2
Readout
Counters
CSCL
From adjacent pixels
To adjacent pixels
right
bot.
MCP
Photocathode
MIRA
UV-ray

## Slide 8: MIRA Charge Sensitive Amplifier (CSA)
MIRA CSA:
Folded Cascode Amplifier
Buffer  Selectable for different shaping times: Fast & Slow Mode
ICON*  Large feedback resistance
for discharge
* Refs:
R. L. Chase, A. Hrisoho, J.-P. Richer: "8-channel CMOS preamplifier and shaper with adjustable peaking time and automatic pole-zero cancellation." Nucl. Instr. and Meth. A, vol. 409, 1998, p. 328−331.
C. Fiorini and M. Porro, “Integrated RC cell for time-invariant shaping amplifiers”, IEEE Trans. Nucl. Sci., Vol. 51, n°5, pp. 1953 –1960, Oct 2004.
K : 1
K : 1
ICON*
Buffer
Amplifier

## Slide 9: Noise current source vs. pulse duration
MIRA CSA
Main noise current source at the input ∝
Shaping time ∝
No dependence between noise of and shaping time
Buffer and left-brench ICON noise sources demagnified by a factor K2  negligible
K : 1
K : 1
ICON
Buffer
Amplifier
Krummenacher*
Shaping time ∝
Noise current source ∝
Dependence between noise of and shaping time
*Ref: Krummenacher, Francois. ”Pixel detectors with local intelligence: an IC designer point of view.” Nuclear Instruments and Methods in Physics Research Section A 305.3 (1991): 527-532

## Slide 10: MIRA CSA Transient Pulse and Noise - Simulations
Slow Mode
Fast Mode
Slow Mode:
Fast Mode:

## Slide 11: Noise contributions - Simulations

## Slide 12: The SuperPixel - Layout
D
A
35μm
35μm
Shared Logic
D
A
Anode
Pixel
m
m
CSA
m
ANODE
Analog
Digital
Cap.
Sum. Stage
& Current Comp.
DAC
PCR
Counters
CSCL
The SuperPixel:
Two mirrored pixels with adjacent digital parts
35x35 μm2 pixel size with 20x20 μm2 anode size
Half-analog and half-digital pixel
Fully-custom design for analog part, RTL design and synthesis for digital part

## Slide 13: MIRA I CSA Transient Response - Measurements
With active probe:
Slow Mode
,

With SMA connection:
Vamp
tfall
trise

## Slide 14: MIRA II –Results
All pixels are configurable and readable
Low-threshold operation
Vout
CK1
Discriminator
Vout
ENC = 20 e-rms

## Slide 15: Gain-switching: standard approach
V
V
V
t
t
t
Threshold
G1→G2
G1→G2→G3
G1

## Slide 16: Gain-switching: ‘predictive’ approach
High Gain
T1
T2
Vth
VDD
High Gain  Mid Gain
T1
T2
Vth
VDD
High Gain  Low Gain
T1
T2
Vth
VDD
Input signal
Output voltage
Features:
Only one gain transition among multiple gains
Relative freedom in setting the threshold
Gain-switch decision taken quite early vs. end of integration

## Slide 17: Implementation in a SiPM-readout ASIC
L.Buonanno, D.Di Vita, M.Carminati and C.Fiorini, "GAMMA: A 16-Channel Spectroscopic ASIC for SiPMs Readout with 84-dB Dynamic Range", (2021) IEEE Transactions on Nuclear Science, 68 (10), pp. 2559-2572.

## Slide 18: Experimental results
Non linearity

## Slide 19: Implementation in a gamma-ray detector
M. Agnolin et al., "A γ-Ray Detector Based on a 3" LaBr3:Ce:Sr Crystal with SiPM Readout for 80 keV – 16 MeV Energy Range with Position Sensitivity for Doppler Correction," in IEEE Transactions on Nuclear Science, doi: 10.1109/TNS.2023.3312424.

## Slide 20: Gain switching statistics

## Slide 21: Study of FE in 65nm for EuXFEL detectors
Q
Range1: 1-20ph @1keV
Range2: 20-1000ph @1keV
Range3: 103-104ph @1keV
CD
CF1
Gain switching
Trapezoidal
Filter
CF2
CF3
G1
G2
G3
300e-
2000e-

## Slide 22: Preliminary noise evaluations...
Range1: 1-20ph @1keV
ENC @50ns Tint: 31e- rms (S/N ~ 9.0 @1keV)
ENC @100ns Tint: 26e- rms
ENC @150ns Tint: 24e- rms
Range2: 20-1000ph @1keV
ENC: 246e- rms  1.1ph @1keV
Range3: 103-104ph @1keV
ENC: 1880e- rms  6.7ph @1keV
(CT=130fF, Range1,2 do not include 2nd stage noise contributions)

## Slide 23: Wrap-up..
Acknowledgments:
Matteo Porro
European XFEL GmbH, Hamburg, Germany and Università Ca’ Foscari Venezia, Venezia, Italy
Leonardo Nassi, Adele Ciavarella, Edoardo Fabbrica, Davide di Vita
Politecnico di Milano an INFN, Milano, Italy
Polimi team is willing to contribute to the development of FE solutions for detectors for EuXFEL and to collaborate with other teams for new large scale ASICs.