## Slide 1
Verbundmeeting 28.02.2023
STRV-R1 A SEU tolerant RISC-V implementation

## Slide 2: Background - Typical Application
Many custom ASICs have a similar structure:
Design of a custom ASIC is complex and time consuming
Reuse of generic blocks possible (ADC, voltage regulators, etc.)
Adaptation of internal logic difficult
   Often custom to original application, requiring full redesign
Idea: Replace internal data processing logic with RISC-V core
  Adaptation to new application / Bugfixes via firmware updates
AD / DA Converter
Internal Logic
Communication Interface
Data Acquisition
Data Transfer
Data Processing

## Slide 3: STRV-R1 | Architecture
RV32-IMC Core
  3 stage pipeline
  Multiplication extensions
  Compressed instruction extension
Three SRAM Instances with Scrubbing algorithm
  Dual Port SRAM
  3x 32Kbyte
1.2V Core & I/O supply

## Slide 4: Triple modular redundancy (TMR)
Triple modular redundancy (TMR)
  Triplication of combinational logic / storage elements
  Elimination of single points of failure
Majority voter  following logic receives corrected Signals
  Mismatch Signal available
Additional feedback is integrated via multiplexer
  Feedback uses majority voter output
  Possible bit errors are corrected within one clock cycle

## Slide 5: SRAM | Single Event Effect Mitigation
SRAM must be treated explicitly
  Large area, high likelihood of SEUs
  Some data accessed very rarely
  Risk of accumulated SEUs
Three SRAM instances with majority voting
  Access to one row at a time
  In case of disagreements:
  Majority voted data written back
Dual-Port RAM required
Refresh rate depended on SRAM module size
Read SRAM Row
Compare 3 Instances
Write SRAM Row
Increase SRAM Row

## Slide 6: SEU Detection Network
Detection of occurred SEUs
  Data acquisition during irradiation
Majority voter provides mismatch signal
  During runtime: SEU occurred
  Signal fed to SEU counters
  Accessible via memory mapped registers
SEU Signal available
  Via Software
  Via Pad on the Chip / direct output
SEU Register
Periph Counter
Core Counter
SRAM Counter
SRAM
SRAM
SRAM
SRAM
Refresh
Periph Instances
Voter
1
Voter
2
Voter X
≥1
Core Instances
Voter
1
Voter
2
Voter X
≥1

## Slide 7: STRV-R1 | Implementation
65nm Technology
Size: 2x2mm
RV32I Core with M and C extension
50 MHz @ 1.2V
3x32 Kbyte Dual-Port SRAM
  Divided into two 16Bit wide SRAM cells
SRAM-Scrubbing
  Upper refresh limit 320μs @ 50MHz
Interfaces:
  UART, JTAG, 27 GPIOs
Separate power domains:
  Core
  SRAM
  Peripherals + Padring
SRAM
1A
SRAM
2A
SRAM
1B
SRAM
2B
SRAM
1C
SRAM
2C
CORE
PERIPH
SRAM Interface

## Slide 8: STRV-R1 | Implementation
65nm Technology
  Thing gate oxide transistors only
  increased TID hardness
  IO-voltage limited to 1.2V
TMR Strategy:
  Triplication of all components
    including peripherals
  Three separate clock-trees
  CLK, Reset, JTAG use triplicated Pads
  Other signals voted before Padring
Spacing between redundant instances:
  15μm
STRV-R1 Layout
Left: SRAM Right: Core & Peripherals

## Slide 9: Test system | Overview

## Slide 10: Test system | X-ray Irradiation
X-ray irradiation with TID >1GRad
Dose-rate 2.08 MRad/h
X-ray irradiation performed at -10°C
Leakage and dynamic power measured
No functional interrupt observed

## Slide 11: TID Results | System Currents

## Slide 12: TID Results | Leakage Currents

## Slide 13: Test system | Heavy-Ion Irradiation
Beam Flux: 1,5 x 104 p/(s*cm²)
Beam Diameter: 25mm (+-10%)

## Slide 14: Heavy-Ion| SEU Cross-Section
SRAM Macros (SRAM-Refresh) RISC-V Core (Majority Voter)
Cross-section of occurring SEUs, no correction / mitigation
RISC-V Core: Cross-section significantly larger than observed by previous works
  Likely caused by large combinational logic between flip-flop
  SETs are propagating through design, captured by flip-flops as SEU

## Slide 15: Heavy-Ion| SEFI Cross-Section

## Slide 16: Heavy-Ion| Event Rate SEUs & SEFIs

## Slide 17: Heavy-Ion| SEFI Type

## Slide 18: Heavy Ion | SEFI Recovery
Test system resets the RISC-V core after a SEFI occurred
Not all SEFI can be recovered by a reset of the RISC-V core
  Data and Instructions in the SRAM can be upset
  Reprogramming of the SRAM required
Reprogramming rate depending on LET:
For low LET (<16 MeV.cm²/mg):
  Reprogramming required in 30% of SEFIs
For higher LET (>16 MeV.cm²/mg):
  Reprogramming required in most cases (>65%)
 More non-corrected upsets
in SRAM at higher LET

## Slide 19: Backup

## Slide 20: Backup | Background
FH Dortmund is member of the ATLAS and RD-53 CERN collaboration
Involved in development of custom ASICs:
  Power supply (regulators)
  Monitoring & control system
Pixel detectors placed around beam pipe

## Slide 21: Backup | Background - Typical Application
Many custom ASICs have a similar structure:
Design of a custom ASIC is complex and time consuming
Reuse of generic blocks possible (ADC, voltage regulators, etc.)
Adaptation of internal logic difficult
   Often custom to original application, requiring full redesign
Idea: Replace internal data processing logic with microprocessor core
  Adaptation to new application / Bugfixes via firmware updates
AD / DA Converter
Internal Logic
Communication Interface
Data Acquisition
Data Transfer
Data Processing

## Slide 22: Backup | STRV-R1 Memory Layout
Instruction and data are stored in the same SRAM
  Instruction data not persistent
Flexible memory layout is possible
  IMEM instruction bus & DMEM data bus can access whole SRAM address range
Instruction and data bus share the same SRAM interface
    Pipeline of RISC-V stalls during load & store instructions to SRAM
    load & store to peripherals simultaneously possible

## Slide 23: Backup | STRV-R1 Peripherals
Memory mapped registers
  Accessible via DMEM bus & MEM Bridge
Address based AHB-lite slave multiplexer
  Currently 3 slaves
  Expandable in the future
GPIOs
  4 control register
  1 status register
16550 compatible UART
  16 Byte FIFO buffer
  Interrupt to Core support

## Slide 24: Backup | Triple Modular Redundancy
Digital circuits usually consist of combinational logic and synchronous storages
Triple modular redundancy (TMR)
  Triplication of combinational logic / storage elements
  Elimination of single points of failure
Majority voter  following logic receives corrected Signals
  Simple cell layout, small cross section
  Three voters, preventing single point of failure
Single majority voter needed at the edge of the digital block
  Single output interface signal

## Slide 25: Backup | Triple Modular Redundancy - Issues
Not all flip-flops updated regularly
  Example: Control / Status Register
  Content of the flip-flop only updated when en signal actice
Data corrupted by SEU remain stored in flip-flops
  Particularly affected : Flip-flops with low refresh rate
  Increased risk: 2 of the 3 flip-flops are flipped by SEUs
 Output signal invalid despite triplication
↯
↯
↯
↯
↯

## Slide 26: Backup | Triple Modular Redundancy - Feedback
Goal: Automatic correction of memory contents
  Logic function and memory elements are already triplicated
Additional feedback is integrated via multiplexer
  Feedback uses majority voter output
  Either new values or corrected data is saved (refresh)
  Possible bit errors are corrected within one clock cycle
Disadvantage: Increased area / power consumption

## Slide 27: Backup | Cross-Section Definition
Cross-Section Definition:

## Slide 28: Backup | Test System Flow

## Slide 29: Backup | X-ray Test Setup

## Slide 30: Backup | X-ray Test Setup

## Slide 31: Backup | Heavy-Ion Test Setup

## Slide 32: Backup | Heavy-Ion Test System Feedthroughs
Feedthrough:
4x RJ45 (Ethernet)
  LVDS DUT
1x RJ45 (Ethernet)
  Sense
  Supply + Temperature
1x DSUB25
  Supply
  3x 1,2V DUT
  1x 3,3V DUT Carrier

## Slide 33: Backup | Heavy-Ion SEFI vs. SEU