## Slide 1: Overview of ultrafast electron scattering activities
Raffael Niemczyk
Institute of Radiation Physics · FWKE · Raffael Niemczyk · r.niemczyk@hzdr.de · www.hzdr.de

## Slide 2: Ultrafast Electron Diffraction (UED)
    Diffraction tells molecular structure
    X-ray diffraction powerful, but parts remain unseen
    Atoms and electrons detected by electron diffraction
    Typical: Pump-probe experiment
      Laser excitation starts sample reaction
      Ultra-short electron bunch probes sample
      Diffraction pattern reveals sample structure
Experiment Principle
Optical pump
Electron
beam
Sample
Diffraction
pattern

## Slide 3: Ultrafast Electron Scattering
    Compared to x-rays
      Stronger interaction (4 – 6 magnitudes higher)
      Less e-beam energy required
        Smaller machine
      Better visibility of lighter atoms
      Same/similar analysis software/hardware
    Compared to keV electrons
      Smaller space charge forces
        Higher brightness
        Shorter bunches
      Less sensitive to E- & B-fields
      Relativistic  no dephasing  Better time resolution
Compared to x-rays & keV electrons

## Slide 4: Ultrafast Electron Scattering
Pros & cons
    Large coherence LC needed
    High-brightness emission regime
      (pancake beam)
      (cigar beams)
      Same physics as (XFEL) injectors

## Slide 5: Ultrafast Electron Scattering
Activities worldwide
SLAC
LBNL
UCLA
BNL
STFC
SJTU
Osaka
KAERI
THU
PKU
HZB
DESY
DELTA
HZDR

## Slide 6: UED beamlines
    LBNL UED beamline ‘HiRES’
      1 MHz
      E < 1 MeV
      APEX gun (cw)820 keV)
    SLAC UED beamline ‘ASTA’
      E ~ 3.7 MeV
      Rep. rate 120 Hz
      Liquid/gaseous samples
Selection of setups

## Slide 7: UED beamlines
    Shanghai Jiao Tong University
      S band gun (3 GHz)
      DBA optics
      Time resolution
        50 fs FWHM
    ‘RUEDI’
      Funding granted: 124 M£
      S band gun (3 GHz)
      Beamline for imaging & diffraction
Cont’d
Imaging/Microscopy
Diffraction
Sample chamber
Sample chamber

## Slide 8: Within Helmholtz…

## Slide 9: REGAE at DESY
Relativistic Electron Gun for Atomic Exploration
Average energy | 3 – 5 MeV
Energy spread | ~5 keV
Bunch charge | 10 – 200 fC
Bunch length | > 20 fs
Beam size | 5 – 500 µm
Trans. emittance | 10 – 100 nm

## Slide 10: REGAE
    Initially developed as X-FEL detector
      Detector group at PSI
    Direct electron detection
      Characterized at CLARA [1]
      Integrating detector
      High dynamic range (3 gain steps)
      ~10% absorption at 3 MeV
      Gate function for dark current suppression
    >10 times higher signal-to-noise ration that scintillator screen based detection
Jungfrau 1M detector for direct electron detection
[1] E. Fröjdh et al., JINST 17 C12004 (2022)

## Slide 11: REGAE
    Fully UHV compatible
    High-precision rotation axis
      Full 360 degree rotation
      Angular resolution: 0.0001 degree
    Centering stage:
      12 mm travel range in x,y,z
      Positioning accuracy of 1 µm
    Upgrade plans:
      Cryogenic sample cooling
      Robotic sample loading through load-lock system
Goniometer in sample chamber: e-Roadrunner

## Slide 12: REGAE
Pumping possible with THz, IR, VIS, UV
3 MeV electron diffraction pattern of a TaS2 sample, recorded at REGAE, showing superlattice reflections of a charge density wave

## Slide 13: SEALab at HZB
    Beamline for diffraction & imaging
      Optics developed
      Partners on-site/close
    SRF gun prepared
      Conditioning started
    First beam planned Oct./Nov.
Superconducting Electron Accelerator Laboratory
Beam energy | 1 – 3.5 MeV
Max. avg. current | 2.5 µA
Bunch charge | > 50 fC
RF frequency | 1.3 GHz
RMS Bunch length | 0.02 – 2 ps
Trans. emittance | 30 nm

## Slide 14: SEALab
    Flexible accelerator & magnet system
      SRF gun & 3 booster cavities
    Allows strong bunch compression
    Allows jitter/TOF reduction
    Magnets allows quick change between imaging & diffraction
    Excellent setup for tests of beam dynamics, instrumentation, controls, & synchronization
Superconducting Electron Accelerator Laboratory

## Slide 15: DALI at HZDR
Dresden Advanced Light Infrastructure
    DALI: Follow-up facility for ELBE
      Several THz sources
      Positron sources
      MeV UED

## Slide 16: MeV UED at HZDR
    THz & positron user facility DALI
    MeV UED instrument at DALI
      SRF Gun as electron source
      Probe lattice in superconducting states
      Addition: Liquid & gas-phase experiments
Dresden Advanced Light Infrastructure
 | Superradiant MIR-THz | Broadband THz | MIR-THz FEL Oscillator
Wavelength range | 10 µm – 3 mm | 120 µm – 3 mm | 10 – 120 µm
Frequency range | 0.1 – 30 THz | 0.1 – 2.5 THz | 2.5 – 30 THz
Pulse energy | 100 – 1000 µJ | 100 µJ | 10 µJ
Repetition rate | 0.1 – 1 MHz | 0.1 – 1 MHz | 10 MHz
Pulse length (rms) | 0.2 – 15 ps | 0.2 ps | 1 – 25 ps
Bandwidth | 0.5 – 15 % | 100 % | 0.5 – 3.0 %

## Slide 17: MeV UED at HZDR
    SRF Gun tests for UED applications
    Gun characterization for UED settings
      Test samples installed
      Further UED upgrades in process
    Beam time limited by user operation
      Non-invasive experimental setup needed
        Standard cathode
        Laser beamline adjustments: small spot sizes
      Detector station
        EMCCD camera in purchase
ELBE
Average energy | 3 – 6 MeV
Repetition rate | 1 MHz
Bunch charge | ~100 fC
Bunch length | 2.5 ps (rms)
Trans. emittance | 30 nm

## Slide 18: MeV UED at HZDR
Simulation: Test experiment at ELBE
SRF Gun II
Solenoid
Quadrupole triplet
Screen station 1
Screen station 2
Screen station 3
Screen station 4
    First experiments in diagnostics beamline
    No disturbance of user operation
      Only quick changes to laser beamline: 100 µm diameter
      No exchange of cathode possible: Cs2Te
      Detector: Quick hardware exchange needed
    Static experiment: Long pulses okay

## Slide 19: MeV UED at HZDR
    ASTRA simulations
      30 MV/m peak gun gradient
      2.5 ps (rms) laser pulse length
      100 µm diameter (Cs2Te)
      100 fC
    Only solenoid, no extra quadrupole focusing
    Gun at off-crest phase
      Check bunching capabilities
      Short bunch at detector possible
    Linearity in phase spaces
      Stronger focus possible
Simulation: Test experiment at ELBE
z = 2.41 m
z = 2.41 m
ε = 36 nm
σ = 480 µm

## Slide 20: Summary
    UED activity at DESY, HZB, & HZDR
      Coordination, but only few people
      Different statuses
      REGAE: Strong push towards user operation
    Synergies with photo injectors
      Cathode gradient
      Mean transverse energy
      Repetition rate
      Stability
    Synergy with synchrotrons & XFELs: Detectors
UED summary

## Slide 21: Outlook
    UED user workshop next week
      Develop & cultivate user community
    Open goals:
      Bunch length & profile measurement
      UED time resolution: Towards 5 fs? 1 fs?
        Most stable machine needed
    Machine optimization: AI applicable
      Fewer knobs & lower beam power
UED outlook
UED user workshop
Thanks to
Klaus Flöttmann & Alke Meents
Thorsten Kamps
J. Michael Klopf

## Slide 22
    Contact
    Helmholtz-Zentrum Dresden-Rossendorf
    www.hzdr.de
    Raffael Niemczyk Institut für Strahlenphysik r.niemczyk@hzdr.de +49 (0) 351 260 2205

## Slide 23: Detectors and instrumentation
    Jungfrau 1M for detection of diffraction image
      Excellent for now, development in long future needed
    TDC and THz streaking for bunch length/profile
    Arrival time correction
    Improve time resolution?
UED summary

## Slide 24: Introduction
    MeV UED vs. x-ray diffraction
      Scattering cross section: 105 higher
      Shorter wavelength: 0.3 pm vs. 100 pm
      Size, cost, access
    MeV UED vs keV UED
      Higher brightness & charge
      At speed of light: Higher time resolution
      Penetration depth
        Allows for thicker (100 nm) samples
Comparison of electron diffraction with other methods

## Slide 25: Ultrafast Electron Scattering
    Many high-brightness injectors in Germany
      Local expertise
      Parameters differ
    Compact facilities
    Beam manipulation ‘easy’
    Space charge limits electron bunch density
    X-ray detectors usable for MeV UED
      Jungfrau 1M
Pros & cons: Compared to x-rays

## Slide 26: Goal of my talk
    Convince H. Schlarb of tasks within POV V
    Give people overview of UED activities
    Show what DESY, HZB, and we are doing
    Diffraction detection is good with Jungfrau 1M detector
    THz streaking/ bunch length measurements next best thing
      No strong user community
    Quick change between imaging and diffraction mode seems interesting for users
For Raffael

## Slide 27: REGAE
    Located at DESY
    Burst-mode S band gun, buncher, TDC
      Electron diffraction
      Time-resolved microscopy
      THz streaking
Relativistic Electron Gun for Atomic Exploration
Average energy | 3 – 5 MeV
Energy spread | ~5 keV
Bunch charge | 10 – 200 fC
Bunch length | > 20 fs
Beam size | 5 – 500 µm
Trans. emittance | 10 – 100 nm

## Slide 28: SEALab
    dsafasdfasdf
Superconducting Electron Accelerator Laboratory

## Slide 29: Ultrafast Electron Scattering
    Large coherence LC needed
    High-brightness emission regime
      (pancake beam)
      (cigar beams)
      Same physics as (XFEL) injectors
Pros & cons

## Slide 30: Ultrafast Electron Scattering
    Large coherence LC needed
    High-brightness emission regime
      Same as (XFEL) injectors
Pros & cons