## Slide 1
Cascaded laser proton acceleration
well beyond 100 MeV energy
Tim Ziegler1,2,
S. Assenbaum1,2, C. Bernert1,2, F.-E. Brack1,2, T. E. Cowan1,2, N. Dover3,4, M. Garten1,2, L. Gaus1,2, I. Goethel1,2,
H. Kiriyama3, T. Kluge1, S. Kraft1, F. Kroll1, J. Metzkes-Ng1, M. Nishuichi3, M. Reimold1,2, M. Rehwald1,2,
H.-P. Schlenvoigt1, M. E. P. Umlandt1,2, M. Vescovi1,2, U. Schramm1,2 & K. Zeil1
Helmholtz-Zentrum Dresden-Rossendorf, Dresden, Germany
Technische Universität Dresden, Dresden Germany
Kansai Photon Science Institute, National Institutes for Quantum and Radiological Science & Technology, Kyoto, Japan
John Adams Institute for Accelerator Science, Imperial College London, London, United Kingdom
9th Annual Helmholtz Matter and Technologies Meeting 2023

## Slide 2
application
beam transport
Laser-driven proton sources for high dose rate radiobiology
major hurdles: performance, instrumentation, readiness and stability level
plasma source: broadband (spatial + spectral), rep. rate, fluctuations
Radiobiological studies are among the most challenging application experiments for a laser acceleration facility
proton beam generation

## Slide 3
Development of laser-driven proton acceleration
  2000
  ~60 MeV@NOVA >400 J laser energy
  ~20 MeV@Ti:Sa laser <5 J laser energy
  2005-2009
  2010
  in-vitro radbiology
  2015
  PW-class Ti:Sa laser

## Slide 4
optimisation procedure for enhanced beam quality (>60 MeV in routine operation)
stable proton beam generation over months
Demonstration of accelerator readiness at HZDR
T. Ziegler, et al., Sci. Reports 11, 7338 (2021)
accelerator readiness + stability benchmarked via application-specific parameters
In total 47 mice at HZDR (7 proton irradiated)
4 ± 0.3 Gy dose delivery precision
3 weeks of irradiation-readiness at DRACO-PW
F. Kroll, et al., Nature Physics 18.3 (2022)

## Slide 5
  2000
  ~60 MeV@NOVA >400 J laser energy
  ~20 MeV@Ti:Sa laser <5 J laser energy
  2005-2009
  2010
  in-vitro radbiology
  2015
  PW-class Ti:Sa laser
  2020
  3D in-vivo irradiation
Development of laser-driven proton acceleration

## Slide 6
What‘s next?
  Favaudon et al. Sci. Transl. Med. 2014
  ultrahigh dose-rate FLASH
  irradiation increases the differential response between normal and tumor tissue in mice
  plasma-accelerators inherently deliver ultrashort part. bunches
  increase acc. performance (energy + particle yield)

## Slide 7
laser mostly
reflected
laser mostly
absorbed
laser mostly
transmitted
plasma density
opaque target
> 1023 cm-3
~1021 cm-3 = ncritical [800nm]
near-critical density
< 1020 cm-3
transparent target
Plasma density tailoring for advanced acceleration regimes
TNSA
Magneto vortex acc.
Bulanov & Esirkepov PRL (2007)
TNSA
Relativistic transparency
Henig PRL(2009), Yin POP (2011), D’humieres POP (2015),
Higginson Nat Commun (2018), Gonzales-Izquierdo ApplSci (2018)
Snavely PRL(2000), Clark PRL (2000)
pre-expansion by preceding light
foil

## Slide 8
enhanced proton energies at optimal thickness
onset of transparency at optimal thickness
targets get transparent during interaction
 increased absorption + coupling into ions
comparison to other high-power laser systems
 excellent agreement
Relativistically transparent targets enhance ion energies
N. Dover & T. Ziegler et al., Light Sci Appl (2023)
3D PIC simulation
2D hydrodynamic simulation

## Slide 9
Experimental setup for relativistic transparency regime
DRACO-PW
EL = 22.4 J (on target), τ = 30 fs
F/2.3 OAP  2.3 µm (FWHM)
Ipeak = 6.5 x 1021 W/cm² (a0=55)
targets: 250±25 nm Formvar foils

## Slide 10
Highest energies in 15° direction / correlation to transmitted light
trans. light suited to identify optimal performance regime
correlation: trans. light - laser-target conditions
high shot-to-shot fluctuations
proton energies >100MeV at 15° & 31°

## Slide 11
T. Ziegler et al. (in review)
Laser energy scaling of relativistic transparency regime

## Slide 12
T. Ziegler et al. (in review)
High energy component features spectral modulation
TPS15: two components (bi-modal)
  exp. decay up to 15-40MeV
  separated high-energy component up to 150MeV
TPS45: one component
  exp. decay up to ~60MeV

## Slide 13
bi-modal feature (low + high-energy component)
high-energy component with reduced divergence
high-energy component shifted towards laser axis
particle numbers match to TPS results
Radio-chromic films confirm spectral energies and directionality
T. Ziegler et al. (in review)

## Slide 14
3D PIC simulations reveal a cascade of acc. regimes
multiple mechanisms contribute to energy gain:
FrontSide Acceleration (FSA)
prompt electrons
thermal sheath
Coulomb Repulsion (CR)
Experimental data
Simulation data
acceleration cascade

## Slide 15
stable beam generation >60MeV  accelerator readiness reached
directed high energy beam >100 MeV  control needed
Systematic radiobiology studies with laser-driven ion beams are feasible

## Slide 16
Thank you!
J. Pawelke, E. Beyreuther, K. Brüchner, E. Bodenstein, L. Karsch, E. Lessmann, M. Krause, E. Troost, N. Cordes, C. Richter, et al.
K. Zeil, J. Metzkes-Ng, C. Bernert, F. Brack, M. Garten, L. Gaus, S. Kraft, F. Kroll, M. Rehwald, M. Reimold, H.-P. Schlenvoigt, M.E.P. Umlandt, T. Kluge, M. Garten, I. Goethel
D. Albach, S. Bock, R. Gebhardt, U. Helbig, M. Löser, T. Püschel, M. Siebold et al.
T. E. Cowan, R. Sauerbrey, U. Schramm
N. P. Dover, A. Kon, M. Nishiuchi, H. Kiriyama et al.