## Slide 1: GPTFEL - A frequency-based GPT extension for FEL interactions
Andrew Fisher
FLASH2020+ 4th Start to End Simulation Workshop
29, June 2023
FLASH2020+ 4th Start to End Simulation Workshop

## Slide 2: Outline
General Particle Tracer (GPT) by Pulsar Physics
GPT-FEL (custom function)
  Field representation and mode evolution
  Input and Output
  Free space/waveguide examples
Other types of operation
  Time-Independent (single frequency)
  Source Dependent Expansion (SDE)
Notes: Bas questions:
No Laguerre polynomial function for c++?
Updated version of GPTFEL?
Did he write script for reading gdf into matlab?
Energy conservation somewhere?

## Slide 3: General Particle Tracer (GPT)
About GPT
  Proprietary code in development since 1996
  3D particle tracking in time domain (adaptive stepsize)
    Macroparticles
  Complete freedom in particle distribution and beamline element orientation
  Use custom fieldmaps
  Users can create customized elements (not black box)
Learning curve
  Detailed manuals with examples
  GUI interface available for Windows

## Slide 4: Code Structure
Input file
  Define/read beam
  Position beamline elements in world coordinate system, “wcs”
  Define output format
Batch file
  Run simulation
  Compute statistics (avg/std at each timestep)
  Convert filetype
Parameter Scans
Notes: Can read from ascii, astra

## Slide 5: GUI Plotting
https://www.pulsar.nl/gpt/gptwin

## Slide 6: GPT-FEL as custom element
Motivation for development at UCLA
  3-14 MeV Student-run Beamline
  Interfaces with beam transport and photoinjector simulation
  Space charge, field maps, waveguide dispersion
  Improvement of existing G00mf function
Collaborations
  PAX at SLAC
  Israeli THz FEL
THz Waveguide FEL at UCLA
GPT-FEL
Notes: PAX – wanted to confirm bunching was implemented correctly in genesis
Built in function Gauss00mf
Space charge, field maps, waveguide dispersion

## Slide 7: GPT-FEL Basics
Field representation
  Frequency and transverse modes (q)
  Complex amplitude
  Mode area and dispersion
  Complex polarization
Evolving mode amplitudes
  Independently derived from Maxwell’s equations or energy conservation
Dispersion relation
Sum over macroparticles

## Slide 8: Frequency Modes
Specify range and number of simulation frequencies
Data saved to gdf file
  Spectral: freq00, lam00, A00, phi00, W00, alphar00, rw00
  Temporal (periodic): z00, At00, Pt00
fmin
fmax
Freq
Simulate modes
Cavity modes
Notes: Mention good plots to look at trouble shooting.
Spectrum to see if resolving peak

## Slide 9: Spatial Modes (free space)
Laguerre-Gaussian Modes
Hermite-Gaussian Modes
Notes: Lowest order is gaussian in both

## Slide 10: Free Space
Laguerre-Gaussian Basis
  Utilize radial symmetry
  Easier SDE implementation
  Modes defined by waist size () and position ()
Frequency index
Spatial index
Notes: Q: Is it okay to allow different frequencies to have spatial bases with different waist sizes?
A: Even in fixed case, different frequency gaussians diffract differently.
Widen plot, change title to Laguerre-Gaussian

## Slide 11: Waveguide Example (TE modes)
Choose spatial basis
Compute mode area
Define dispersion
  Example of propagation
where

## Slide 12: Radiation Seeding
Parameters
  Peak field
  Bandwidth
  Temporal pulse location
  Transverse waist location
Starting from noise
  Quiet start algorithm
Temporal pulse
Transverse waist
Beam
Undulator
Notes: Figure showing examples of these.
At00 vs z00, peak field equaling Ain with given bandwidth
rw00 vs avgz, for “pulse shifted” and “pulse and waist shifted”
Assume gaussian seed

## Slide 13: Time-Independent
Faster, single frequency simulation
Define total charge as for single bunch
W00 is power, not energy
Notes: Show figure of multifrequency and single frequency simulations giving same power results.
Show input file

## Slide 14: SDE Motivation
Convergence as function of
  Fit target gaussian with Gauss-Laguerre spatial modes
  Mismatching waist requires more modes
Trouble when simulating FEL amplifier with gain-guiding
  Choose to minimize over undulator
Notes: Change label in bottom right figure.

## Slide 15: Source Dependent Expansion
Allow mode parameters to vary
  Sprangle et al.
Recursive structure
  Polynomial identities
B parameter
  Controls mode evolution
  Recover previous in limit
Need constraint to specify B?
Normal mode diffraction
beam interaction

## Slide 16: Adding a constraint
A number of spatial modes (M) accurately describe field if
Use threshold to set B=0 when
Plots show 3 SDE modes for increasing thresholds
0
0
0
IF
ELSE
Notes: Figure of amplifier where mode diverges
Still want to set w_0 accurately, so B=0 (fixed mode) case works and method doesn’t have to work hard/do large changes
Why seed with only zeroth order if the is not a “stable” configuration under SDE evolution?
Post saturation dip

## Slide 17: SDE Benchmarking
FEL amplifier with radiation seed
Compare to theoretical gain length
  ~15% error for single SDE, ~8% error for 11 SDE

## Slide 18: Summary
GPT-FEL improves ability of GPT to simulate FEL interactions
  Parallel processing over multiple-cores
Single-frequency and SDE to reduce modes and simulation time
Benchmarked against Genesis and experiment (waveguide)
Dimensions
Beamline position, cavity length
Frequency modes
Number of modes
Simulation bandwidth (fmin, fmax)
Spatial modes
Number of modes
Waist size
Waist position (shift from center of cavity)
SDE
B threshold
Seed radiation (gaussian)
Peak Field
Seed bandwidth
Shift seed pulse
Inputs
Notes: Similar results to Genesis for PAX and high efficiency experiments.
How long do simulations take?