## Slide 1: Compression and data reduction in serial crystallography
M. Galchenkova, A. Tolstikova, O.M. Yefanov, CFEL @ DESY

## Slide 2: Questions will be answered
Do we need to reduce data?
What must we consider when applying compression algorithms?
Are they universal?
Can we not evaluate data quality afterwards?
Do we have solutions?
No, a quality check is crucial
Our work showcases the application for serial crystallography
Some of them can be used in other fields
What if you have to pay by yourself?
The nature of data matters

## Slide 4: RAW data volume per experiment
LCLS (CS-PAD) from 2011:
4.6Mb * 120Hz * 3600sec * 10hours * 5days = 95Tb
PINK beam at APS (JoungFrau 1M):
2Mb * 1000Hz * 3600sec * 20hours * 5days = 860Tb
Modern synchrotron (Eiger2 XE 16M, compressed!):
16Mb * 400Hz * 3600sec * 20hours * 5days = 2.1Pb
eXFEL now (AGIPD):
(2+2)Mb * 3520Hz * 3600sec * 10hours * 5days = 2.5Pb
eXFEL soon (AGIPD 4M, 2023+):
(8+8)Mb * 3520Hz * 3600sec * 10hours * 5days = 10Pb
LCLS2 soon (ePix10k-HR, 2023+):
8.4Mb * 10000Hz * 3600sec * 10hours * 5days = 14Pb
Calculations done by O. Yefanov
Do we need to reduce data?
The storage costs will not let us to store all collected data

## Slide 5
Possible strategies for data reduction
Lossless compression
Lossy with lossless compression
Saving the 1/2/3 significant bit/s.
Binning
Rounding with constant step (incl. integer and photon conversion)
Measuring less data
Non-hits rejection
Lossless compression gives low CR, Meanwhile lossy compression requires proper data quality check
**CR = compression rate = (uncompressed data)/(compressed data)
*Tests were performed for various detectors (CS-PAD, JungFrau, AGIPD, Eiger) and data from different facilities.

## Slide 6: Lossless compression
 | CR | type | CR | type | CR | type | CR | type | CR | type | CR | type
Bitshuffle with lz4 | 1.103 | F32 | 3.345 | I32 | 8.25 | I32 | 3.581 | U16 | 9.939 | I32 | 7.805 | I32
Bitshuffle without lz4 | 1 | F32 | 1 | I32 | 1 | I32 | 1 | U16 | 1 | I32 | 1 | I32
Blosc,blosclz,level = 6,with bitshuffle | 1.118 | F32 | 2.837 | I32 | 6.361 | I32 | 3.571 | U16 | 10.476 | I32 | 7.897 | I32
Blosc,blosclz,level = 6,with shuffle | 1.095 | F32 | 1.88 | I32 | 3.453 | I32 | 2.194 | U16 | 8.388 | I32 | 5.325 | I32
Blosc,blosclz,level = 6,without shuffle | 1 | F32 | 2.335 | I32 | 2.091 | I32 | 1.986 | U16 | 3.781 | I32 | 2.48 | I32
Blosc,blosclz,level = 9,with bitshuffle | 1.118 | F32 | 2.837 | I32 | 6.361 | I32 | 3.571 | U16 | 10.476 | I32 | 7.897 | I32
Blosc,blosclz,level = 9,with shuffle | 1.095 | F32 | 1.927 | I32 | 3.453 | I32 | 2.267 | U16 | 8.388 | I32 | 5.325 | I32
Blosc,blosclz,level = 9,without shuffle | 1 | F32 | 2.335 | I32 | 2.091 | I32 | 1.986 | U16 | 3.781 | I32 | 2.48 | I32
Blosc,lz4hc,level = 6,with bitshuffle | 1.138 | F32 | 3.038 | I32 | 7.295 | I32 | 3.784 | U16 | 11.502 | I32 | 8.29 | I32
Blosc,lz4hc,level = 6,with shuffle | 1.156 | F32 | 2.379 | I32 | 5.181 | I32 | 2.671 | U16 | 11.453 | I32 | 6.464 | I32
Blosc,lz4hc,level = 6,without shuffle | 1 | F32 | 3.06 | I32 | 5.298 | I32 | 2.275 | U16 | 7.235 | I32 | 4.147 | I32
Blosc,lz4hc,level = 9,with bitshuffle | 1.139 | F32 | 3.044 | I32 | 7.34 | I32 | 3.788 | U16 | 11.573 | I32 | 8.303 | I32
Blosc,lz4hc,level = 9,with shuffle | 1.162 | F32 | 2.471 | I32 | 5.744 | I32 | 2.672 | U16 | 12.636 | I32 | 6.479 | I32
Blosc,lz4hc,level = 9,without shuffle | 1 | F32 | 3.285 | I32 | 6.232 | I32 | 2.371 | U16 | 8.477 | I32 | 4.707 | I32
Blosc,lz4,level = 6,with bitshuffle | 1.119 | F32 | 2.907 | I32 | 6.424 | I32 | 3.654 | U16 | 10.453 | I32 | 8.019 | I32
Blosc,lz4,level = 6,with shuffle | 1.094 | F32 | 1.889 | I32 | 3.185 | I32 | 2.313 | U16 | 7.143 | I32 | 5.243 | I32
Blosc,lz4,level = 6,without shuffle | 1 | F32 | 1.639 | I32 | 2.374 | I32 | 1.508 | U16 | 2.872 | I32 | 1.726 | I32
Blosc,lz4,level = 9,with bitshuffle | 1.122 | F32 | 2.977 | I32 | 6.683 | I32 | 3.664 | U16 | 10.572 | I32 | 8.05 | I32
Blosc,lz4,level = 9,with shuffle | 1.096 | F32 | 1.9 | I32 | 3.196 | I32 | 2.411 | U16 | 7.16 | I32 | 5.508 | I32
Blosc,lz4,level = 9,without shuffle | 1 | F32 | 1.638 | I32 | 2.374 | I32 | 1.512 | U16 | 2.872 | I32 | 1.726 | I32
Blosc,snappy,level = 6,with bitshuffle | 1 | F32 | 1 | I32 | 1 | I32 | 1 | U16 | 1 | I32 | 1 | I32
Blosc,snappy,level = 6,with shuffle | 1 | F32 | 1 | I32 | 1 | I32 | 1 | U16 | 1 | I32 | 1 | I32
Blosc,snappy,level = 6,without shuffle | 1 | F32 | 1 | I32 | 1 | I32 | 1 | U16 | 1 | I32 | 1 | I32
Blosc,snappy,level = 9,with bitshuffle | 1 | F32 | 1 | I32 | 1 | I32 | 1 | U16 | 1 | I32 | 1 | I32
Blosc,snappy,level = 9,with shuffle | 1 | F32 | 1 | I32 | 1 | I32 | 1 | U16 | 1 | I32 | 1 | I32
Blosc,snappy,level = 9,without shuffle | 1 | F32 | 1 | I32 | 1 | I32 | 1 | U16 | 1 | I32 | 1 | I32
Blosc,zlib,level = 6,with bitshuffle | 1.155 | F32 | 3.096 | I32 | 8 | I32 | 3.785 | U16 | 12.524 | I32 | 8.561 | I32
Blosc,zlib,level = 6,with shuffle | 1.281 | F32 | 3.461 | I32 | 7.918 | I32 | 3.673 | U16 | 17.007 | I32 | 8.952 | I32
Blosc,zlib,level = 6,without shuffle | 1.14 | F32 | 4.339 | I32 | 8.461 | I32 | 3.094 | U16 | 12.958 | I32 | 6.809 | I32
Blosc,zlib,level = 9,with bitshuffle | 1.156 | F32 | 3.109 | I32 | 8.144 | I32 | 3.826 | U16 | 12.732 | I32 | 8.613 | I32
Blosc,zlib,level = 9,with shuffle | 1.284 | F32 | 3.504 | I32 | 8.416 | I32 | 3.676 | U16 | 17.613 | I32 | 8.954 | I32
Blosc,zlib,level = 9,without shuffle | 1.14 | F32 | 4.244 | I32 | 9.353 | I32 | 3.126 | U16 | 13.978 | I32 | 6.989 | I32
Blosc,zstd,level = 6,with bitshuffle | 1.155 | F32 | 3.608 | I32 | 11.201 | I32 | 3.887 | U16 | 13.253 | I32 | 8.753 | I32
Blosc,zstd,level = 6,with shuffle | 1.279 | F32 | 3.453 | I32 | 8.235 | I32 | 3.841 | U16 | 17.568 | I32 | 9.409 | I32
Blosc,zstd,level = 6,without shuffle | 1.121 | F32 | 4.412 | I32 | 8.346 | I32 | 3.291 | U16 | 12.729 | I32 | 7.004 | I32
Blosc,zstd,level = 9,with bitshuffle | 1.161 | F32 | 3.63 | I32 | 11.449 | I32 | 3.943 | U16 | 13.547 | I32 | 8.855 | I32
Blosc,zstd,level = 9,with shuffle | 1.283 | F32 | 3.871 | I32 | 9.439 | I32 | 3.935 | U16 | 20.276 | I32 | 9.929 | I32
Blosc,zstd,level = 9,without shuffle | 1.193 | F32 | 5.022 | I32 | 10.972 | I32 | 3.619 | U16 | 16.87 | I32 | 8.547 | I32
bzip2,level = 6,with shuffle | 1.266 | F32 | 3.579 | I32 | 9.368 | I32 | 4.233 | U16 | 20.355 | I32 | 10.472 | I32
bzip2,level = 6,without shuffle | 1.227 | F32 | 5.918 | I32 | 12.006 | I32 | 4.209 | U16 | 19.7 | I32 | 10.352 | I32
bzip2,level = 9,with shuffle | 1.265 | F32 | 3.643 | I32 | 9.355 | I32 | 4.236 | U16 | 20.405 | I32 | 10.485 | I32
bzip2,level = 9,without shuffle | 1.235 | F32 | 5.923 | I32 | 12.029 | I32 | 4.216 | U16 | 19.752 | I32 | 10.377 | I32
gzip,level = 6,with shuffle | 1.28 | F32 | 3.448 | I32 | 7.887 | I32 | 3.726 | U16 | 17.214 | I32 | 9.233 | I32
gzip,level = 6,without shuffle | 1.14 | F32 | 4.506 | I32 | 8.465 | I32 | 3.182 | U16 | 13.077 | I32 | 6.865 | I32
gzip,level = 9,with shuffle | 1.283 | F32 | 3.504 | I32 | 8.439 | I32 | 3.729 | U16 | 18.264 | I32 | 9.243 | I32
gzip,level = 9,without shuffle | 1.14 | F32 | 4.408 | I32 | 9.542 | I32 | 3.229 | U16 | 14.427 | I32 | 7.169 | I32
lz4,nbytes0 | 1 | F32 | 1 | I32 | 1 | I32 | 1 | U16 | 1 | I32 | 1 | I32
lz4,nbytes = 16384 | 1 | F32 | 1 | I32 | 1 | I32 | 1 | U16 | 2.867 | I32 | 1.726 | I32
lz4,nbytes = 2048 | 0.998 | F32 | 1.621 | I32 | 2.335 | I32 | 1.474 | U16 | 2.824 | I32 | 1.721 | I32
lzf,with shuffle | 1.106 | F32 | 2.028 | I32 | 3.747 | I32 | 2.509 | U16 | 8.051 | I32 | 5.662 | I32
lzf,without shuffle | 1 | F32 | 2.429 | I32 | 3.162 | I32 | 2.078 | U16 | 3.951 | I32 | 2.541 | I32
zfp,reversible | 1 | F32 | 1 | I32 | 1 | I32 | 1 | U16 | 1 | I32 | 1 | I32
zstd | 1.12 | F32 | 4.41 | I32 | 6.893 | I32 | 3.276 | U16 | 10.546 | I32 | 5.97 | I32
The best CR is usually Bzip2 and zstd, but gzip (lev6) is a good compromise.
>200 tests
CR up to 4 for int (noisy data)
CR up to 1.3 for float
Doesn’t solve the problem!

## Slide 7
What must we consider when applying compression algorithms?
We have to deal with the sparse nature, high dynamic range, high noise level, and sharp intensity changes observed in diffraction patterns
The nature of data matters
Notes: Typical features of the diffraction pattern:
It compromises bright and sharply defined Bragg peaks (greed circles)
It has a relatively smooth background
  the sample delivery medium
  disordered structure
  solvent within the crystal
  parasitic scattering from the beamline
The Bragg peaks at high scattering angles may be comparable to the background noise

## Slide 8
Can we not evaluate data quality afterwards?
Quality check for lossy compression
Quality checks for SX/MX:
1. Data quality: Rsplit,CC*
2. Model quality: Rfree/Rwork
3. Anomalous signal (SAD/MAD)
4. Electron density maps
Should be not worse than original
Highly sensitive to data quality For checking the limitation of lossy compression application
But the checks have to be done properly!
Typical errors:
Using overall CC*/Rsplit  use a plot instead (at least the last shell)
Resolution is limited by the detector  use weakly scattering data
Very good statistics for anomalous data  use a small subset (just sufficient for the pipeline to work)
Does not matter, how you reduce data, Checking data quality is the key!

## Slide 9: Ultimate data reduction in SX
Why do we need to store hits?
On-the-fly processing (under development) No intermediate data is stored
Short time storage  .mtz (possible) Reduction from 100Tb to 1Mb
Storing hits (for now the best) Reduction from 100Tb to 1-10Tb but only for strong datasets
data | Rwork/Rfree | Resolution, Å
Published 66k patterns | 0.196/0.229 | 1.9
Reprocessed 66k patterns | 0.172/0.195 | 1.51
Reprocessed from raw 108k | 0.168/0.189 | 1.49*
*it is the detector corner limit
LCLS 2011 reprocessing

## Slide 10: Electron density
Old
New
We have some solutions, but can we compress even better?

## Slide 11: Measuring less
Max resolution
1.58A
Less data – worse quality
Best per pattern resolution 2.0A
Saving only found peaks – also a bad idea!
The resolution cutoff was 1.81Å
Refinement by D. Oberthuer

## Slide 12: But why cannot we store only found peaks?
From Gati, et al, PNAS 114(9), 2017

## Slide 13: Binning (2x2) and non-hits rejection data from Eiger 16M
We can binn data if the spacing between Bragg peaks at least 5 pixels
Subset of sample | Raw, only hits | Binned, only hits
 | CR | CR
ferritin_1 | 66.08 | 105.32
lyso_1 | 5.25 | 12.22
MPro_1 | 19.73 | 90.21
lyso_2 | 1.35 | 3.06
lacta_1 | 1.06 | 2.74

## Slide 14: Quantization to different levels (AGIPD dataset)
(int div 2e6) * 2e6
int
Even this crap still works (thanks to statistics)!
(int div 2e10) * 2e10
(int div 2e8) * 2e8
Truncating to several photons can work, but it is not applicable all the time

## Slide 15: Non-uniform quantization
Original Uniform quantization Non-uniform quantization
Low intensity data is more important Example: multi-gain detectors
The easiest way – save just a few significant bits!

## Slide 16
8
1
0
1
0
1
0
0
0
1
0
1
0
1
0
0
0
0
0
0
0
1
1
1
0
1
8
0
8
7
0
1
0
1
0
1
1
1
0
1
0
1
0
0
0
0
0
0
0
1
1
1
0
1
8
0
8
8
0
1
0
1
1
0
0
0
0
1
1
0
0
0
0
0
0
0
0
1
1
1
1
0
9
6
5
8
0
1
0
0
0
0
2
0
0
1
0
0
1
0
0
0
0
0
0
0
0
5
6
2
0
0
1
0
0
1
0
0
1
6
0
1
0
1
0
0
1
0
3
0
1
0
0
0
0
1
0
1
1
0
1
1
8
0
2
1
5
0
0
1
0
1
1
0
1
0
1
0
1
0
0
0
1
0
1
1
1
0
1
3
6
5
1
4
Initial number
Binary representation of the initial number
Binary representation of the resulting number
8-bit floating-like representation
Resulting
number
Do we need to store all bits?
The best way to implement – HDF5 plugin.
In this way 3.5 bits are store

## Slide 17: Anomalous dataset for lossy compression evaluation
Data from Nass, Karol, et al., IUCrJ 7.6 (2020): 965-975. (JF 16M, SwissFEL)
For proper evaluation of your compression technique, use the data sensitive to any distortions
Type | Rwork/Rfree | N. of residues | CR | CR after 8bit compressor
raw | 0.2232/0.2821 | 209 | 1 | -
binned | 0.2165/0.2831 | 208 | 5 | -
binned, 3 sign bits | 0.2379/0.2993 | 205 | 32.2 | 36.3
binned, 2 sign bits | 0.2700/0.3337 | 205 | 38.8 | 45.1
binned, 1 sign bit | 0.5314/0.5514 | 181 | 49 | 59.3
binned, 3 sign bits
binned, 2 sign bits
binned, 1 sign bits
binned

## Slide 18: What has been done already?
Conferences, workshops, discussions
User Meeting at EuXFEL (poster 2021, poster and talk 2022)
LCLS User Meeting (poster 2021)
BioEXFEL 9th International Conference (2022 poster)
SRI (poster 2022), CDCS workshop (poster 2022)
local meeting with DA groups from EuXFEL and LCLS (February, 2022)
Apply lossy compression (non-hits rejection and/or binning) at P11, Petra III (SX) -> check data quality -> delete raw data and substitute it with reduced data!
26.11.2020 (11010575): 89Tb -> 34Tb: CR ≈ 2.62 (no binning, only hits)
25.03.2021 (11010929): 116Tb -> 18Tb : CR ≈ 6.44 (binning, only hits)
07.07.2021 (11010938): 95Tb -> 13Tb : CR ≈ 7.31 (binning, only hits)
16.09.2021 (11010507): 130Tb to 23Tb: CR = 5.87 (binning, only hits)
Multiple experiments with pink beam and JF detector at ESRF and APS
RAW data was not even backed up to tape!

## Slide 19
Modern detectors generate too much data to store
But old data can be still useful
Lossless compression not enough: up to 4 (int) and 1.3 (float)
Non-hits are not needed if enough strong hits are present. But hits should be stored in “raw” format for future improvement
Many Mpix detectors are not always needed, so some data can be binned (more than 10pixels between Bragg peaks are usually useless)
SX is more sensitive to the number of measurements than the precision, so quantization can be used
Additional lossless compression has to be be applied
Data quality has to be carefully checked!
Not recommended: “measuring less” and “storing only peaks”
Conclusions

## Slide 20: Acknowledgements
Alexandra Tolstikova Bjarne Klopprogge Janina Sprenger Dominik Oberthuer Wolfgang Brehm Thomas A. White Anton Barty
Henry N. Chapman Oleksandr M. Yefanov
Yaroslav Gevorkov
Valerio Mariani
Karol Nass
Dmitry Ozerov
Thank you!

## Slide 21: Data quality metrics
CC* measures the correlation between measured data and hypothetical noise-free signal. Values close to 1 indicate good agreement.
Rsplit evaluates the agreement between two halves of the dataset merged independently. Lower values around 0.05 indicate higher precision.
Rfree measures how well the model predicts a subset of data not used in refinement. Lower values mean better agreement between model and data.
Rwork measures how well the refined model fits the measured data. Lower values indicate a better fit between observed and calculated data.
Notes: Since we want to check whether masking does not make things worse, we need to check the quality somehow. There are many figures of merit that can be used to check data quality at the different steps of the processing pipeline, for example: СС*, Rsplit, Rwork and R free and many others. In this studies we focused only on this metrics. Each metric is applicable for a specific step of data processing. Here on this slide you can see the formula for this metrics.
СС* is Coefficient derived from CC1/2 in order to estimate the correlation of the merged dataset with the true intensities using the assumption that errors in the subsets are random. R-values measure the agreement between observed and calculated structure factors moduli. CC1\2 is Pearson correlation coefficient.

## Slide 22
8
1
0
1
0
1
0
0
0
1
0
1
0
1
0
0
0
0
0
0
0
1
1
1
0
1
8
0
8
7
0
1
0
1
0
1
1
1
0
1
0
1
0
0
0
0
0
0
0
1
1
1
0
1
8
0
8
8
0
1
0
1
1
0
0
0
0
1
1
0
0
0
0
0
0
0
0
1
1
1
1
0
9
6
5
8
0
0
0
1
0
0
0
0
2
0
0
1
0
0
0
0
1
0
0
0
0
0
0
0
0
5
6
2
0
0
1
0
0
1
0
0
1
6
0
1
0
1
0
0
1
0
3
0
1
0
0
0
0
1
0
1
1
0
1
1
8
0
2
1
5
0
0
1
0
1
1
0
1
0
1
0
1
0
0
0
1
0
1
1
1
0
1
3
6
5
1
4
Initial number
Binary representation of the initial number
Binary representation of the resulting number
8-bit floating-like representation
Resulting
number
Do we need to store all bits?