## Slide 1: WLCG T0 at CERN: Operational experience
Helge Meinhard / CERN-IT
WLCG Workshop at DESY
11 July 2011

## Slide 2: Background (1)
Very smooth, successful LHC running
  Record intensities, record luminosities
    1 fb-1 (goal for end 2011) already reached on 17-Jun
    Pile-up is a problem…
  Confirmation to run until end 2012 at 2 x 3.5 TeV
    Shutdown in 2013
ITIL
  Attempt to follow best practices
  Introduced service desk and new ticketing system on 15-Feb-2011
    Initially covering IT and GS departments

## Slide 3: Background (2)
Monitoring: IT workshop to review situation
  Plenty of monitoring done, plenty of information gathered and stored
  Demands on integrating different systems, and on providing ad-hoc queries, mining, analysis, trends
  Working group has been formed
More generally, revising how T0 operates
  Virtualisation/clouds, configuration management

## Slide 4: Background (3)
Community support
  IT recommended / IT supported / community supported / unsupported / IT prohibits
  Applies to smartphones, tablets, browsers, mail clients, …
  Infrastructure created
Interesting times with EGI and EMI

## Slide 5: Computing Facilities (1)
Stable running
  ... at the limit of power and cooling
In main machine room, temperature of cold air risen carefully
‘Barn’ refurbishment project
  Annex to main machine room being converted into a small high-density room of 450 kW
  Some infrastructure ‘oddities’ of old building being corrected as well

## Slide 6: Computing Facilities (2)
External ‘local’ hosting
  Part of our ‘critical machines’ are now run in hosting centre 15 km away from CERN
Remote T0
  Centre in a CERN member state running part of T0 capacity
  Addressing business continuity as well
  Call for expressions of interest closed, analysis ongoing, formal tender in preparation

## Slide 7: The CERN Data Centre in Numbers
Data Centre Operations (Tier 0)
  24x7 operator support and System Administration services to support 24x7 operation of all IT services.
  Hardware installation & retirement
    ~7,000 hardware movements/year; ~1800 disk failures/year
  Management and Automation framework for large scale Linux clusters
Chart: 
| Fujitsu | Hitachi | HP | Maxtor | Seagate | WDC | Other
 | 1562 | 12389 | 32 | 30 | 8072 | 31561 | 82
High Speed Routers (640 Mbps → 2.4 Tbps) | 24
Ethernet Switches | 350
10 Gbps ports | 2000
Switching Capacity | 4.8 Tbps
1 Gbps ports | 16,939
10 Gbps ports | 558
Racks | 828
Servers | 11,728
Processors | 15,694
Cores | 64,238
HEPSpec06 | 482,507
Disks | 64,109
Raw disk capacity (TiB) | 63,289
Memory modules | 56,014
Memory capacity (TiB) | 158
RAID controllers | 3,749
Tape Drives | 160
Tape Cartridges | 45000
Tape slots | 56000
Tape Capacity (TiB) | 34000
IT Power Consumption | 2456 KW
Total Power Consumption | 3890 KW
Chart: 
| AMD Opteron 6164 HE | Intel Xeon 5150 | Intel Xeon 5160 | Intel Xeon E5335 | Intel Xeon E5345 | Intel Xeon E5405 | Intel Xeon E5410 | Intel Xeon L5420 | Intel Xeon L5520 | Intel Xeon L5630 | Intel Xeon L5640 | Intel Xeon X5650 | Intel Xeon X5680
 | 31032.24 | 1285.16 | 9142.32 | 10135.32 | 48962.01 | 12692.25 | 56134.91 | 40356.46 | 234813.87 | 40 | 68800.52 | 6668.8 | 231.63

## Slide 8: Computing Facilities (4)
Procurement fun points
  7’000 drives (2 TB) swapped out, manufacturer needed several attempts
  Finally got a batch of CPU servers to work
  Bad or late (or both) repair interventions by vendor agents
    Discussing alternative schemes for warranty services

## Slide 9: Communication Systems
Typical tier-0 bandwidth
  Average in: 2 GB/s with peaks at 11.5 GB/s
  Average out: 6 GB/s with peaks at 25 GB/s
Router infrastructure being migrated to new supplier
  More bandwidth
  Experimenting with 100 GE

## Slide 10: Storage (1): Castor
Bulk storage for T0: Castor
In: avg 2.6 GB/s, peak 6.4 GB/s Out: avg 7 GB/s, peak 13.5 GB/s (binning: day)
Total: ~ 47 PB On tape: ~ 36 PB

## Slide 11: Storage (2): Tapes, EOS
Experience: Given the size of the system and the cost-effective components, rather smooth running
  Still, storage and closely related services responsible for most problems with T0 operations
Tapes
  Commissioned 5 TB drives/cartridges
  Tape mark handling improved
For analysis purposes at CERN: EOS
  See dedicated talk on Tuesday morning (Dirk Duellmann)

## Slide 12: Storage (3): DB incident analysis
0.17
0.96

## Slide 13: Storage (4): DB directions
DB (Oracle) storage will be consolidated on NAS rather than FC
Active DataGuard to be used instead of Streams in some places

## Slide 14: Batch services (1)

## Slide 15: Batch Services (2)

## Slide 16: Virtualisation (1): CVI
The CERN Virtual Infrastructure provides custom virtual machines in the CERN computer centre
  These VMs have a long-term lifetime of months/years
User kiosk for requesting a VM in less than 30 mins
Based on Microsoft’s System Center Virtual Machine Manager (SCVMM)
  Enterprise class centralized management
  Rich feature set:
    Allows grouping of hypervisors, with delegation of administrative privileges
    VM migration, High availability
    Checkpointing
    PowerShell for administration / scripting

## Slide 17: Virtualisation (2): CVI
Number of Virtual Machines per Operating System
54% Windows VMs
46% Linux VMs
Apr 2011: 1250 VMs on 248 hypervisors
Nov 2010: 680 VMs on 170 hypervisors

## Slide 18: Virtualisation (3): Cloud
Lxcloud production
CERN VMIC
CERNVM
“Golden Nodes”
Quattor
ONE
production master
ONE
test master
ONE EC2 interface
Lxcloud - Test
Physical Resources
Image creation
VM provisioning
Enduser
VO
Application
Manager
(lxbatch)

## Slide 19: Virtualisation (4): Cloud and lxbatch
1 rack of nodes (~ 400 VMs) in production
Full Lemon monitoring, usage pattern as for public lxbatch

## Slide 20: Virtualisation (5): EC2 i/f
ATLAS/CERN IT-ES are evaluating LxCloud with HammerCloud tests:
  10 virtual CERNVM nodes in LxCloud accessed via PanDA (ANALY_CERNVM_test queue)
  VM instances are created manually with the cvm cloud tool; the VMs start the PanDA pilot to retrieve jobs
  Submitting analysis jobs to measure CPU/Walltime, Events/second and various job timing metrics; comparison with identical hardware on LSF
  Data read with root:// to EOS @ CERN. Outputs lcg-cp’d to CASTOR.
LxCloud raw metrics:
~51.1% mean CPU/Walltime
~9.8Hz event rate
Reference metrics:
~59.1% mean CPU/Walltime
~9.8Hz event rate
Preliminary Results! Work in progress...

## Slide 21: CVMFS at CERN (1)
Client status
  CVMFS on lxbatch/lxplus since Nov 2010
    LHCb fully migrated Apr 2011
    ATLAS partial migration May 2011
      ATLAS now in final preparations for full migration
        See presentation on Wednesday
    CMS working towards use of CVMFS
  AFS software area could be dropped later
    ALICE have their bit-torrent based system
    Previously during ATLAS production AFS has been affected, impacting interactive users

## Slide 22: CVMFS at CERN (2)
Client monitoring
  service cvmfs probe executed once/hour /node
    Executes ls /cvmfs/cms.cern.ch /cvmfs/atlas.cern.ch
    Ran under lemon framework
  This scale testing resolved CVMFS corruption bugs
    Bugs investigated/fixed incredibly fast – thank you
    Fixed with cvmfs >= 0.2.68
  Number of failures out of ≈ 2600000 attempts:
    Apr (part) = 9543, May = 10137, June = 803 , Jul = 64
  cvmfs includes cvmfs_fsck utility:
    Checksums every file on disk so quite expensive
    Run once per week to identify further problems
    Recent bug fixes allow cvmfs_fsck to fix what it finds

## Slide 23: CVMFS at CERN (3)
‘Stratum 1’ service
  cvmfs-stratum-one.cern.ch is one of three
    BNL and RAL have near identical setup
  Service comprises:
    1 disk server pulling new files hourly from stratum0
    2 reverse proxies “protecting” this disk server
  New sites every day in last week

## Slide 24: CVMFS at CERN (4)
Stratum 1 service
  Stratum 1 load dependent on site squid configurations
  Common configurations errors:
    Default max file size to cache only 2 MB (CERN, NIKHEF)
    Only 1 GB of cache on their squids (PIC)
  CERN will continue to contact top subscriber
    Plenty of capacity, < 1MB/s of network today per stratum1 node.

## Slide 25: ActiveMQ service (1)
MQ messaging service
  Provides a general asynchronous messaging service to allow applications to communicate
  Decoupled architecture – the service takes care of the reliable delivery of the messages so your applications don’t have to
  ActiveMQ is an open source Apache project (with a commercially supported version called Fuse)

## Slide 26: ActiveMQ service (2)
Have built service for ATLAS based on the successful deployment of ActiveMQ for the WLCG SAM Nagios testing infrastructure
Atlas tracer service:
  Collects file events from worldwide Atlas DDM clients (3.6 Mevents/day, bursts of 300/s)
Atlas notification service:
  Broadcast notification of dataset states, data availability to interested ATLAS applications (Panda + AMI catalogue currently), 1-2 events/s
Successful pilot service: now moving to production

## Slide 27: GGUS Alarms against CERN
Statistics 01-Jul-2010 to 30-Jun-2011
Source | Number
Castor | 23
Batch | 5
AFS, Kerberos | 6
LFC | 1
Power | 1
VOMS | 1
DB | 1
FTS | 2
Total | 40