## Slide 1: WLCG Storage planning
Andrea Sciabà
WLCG Collaboration Workshop 11-13 July 2011 DESY

## Slide 2: Outline
Global overview of storage systems
Storage system deployment at Tier-1 sites
Storage upgrade plans at Tier-1 sites
Storage development
  Short/medium term plans
Conclusions

## Slide 3: Introduction
WLCG ensures a proper information flow among the project, the sites and the experiments concerning storage and data management issues
The Tier-1 Service Coordination Meeting serves this purpose
Installed software versions, recent and scheduled interventions, new middleware releases, incidents are reported and discussed

## Slide 4: Storage systems in WLCG
ARC: 2
BeStMan: 40
CASTOR: 3
StoRM: 40
dCache: 63
DPM: 215
Xrootd: 6
HDFS: 1
Chart: 
| DPM | dCache | StoRM | BeStMan | xrootd | CASTOR | ARC | HDFS
Storage systems | 215 | 63 | 51 | 40 | 6 | 3 | 2 | 1
DPM is still by far the most common Storage Element
Tier 0+1+2

## Slide 5: Storage systems at the Tier-0/1 sites
Site | CASTOR | dCache | StoRM | DPM | EOS | xrootd | Lustre
CERN | 2.1.11 |  |  |  | 0.1.0 |  | 
ASGC | 2.1.10 |  |  | 1.8.0-1 |  |  | 
BNL |  | 1.9.5-23 |  |  |  |  | 
CNAF |  |  | 1.7.0 |  |  |  | 
FNAL |  | 1.9.5-23 |  |  |  | 2.9.1 | 1.8.3
IN2P3-CC |  | 1.9.5-26 |  |  |  |  | 
KIT |  | 1.9.5-26 |  |  |  |  | 
NDGF |  | 1.9.12 |  |  |  |  | 
NL-T1 |  | 1.9.5-23 |  |  |  |  | 
PIC |  | 1.9.5-26 |  |  |  |  | 
RAL | 2.1.10 |  |  |  |  |  | 
TRIUMF |  | 1.9.5-21 |  |  |  |  | 
CASTOR sites have all very recent releases
dCache sites with the old golden release, only one with the new

## Slide 6: Foreseen upgrades (I)
ASGC
  CASTOR ≥ 2.1.11
  DPM 1.8.2 (allows to define no. of threads for DPM and SRM servers, better filesystem selection algorithm)
  Upgrade all network for disk servers to 10 Gb before Q4
BNL
  migrate to Chimera on August 22
  Evaluate data access via NFS 4.1 on dCache and BlueArc
CNAF
  migrate all instances to StoRM 1.7.0-7 when testing completed
FNAL
  new dCache golden release after Heavy Ions run; will not move to Chimera
  Deploy 400 TB of EOS to move users off dCache resilient pools
  Add more disk before winter
IN2P3
  Upgrade non-WLCG dCache instance to new golden release on September 20th and WLCG instance in January

## Slide 7: Foreseen upgrades (II)
KIT
  Apply bug fixes as appropriate
  New dCache golden release by beginning of next year
NDGF
  Closely follow new dCache patches
  Change authentication to per-DN file ownership and VOMS group ACLs in autumn
PIC
  Migrate to Enstore2 (Jul 26)
  Migrate to new dCache golden release (Aug 9)
RAL
  SRM 2.11 upgrade (VOMS support) in August/September
  CASTOR 2.1.11 (no LSF, new tape gateway) in November/December
TRIUMF
  New dCache golden release after (successful) testing and increase disk from 4 to 6 PB

## Slide 8: dCache “golden releases”
1.9.12 was released in April
Brings several improvements
  Easier, more flexible configuration
  Better xrootd and NFS 4.1 support
  SRM: asynchronous getTURL
  GLUE 2.0 support
  Powerful migration module

## Slide 9: dCache plans (I)
On-demand flush to tape by
  Moving name space entry from ONLINE directory to CUSTODIAL directory
  Creation of an internal copy of a file to the CUSTODIAL space, resulting in two name space entries (only one custodial)
  WebDAV based storage control
Operational improvements
  Random distribution of incoming data and automatic reshuffling of data when new pools are added
  Easier to upgrade components without service downtimes

## Slide 10: dCache plans (II)
Support for a 3-tiered industry storage model
  Layer I: optimized for random I/O: SSD space, NFS4.1/pNFS
  Layer II: optimized for streaming: high density disk space on HDFS, WAN /IO
  Layer III: custodial storage: controlled tape access
Other stuff
  Federations: NFS 4.1 (fedFS), HTTP(S) (+GridFTP, xrootd, …)
  Fully secure HTTP read access to data with standard tools and browsers with X.509 certificates
  “Amazon”-like browser-based console for file browsing and storage control (e.g. disk ↔ tape)
  IPv6

## Slide 11: BeStMan plans
Current version: 2.1.0
Development plans depend on available funding
  Joint proposal submitted to NSF
BeStMan SRM server
  Additional transfer protocol support
BeStMan SRM clients
  Improvement in data transfer efficiency
    Data channel caching with GridFTP transfers for a request with many files
    Determine the transfer parameters from the previous transfer performance
      E.g. number of concurrent transfer connections, number of parallel streams
  Additional transfer protocol support
      E.g. FDT (Fast Data Transfer)
HTTPS support

## Slide 12
CASTOR disk cache evolution
Future plans driven by increasing requirements from the experiments
  E.g. ATLAS trigger at 400 Hz, moving to 600 Hz
Recent changes (CASTOR 2.1.11)
  Transfer Manager, replacing LSF scheduling
    In production for ATLAS, to be deployed everywhere
  Basic VOMS support in SRM
Future developments (CASTOR 2.1.12 and beyond)
  Reduce file open latency
  Garbage collector logic improvements

## Slide 13
CASTOR tape interface
Recent changes
  Support for 5TB tapes
    In production at CERN and at RAL
  One tape mark per file as opposed to three
Future developments (2.1.12 and beyond)
  Towards improving support for the new tape drive families and their increased throughput
    Buffered tape marks and multi-file metadata handling
    Repack re-engineering to address scalability
  Media migration to start next year
    40PB to be moved from 1T to 5T tapes

## Slide 14
EOS evolution
EOS 0.1.0
  release candidate deployed in EOSCMS/EOSATLAS
EOS 0.2.0 (September/October)
  Redundancy CODECs
    dual parity & Reed-Solomon based give better file availability with less space usage
  Client bundle (Linux + OSX)
    user FUSE EOS mounting via KRB5 & X509
  Performance improvements in low-level FUSE client
EOS 0.x.0 ...some ideas to follow within next year
  HTTPS/HTTP Gateway
  Monitoring/Web Interface
  Layout Migration
    convert on the fly replica to CODEC files and vice-versa
  Extended FUSE Mount Daemon
    move part of the server code into the client (parallel IO + lower MD latency)
    policy-based persistent file page cache (for Software, Calibration, Geometry files etc...)
  policy-based file backup into CASTOR
  LAN/WAN Transfer Interface

## Slide 15: StoRM plans
Defined in the EMI 2 work plan
  WebDAV support
  ARGUS integration

## Slide 16: DPM
NFS 4.1 / pNFS
  Now functional beta, monthly releases, can be tried
  Short term: improve performance (heavy on metadata query), integration with dCache
  Medium term: X.509 support, investigate federations
WebDAV
  Beta release available for testing
  Short term: X.509 support in browser, help to improve HTTP support in ROOT, evaluate HTTP as alternative to GridFTP
  Medium term: help to improve common clients (e.g. curl)

## Slide 17: DPM (II)
Simpler system administration with Puppet
  Strong, widely supported solution
  first release available to sites
  Short term
    extend Nagios performance probes, add probes as needed
    Add reporting per storage area / virtual organization
  Medium Term
    Promote sharing of Puppet manifests among developers and site admins
DPM 1.8.2
  Better file system selection
  Improvements in the client connection pools for all daemons
  GLUE 2.0 support
  Faster draining of disk servers
  SEMsg support

## Slide 18: SEMsg: SE-catalogue consistency
Support integration with experiment frameworks
Support deployment of SEMsg-enabled LFC/DPM servers
Short term
  investigate more advanced security features (e.g. whitelisting)
Medium term
  Investigate other possible usages of the framework, e.g. sync among LFCs
  Support the developers of other SE products in using it
  Support Grid-wide deployment

## Slide 19: Checksum support (I)
BeSTMan
  MD5, ADLER32, CRC32
  Supports user-provided checksum
  Internal checksum calculations on-demand
    srmLs expensive if it involves checksum calculation
CASTOR
  Checksum recalculated by RFIO, GFTP and XROOT at each full file read/write
  Cannot be calculated on demand
  Stored for both disk and tape copies of files
  Checksum is checked against stored tape value when file is recalled

## Slide 20: Checksum support (II)
dCache
  ADLER32 (and MD5)
  Can be user-provided
  Calculated after writing a file
  Lazy checks on all files (from 1.9.13)
StoRM
  Checksum calculated either on the fly by GridFTP or on demand by the Checksummer service
  Checksum returned when present as file attribute

## Slide 21: Conclusions
All Tier-1 sites are well aligned to the most recent versions of the storage systems
All dCache sites plan to go for the new golden release by beginning of next year at the latest
Disk-only solutions are being deployed in parallel to traditional HSM systems
The main WLCG storage systems are still very actively developed
  Stronger support for common standards: NFS 4.1, HTTP support, WebDAV, etc.
  Increasing performance and scalability for both disk and tape layers

## Slide 22: Acknowledgements
Thanks to the Tier-1 contacts and to the storage system developers for providing the necessary input