## Slide 1: Time-to-digital converter (TDC) in CMOS technology – overview and design example
Juli 2023
Outline
Introduction
  Application
  Classification
  Types of sampling TDCs
  Characterization
Design Example
Summary

## Slide 2: Introduction
TDC
Precise time-interval measurements
Time-of-flight measurements
Act as phase detector in all-digital phase-looked loops (ADPLLs)
Positron emission tomography (PET)
Light detection and ranging (LiDAR)
…
Key components of time-mode circuits
Enablers for digital processing of analog signals encoded in time
  translates the analog time interval into a digital value
  digital signals are far more robust against noise and coupling than analog signals
Applications
Sampling TDC
Noise-shaping TDC
Stochastic TDC
Classification
J. Szyduczyński, D. Kościelnik, M. Miśkowicz,
Time-to-digital conversion techniques: a survey of recent developments.
Measurement, 214, 2023, 112762,
https://doi.org/10.1016/j.measurement.2023.112762.

## Slide 3: Introduction
Comparison
n-bit TDC
Start
Stop
1010…
Chart: x
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
y | 2 | 4 | 2 | 1 | 2 | 4 | 5 | 3 | 1 | 1 | 3 | 2 | 4 | 6 | 3
a | 0 | 2.2 | 3.8 | 2.3 | 1.1 | 1.9 | 4.1 | 5.4 | 3.2 | 0.8 | 0.7 | 2.6 | 1.8 | 3.9 | 5.6 | 3.4
TDC
ADC
∆t
∆tLSB
a sampler and a quantizer
  The sampler evaluates the input signal at discrete time instances.
  The quantizer maps the resulting continuous values to discrete ones.
  Both together result in a digital signal representation.
sampling
quantizing
Time-interval counting
LSB = least significant bit

## Slide 4: Introduction
Sampling TDC overview
coarse TDC
Counter TDC
direct time-to digital conversion
counting of clock cycles (< 1GHz)
for low time resolution > 1ns
large measuring range
fine TDC
for high time resolution < 1ns
small measuring range
analog
ramp interpolator
digital
delay lines
Vernier delay lines
Successive-approximation
Pulse-shrinking
Iconstant
C
Vramp
start/stop
reset
V
t
ADC
reset
Start/stop
Vramp
sampling
quantizing
TIn
TIn
N*TClk
∆TStart
∆TStop
S
R
Q
T0
T0
T0
S
R
Q
S
R
Q
T0
S
R
Q
TIn
Start
Stop
Successive delaying of start through a DL
Time comparator records the order in which the events arrive
Result in thermometer code
Notes: The analog-based TDC precision depends on the linearity of the TVC and the resolution of VDC .
Analog-based TDCs attracts less attention in modern CMOS processes because it does not take advantage of downscaling of CMOS technology.
The analog-based TDCs usually suffer from substantial power consumption, high cost due to large silicon area occupied by capacitors, large temperature drift, and decreasing voltage resolution.

## Slide 5: Introduction
Delay-line based TDCs
S
R
Q
T0
T0
T0
S
R
Q
S
R
Q
T0
S
R
Q
TIn
Start
Stop
Vernier delay lines
Successive-approximation
Pulse-shrinking
T‘0
T‘0
T‘0
T‘0
Resolution:
use of differential delays of two delay lines with slightly different propagation latencies (T0 and T’0)
Better resolution than delay line, but increased number of delay components
Tm
TSn-2=2n-2T0
Tm
S
R
Q
/Q
Tm
TRn-2=2n-2T0
Tm
Cn-1
bn-1
Cn-2
C1
C0
bn-2
b1
S
R
Q
/Q
b0
TIn
Start
Stop
Binary-weighted latencies enables reduction of number of conversion steps
Delaying 2 events by binary-scaled latencies, such that both events coincide in time at the end of conv.
Feedforward SA-TDC shown
sensitive to errors due to metastability of time comparator (RS-flipflop)
S
R
Q
S
R
Q
S
R
Q
TIn
Start/Stop
tr1, tf1
tr2, tf2
tr1, tf1
tr2, tf2
tr1, tf1
tr2, tf2
∆T
2∆T
TIn
Start
Stop
8T0
4T0
2T0
T0
<T0 (LSB)
b1
b0
b2
b3
b4
1
0
0
1
0
achieving a sub-gate delay TDC resolution
TIn in the form of a pulse is gradually shrinked until it ceases to exist
unit cells with the different rising (tr) and falling (tf) transition time
Notes: Metastability is a general problem of TDCs of any type. But in the SA-TDCs, the metastability implies gross conversion errors especially if it occurs at the evaluation of one of the most significant output bits. By comparison, in the delay line TDCs with uniform delays, the metastability results in the possible error just on the state of the LSB.

## Slide 6: Introduction
TDC performance characterization – Nonlinearity
DNL
differential nonlinearity
Deviation of the step width from the ideal value
Transfer function response
Ramp input

## Slide 7: Introduction
TDC performance characterization – Nonlinearity
INL
integral nonlinearity
Deviation from a linear fit or
deviation of code transitions from their ideal values
→ cumulative sum of DNL
INL = 0.4 LSB
INL = -0.9 LSB
Transfer function response
INL = 0 LSB
Ramp input

## Slide 8: Design in 130-nm CMOS Process from Global Foundry
Combination of delay-line locked loop TDC and counter TDC
Multi-level TDC
  5-bit fine and 7-bit coarse TDC
  DLL as fine TDC: 32 elements delayline in a loop, locked to a reference clock
  Ripple Counter as coarse TDC: increments after each DLL cycle
Encoder
DLL output is in thermometer code
Encoder output in binary code
ref
del
up
down
Phase-Frequency
Detection
Clock
Frame reset

## Slide 9: Design in 130-nm CMOS Process from Global Foundry
Output
20-ps time conflict, caused by registers setup/hold time
20-ps long spike of 32 bins
    TDC is designed for target frequency 408 MHz
    small bug, caused by registers setup/hold-time
    mean bin width (77.2 ps) is in good agreement with ideal value (76.6 ps)
    upper limit ≤450 MHz
+1
Solution: include delay

## Slide 10: Design in 150-nm CMOS Process from LFoundry
Combination of delay-line locked loop TDC and counter TDC
    Delay include
    Incrementation after first delay element
    Modification in encoder for the case that DLL doesn’t work properly
resulting transfer function

## Slide 11: Design in 150-nm CMOS Process from LFoundry
Combination of delay-line locked loop TDC and counter TDC
    Delay include
    Incrementation after first delay element
    Modification in encoder for the case that DLL doesn’t work properly
            This case happened
only 25 fine bins
resulting transfer function
vulnerable to PVT variations

## Slide 12: Design in 150-nm CMOS Process from LFoundry
Output
bin width

## Slide 13: Design in 150-nm CMOS Process from LFoundry
Layout
DLL
Delay line
78 µm
157 µm
Latches
Phase-Frequency Detector
Charge pump with Loop Filter
Encoder
Register
synthesized Thermometer-to-binary Encoder
Counter
Data serializer

## Slide 14: Summary
TDC
Overview of TDC types
Many applications for HEP experiments
Design example for dSiPM project
TDC design is challenging
Measurements can differ from simulations