## Slide 1: Experience with cell experiments at ARES
Logistics, challenges, points for discussion.
Florian Burkart
on behalf of the ARES team: Hannes Dinter, Frank Mayet, Sonja Jaster-Merz, Max Kellermeier, Willi Kuropka, Blae Stacey, Thomas Vinatier
with input from Elisabetta Gargioni, Nina Struve, Joel Senador (UKE)

## Slide 2: The ARES Linac at DESY
Present – Final Layout and Status
ARES goal: Generate and characterize ultrashort e- bunches (fs to sub-fs) with high stability for applications related to accelerator R&D and beam time for external R&D users.
~45 m
S-Band
Gun
Gun Diagnostics
S-Band
Traveling Wave Structures (TWS)
Experimental Area 1
Experimental Areas 2&3
Bunch Compressor
X-Band PolariX TDS (2 Cavities)
High Energy Spectrometer
Parameter | Target | Status
Charge | 0.05 - 200 pC | 0.003 - 200 pC
Momentum | 50 - 150 MeV/c | 20 - 160 MeV/c
Momentum Spread | 10-4 | 10-4 (res. limited)
Transv. Norm. Emittance | < 0.8 µm.rad | ≈ 0.07 µm.rad
Bunch Length (rms) | Sub-fs to ~10 fs | ≈ 2.9 fs (VB ¦¦ BC)
Design start (incl. removal of DORIS): 2014
Construction start: March 2018
First beam (gun section): October 2019
ARES fully installed: April 2023

## Slide 3: Medical applications
New challenges in 2021
FLASH RT
VHEE
Medical imaging
The accelerator phycisist
In-vivo experiments

## Slide 4: Logistics & Infrastructure

## Slide 5: Three Experimental Areas for Users
Full Flexibility
In UHV (~7e-10 mbar), highest precision,
best beam control.
In air, highest flexibility.
In low pressure vacuum, detector test stand.

## Slide 6: S2 Bio lab
Now available for medical experiments at ARES.
provides all the necessary equipment to cultivate, store, manipulate and analyse biological agents
Work place in the Bio-Laboratory.
inverse fluorescence microscope.
BSL2 safety workbench equipped with a mini centrifuge, vortexer, vacuum pump,…
More info:
https://photon-science.desy.de/facilities/on_site_infrastructure/laboratories_technical_infrastructure_shift_service/biology_laboratory_bsl_2/equipment/%20index_eng.html
photo by courtesy of M. Osterhoff

## Slide 7: Locations on the DESY campus
5 min walking distance from Lab to ARES
FLASH
PETRA III
DESY II
EuXFEL
FLASH II
SINBAD
ARES Linac
KALDERA

## Slide 8
Research and Development at ARES
Online dosimetry and cell irradiation
Experimental station designed for medical research
Up to 160 MeV high precision electron beams for research & development.
  Cutting-edge stability of the electron pulse energy
  Excellent beam control and highest flexibility in beam parameters
  In-vivo experiments possible
Ideally suited for VHEE & FLASH RT studies, dosimetry and medical imaging.
Collaborations started with UKE, Uni Manchester and Uni Wollongong
ARES, a worldwide unique facility for medical research
First living cancer cells treated with VHEE.

## Slide 9: Challenges

## Slide 10: Completely new field for us
How to translate electrons to dose?
Medical side ~ translator ~ accelerator side
But:
What is the „right“ dose?
  Integrated dose
  Dose rate
  Dose rate/pulse
  How do we measure dose (fast!)

## Slide 11: How to hit the cells?
Preparation in the lab and transport to ARES is not an issue.
Bringing the cells in the tunnel is also not a problem (special access mode to keep most of the accelerator parameters).
Part 1
Eppendorf tubes are not Eppendorf tubes.
Different holder systems from DESY and UKE
Combination with online dosimetry.

## Slide 12: How to hit the cells?
ARES is limited in the amount of charge we can produce / transport.
Small spot size, where we can achieve FLASH like beam parameters.
Cells need to be prepared very carefully.
We have to rely on dosimetry!
Still the issue remains: are we sure that we hit the cells with the right dose?
Different irradiation patterns: Spot (FLASH like parameter) vs. Snake pattern (uniform distribution) irradiation
Part 2

## Slide 13: Studies with all types of samples
Studies for tumor treatment with high energetic electrons and FLASH parameters in collaboration with UKE and Uni Wollongong.
Mosfet detectors from Uni Wollongong as online dosimetry.
Animal and skull phantoms and living tumor cells.
Dosimetry development for medical applications with D3

## Slide 14: The solution for (almost) everything
ARES upgrade for more charge
Our RF structure
1.5 mu sec
10 – 50 Hz rep. rate
We want to place more bunches on our RF flat top

## Slide 15: The solution for (almost) everything
ARES upgrade for more charge
Our RF structure
1.5 mu sec
10 – 50 Hz rep. rate
We want to place more bunches on our RF flat top.
Looking for funding possibilities.

## Slide 16: Summary / Discussion
Fruitful collaboration with DESY and UKE.
  Many beam times
  Joel Master thesis
  Bringing together also radio protection and detector developers
  Successful project for novel online dosimetry.
Getting the dose right is a challenge.
Very tight budgets on DESY side  limits in availability in 2024/2025.
Looking for funding possibilities.
Looking for inspiring discussions also here at the workshop.