## Slide 1: Simulation-based optimization of the injection of ultrashort non-Gaussian electron beams into a storage ring
Jens Schäfer,
M. Fuchs, B. Härer, R. Ruprecht, M. Schwarz, M. Schuh, C. Xu

## Slide 2: Content
Motivation cSTART and Injection Line (IL)
Challenges and solving strategies
Longitudinal compression
Transverse Matching
Jens Schäfer (et al.) KIT – IBPT

## Slide 3: cSTART motivation
  compact STorage ring for Accelerator Research and Technology
  Injection and storing of ultrashort LPA beams
  Opportunity to study non-equilibrium beam physics
  FLUTE as 2nd injector for comparison
  Development since initial IL design
  Conceptual initial design laid the foundation of IL
  cSTART advanced towards Final Design Report stage
  Advanced IL simulations required:
      Addressing technical constrains (space claims)
      Solutions for different beam parameter and optics
      Speed up simulation time from months to days
cSTART:
  LPA‘s
  FLUTE
  Injection Line (IL)
  Storage ring (VLA-cSR)

## Slide 4: 0verview
  FLUTE: bunch creation up to 90 MeV
  IL1: vertical arc around storage ring
  IL2: tilted DBA into the horizontal plane
  IL3: matching section and injection
  VLA-cSR: cSTART storage ring
# | Magnets
14 | Dipoles
32 | Quadrupoles
4 | Sextupoles
1 | Septum
1 | Kicker
          Injection Line Challenges
  Tight geometrical constrains
  Handling vertical, horizontal and tilted deflections
  Longitudinal bunch compression to femto-seconds!
  Transverse matching to storage ring
  Coping with non-linear effects and xy-coupling
  Adaptable for a parameter range (q, E, chirp …)

## Slide 5: Bunch compressor
  FLUTE Bunch compressor (FL_BC) delayes low-energy electrons
  The BC “shears” the long. phase space counter-clockwise by R56
  A bunch with a positive chirp h compresses
  Transporting ultrashort bunches leads to intense CSR bursts, energy loss and particle losses.
  A fs-bunch cannot be transported through the IL!
positive
chirp
h > 0

## Slide 6: Initial chirp
  IL designed to compress the bunches just at the septum.
  FLUTE linac operation on “opposite flank” for a negative chirped bunch.
          IL phase space operation
  Starting with a negative chirp
  Bunch elongates first in BC & IL1 (R56<0)
  and compresses in IL2 & IL3 (R56>0)
       No ultrashort bunches during transport.
positive
chirp
h > 0
Negative
chirp
h < 0
h < 0
h > 0

## Slide 7: Strategy towards an optics solution
  Compose the TL out of achromatic sections: η=0 before/after section
  Only Quads at η≠0 influence long. Dynamics
  All Quads influence transverse dynamics
  Optics discussion:
  1. solve long. compression in η≠0 sections
  2. solve transverse matching in η=0 sections

## Slide 8: Full compression condition
  Bunch chirp transforms by R56
  Initial chirp: h-1(S1) = -2.8 cm-1
  Full compression: h-1(S2) = 0 cm-1
  Full compression condition (FCC):
  The sum of all R56 values have to counteract the initial chirp
  BC, IL2 & IL3 have limited margin in R56
  IL1 designed for flexible R56 value
Section | Structure | R56 / cm
BC | BC | -2.5
IL1 | HBA | [-420; +130]
IL2 | DBA | +3.4
IL3 | DBA | +20.1
ToF |  | -0.4

## Slide 9: IL1 optics with NN
  Investigating the full parameter volume of possible optics
      IL1 optics serves 9 quadrupoles
      5 individual quadrupoles, considering mirror symmetry
      4 open DoF, considering achromaticity
  4 input parameter: K1-values of quadrupoles: A3, A4, B2, B3
  For one set of inputs, several optic functions are calculated, e.g. R56 and Twiss functions max values  10 outputs
  Repeated for different input combinations  created ~ 16.000 different input/output pairs
  This data is used for training a NN* and constructing a surrogate model (SM).
  SM prediction has high accuracy: Pearson correlation coefficient > 0.99 for 6/10 outputs, e.g. R56
  SM allows for an investigation of complete parameter volume with only 16.000 simulations, taking minutes instead of days!
*PyTorch: 6 layers, 32 neurons fully connected, feedforward, min-max-normalized, rectified linear unit (ReLU) activation function, Adam optimizer, 9:1 training:evaluation

## Slide 10: Transverse Optics
  Remaining quadrupoles utilized for
      Beam transport (FLUTE, IL1, IL2)
      Matching (IL2, IL3) with 6 quadrupoles
  6D tracking shows non-gaussian bunch shape at injection point due to IL2 rotation and higher order effects
      Matching optimization based on expensive 6D tracking,
      NN training not feasible
      Ideal for Bayesian Optimization (BO)
  BO implementation in python with xopt
  Fully customizable optimization function f
      Calculation of matching parameter : (𝛽x,y , 𝛼x,y , 𝜂x,y ) directly from 6D particle distribution
      trimming of long non-gaussian tails
          Work in progress…
Transport Transport Matching

## Slide 11: Summary
BO implemented for Matching
Approach for coping with non-linearities
No ultra-short bunches during transport
  Full compression condition (FCC)
NN & SM make IL1 optics for entire parameter volume accesible
Allows fast investigation and finally formulating for optimization criterions

## Slide 12: Summary & Outlook
BO implemented for Matching
Approach for coping with non-linearities
          Further ingeneering on optimization function f required
No ultra-short bunches during transport
  Full compression condition (FCC)
NN & SM make IL1 optics for entire parameter volume accesible
Allows fast investigation and finally formulating for optimization criterions
          Adding higher order dynamics to the SM

## Slide 13: Backup Slides

## Slide 14: Backup: IL1 optics
  IL1 optics are calculated independent of surrounding IL.
  Considering Mirror symmetry, IL1 optics have 5 open DoF: K1-strengh of quadrupoles: A3, A4, AB, B2 and B3.
  For a given set of K1-values, the twiss parameter and dispersion are defined by:
  1 DoF (quadrupole AB) is set to met achromaticity:
  Remaining DoF are considered Input: A3, A4, B2, B3
  A set of output parameters is calculated:
  These instructions are used to create a dataset of ~16.400 input/output pairs.
  A data selection is applied:
  The remaining 6,400 input/output pairs are used to train a feedforward Neural Network*.
*PyTorch: 6 layers, 32 neurons fully connected, min-max-normalized, rectified linear unit (ReLU) activation function, Adam optimizer

## Slide 15: Backup: BO optimization function
  BO Implementation in python with xopt
  allows for a custom optimization function:
  minimization of
    L: beam losses in %
    mi: Matching metric for each parameter Vi: (𝛽x,y , 𝛼x,y , 𝜂x,y )
      mi = sene(V1, V2 ) (soft-edge not equal), sensitivity function
      Distance between V1 (desired value in VLA-cSR) and V2 (injected)
      V2 calculated directly from macro particle distribution
      Allows for advanced pre-processing, e.g. outlier handling