## Slide 1: Bunch shape and longitudinal measurements for non-relativistic beams at GSI LINAC
Nimue Schmidt

## Slide 2: GSI/FAIR Overview
Helmholtz Centre for Heavy Ion Research
Founded 1969
Facility for Antiproton and Ion Research
[2] https://www.gsi.de/en/researchaccelerators/fair/the_machine
[1] https://www.gsi.de/forschungbeschleuniger/beschleunigeranlage/linearbeschleuniger
Notes: Alvarez

## Slide 3: UNiversal Linear ACcelerator
Acceleration of Ions from Protons up to 92-fold ionised Uranium
Pulsed operation: 50 Hz
RFQ & IH: 36.136 MHz
Alvarez & ER: 108.41 MHz
Multi-Experiment Beam Sharing
[3] https://www.gsi.de/work/beschleunigerbetrieb/beschleuniger/unilac/unilac
Notes: operated without acceleration: any arbitrary ion energy between 3.4 and 11.6 MeV/u = 16% speed of light,
Commissioning 1975
Sources Terminals can be equipped
Possible switching of beam parameters between two subsequent beam pulses
UNILAC experts

## Slide 4: Motivation
Why do we need Longitudinal Diagnostics?
Matching to Acceptance of RF-Structures
Controlling Energy Spread
  Minimized at Injection to SIS-18
[3] https://www.gsi.de/work/beschleunigerbetrieb/beschleuniger/unilac/unilac
Notes: Whole longitduinalt PS was not measured in a long time

## Slide 5: Longitudinal Beam Diagnostic Devices
FFC
BSM
GTR
Measurement of Longitudinal Phase Space
Fast Faraday Cup (FFC)
Bunch Shape Monitor (BSM)
GHz Transition Radiation monitor (GTR) [4]
Phase Probe [4]
[3] https://www.gsi.de/work/beschleunigerbetrieb/beschleuniger/unilac/unilac
[4] Rahul Singh (Nov 2022). LONGITUDINAL BEAM DIAGNOSTICS R&D AT GSI-UNILAC, DOI:10.18429/JACoW-HIAT2022-TH2I2
Notes: Link to GTR Paper Rahul

## Slide 6: Fast Faraday Cup
Destructive Bunch-by-Bunch Method
  Longitudinal Bunch Shape
Radially Coupled Coaxial Fast Faraday Cup (RCFFC)
  30 ps Resolution
  5 GHz Bandwidth at β = 15%
[6] R. Singh et al. (2022) Simulation and measurements of the Fast Faraday Cups at GSI UNILAC, doi:10.18429/JACoW-IBIC2022-TUP25
[5] R. Singh et al. (2021). Comparison of Feschenko BSM and Fast Faraday Cup
with low energy ion beams, DOI: 10.18429/JACoW-IBIC2021-WEPP16
[7] R. Singh et al. (June 2022). Longitudinal beam diagnostics R&D at GSI UNILAC, HIAT 2022, Darmstadt
Notes: Faraday Cup: current  same but whole lot quicker
Provide a small hole from the side of a co-axial into central conductor
Fermi 5 GHz at 15%c, around 30ps, 4 degrees at 108 MHz

## Slide 7: Recent Measurements
GTR
[3] https://www.gsi.de/work/beschleunigerbetrieb/beschleuniger/unilac/unilac
IH1
IH2
β = 0.05473
β = 0.03995
β = 0.15591
FFC
BSM
Notes: Gasstripper region,
IH1: beta 3.995 == 743keV/u
IH2: 5,473 == 11.4 MeV/u

## Slide 8: Recent Measurement
Measurement in X2
Notes: November
IH1: beta 3.995 == 743keV/u
IH2: 5,473 == 11.4 MeV/u

## Slide 9: Recent Measurement
Measurement in X2
Notes: November
IH1: beta 3.995 == 743keV/u
IH2: 5,473 == 11.4 MeV/u
SE suppression (geometrical, apply Bias voltage )

## Slide 10: Recent Measurement
Measurement in X2
Notes: 2025_04_02_CH1_HF_CH2_fFFC_CH3_current_CH4_PP_E10_6.5V_249deg_Ar8_Set1_Bias220V_fFFC_Pos162.5mm_001_ch2
SE suppression (geometrical, apply Bias voltage )

## Slide 11: Recent Measurement
Measurement in X2
Notes: 2025_04_02_CH1_HF_CH2_fFFC_CH3_current_CH4_PP_E10_6.5V_249deg_Ar8_Set1_Bias220V_fFFC_Pos162.5mm_001_ch2
SE suppression (geometrical, apply Bias voltage )

## Slide 12: Emittance Measurement
Measurement of Dispersion-assisted Longitudinal Emittance
Notes: 1 dimension of long phase space, whole & emittance
Second axis == deviation in momentum/energy
Allocate x - p

## Slide 13: Emittance Measurement
Measurement in X2

## Slide 14: Emittance Measurement
Measurement in X2
Dispersion Measurement
  5.03 m

## Slide 15: Emittance Measurement
Measurement in X2

## Slide 16: Longitudinal Beam Diagnostic Devices
[3] https://www.gsi.de/work/beschleunigerbetrieb/beschleuniger/unilac/unilac
GTR
FFC
BSM
Measurement of Longitudinal Phase Space
Fast Faraday Cup (FFC)
Bunch Shape Monitor (BSM)
GHz Transition Radiation monitor (GTR) [4]
Phase Probe [4]
[4] Rahul Singh (Nov 2022). LONGITUDINAL BEAM DIAGNOSTICS R&D AT GSI-UNILAC, DOI:10.18429/JACoW-HIAT2022-TH2I2

## Slide 17: Bunch Shape Monitor (BSM)
Secondary electrons liberated from a wire (0.1mm, 10kV)
Accelerated towards rf-deflector
  Same Frequency as accelerating RF
  Time-to-space converter
Electron detection behind slit with
  SEM (Secondary electron multiplier)
  FC (Faraday Cup)
Change of phase of deflecting RF
  Scanning of whole bunch
Resolution of 1 degree, 26 ps
[8] P. Forck (2024). JUAS Lecture notes on beam instrumentation,
DOI: https://doi.org/10.23730/CYRSP-2024-003
Notes: Difference to FFC: non destructive, average over multiple bunches

## Slide 18: Bunch Shape Monitor (BSM)
Plots from X2 measurement

## Slide 19: Bunch Shape Monitor (BSM)
Plots from X2 measurement

## Slide 20: Bunch Shape Monitor (BSM)
X2 measurements, Buncher at 2.0 V
Different wire positions
Notes: Bunch not gaussian like at some positions (other part of bunch)

## Slide 21: Summary & Outlook
Fast Faraday Cup
  Destructive, Bunch-by-Bunch Method for Bunch Shape Measurement
  30 ps, 4 degrees Resolution @108 MHz with electronics + 40 mm cables
    Improvements planned to reach 2 degrees
Bunch Shape Monitor
  26ps, 1 degrees Resolution
Dispersion-assisted Longitudinal Emittance
  Dispersion is sufficiently high in X2
  Demonstration of the Method’s Functionality
  Calculation of the Emittance
Comparison measurement with BSM
  Moving wire to scan phase space
Notes: Next FFC resolution 2 degree , smaller hole and moving osci closer to FFC  Improvement

## Slide 22
Many thanks to all the Physicists involved!
Prof. Dr. Winfried Barth
Dr. Maksym Miski-Oglu
Dr. Rahul Singh
Stephan Klaproth
Dr. Peter Forck
Uwe Scheeler
Dr. Simon Lauber
Dr. Thomas Sieber
Dr. Timo Milosic
…and many more

## Slide 23: Backup slides

## Slide 24: Difficulties
Hitting cable in Gasstripper FFC
Bunch movement
  In phase
  Amplitude change in Macropulse
Notes: BACKUP

## Slide 25: Difficulties
Hitting cable in Gasstripper FFC
Bunch movement
  In phase
  Amplitude change in Macropulse
Notes: LATER/BACKUP

## Slide 26: Emittance Measurement
Measurement in X2