## Slide 1: ARES Operation Meeting
Summary of week 35 / 2023
Willi Kuropka, on behalf of the ARES crew

## Slide 2: ACHIP
Over the weekend: Gun RF station conditioning, stable charge voltage could be improved
Monday: MKK work, 74MV/m gun gradient restored
Tuesday: Check and readjust laser on table, transmission to IP improved!, On-crest WP established
Wednesday: Stage 0 modulation achieved!
Thursday: D3 NitroFlash detector with Oliver
Friday: AutoAcc shift, On-crest WP for ACHIP restored
Weekend: improved ACHIP modulation by aligning laser, established velocity bunching WP with relatively stable transmission, but no interaction achieved, yet

## Slide 3: Modulation result wednesday
Again with 74MV/m gun gradient WP
Less modulation, but very clear signal
Aligning the laser with the Cherenkov light on the observation cam appears to work reasonably well

## Slide 4: Gated camera timing works very well!

## Slide 5: Very clear modulation signal
Improved modulation on weekend, ca 1mJ laser power on the last lens
Laser off
Laser on

## Slide 6: Very clear modulation signal
Improved modulation on weekend, ca 1mJ laser power on the last lens

## Slide 7: Spectrum of velocity bunching WP

## Slide 8: Schedule this week
MCS server updates
MKK commissioning of the precision water cooling for the X-band system