## Slide 1
Alessio Rettaroli
alessio.rettaroli@lnf.infn.it
COST Action COSMIC WISPers (CA21106) Working Group Meeting
1 - 2 Feb 2024 DESY, Hamburg
Recent results of QUAX @ LNF

## Slide 2
The QUAX experiment is a light DM hunt experiment
a
g
Photon detector
Axions from DM halo
LNF (Frascati)
LNL (Legnaro)
Classical haloscope (just like ADMX, HAYSTAC etc)
Searching for QCD axions
Between GHz

## Slide 3
QUAX timeline
2017
2018−2019
2022
2020−2021
2023
2024
→2025
2024
→2025
Proposal
First
measurements
QCD band
Almost KSVZ with TWJPA
QCD band
with Photonic cavity
First scan with tuning rod
2 GHz Scan experim.

## Slide 4
Group and lab are enlarging

## Slide 5
Haloscope ingredients
Dilution refrigerator
Low noise receiver
Microwave resonant cavity
SC magnet
Tunable frequency
Ongoing
Already purchased
Recent Achievements
Recent Achievements

## Slide 6
QUAX@LNF first axion search with tuning rod mechanism

## Slide 7
Dilution refrigerator
Temp. of 10 mK plate
Leiden Cryogenics
Cooling power
Cavity temperature

## Slide 8
9 T magnet
Anchored to 4 K stage
Reached 9 T
Took data at one freq with 9 T
Quench
Ramp to 8 T ok
Took data with 8 T stably for 2 weeks

## Slide 9
Microwave cavity + tuning
OFHC Copper
Radius = 13.5 mm, height = 246 mm
TM010 mode
Starting frequency (): 8.83 GHz
Tuning MHz with
HFSS simulations by Simone Tocci

## Slide 10
Microwave cavity + tuning
Expected from simulations, and measured w/out rod
Measured w/ rod
This is likely due to losses caused by the rod configuration and PEEK
Trapped field between metallic disk and cavity endcap

## Slide 11
Rod and antenna movimentations
Frequency vs rod position
6 MHz for this run
1 linear motor for Antenna
1 rotative motor for Rod

## Slide 12
Amplification chain
Coming soon:
FPGA
2 MHz ADC
LO
low-noise cryogenic HEMT
4 K
300 K
FET
low-freq Voltage ampli
I-Q mixer
RF
LO
I
Q
16 bit
Tot eff. Gain = 116 dB
Noise Temp = 4.5 K
Coming soon:
JPA

## Slide 13
Calibration + spectrum
Fits by Gianluca Vidali (student)
cavity
LO
From fit we extract , , ,
Fit procedure
Raw power spectrum
GHz
= 0.5
C010 = 0.667
T (Bav=6.5 B0)
mK
From calibrated power spectrum we extract the noise temp

## Slide 14
6 MHz tuning
6 MHz scan
, and remain stable
Effective scan rate in this test: 220 MHz/year
Performed the same procedure on each run

## Slide 15
Analysis
Analysis procedure by Alessandro D’Elia
Fit to power spectra with Savitzky-Golay filter to calculate residuals
Maximum likelihood over all scans to estimate the best value
Calculate the efficiency of the SG filter by Monte Carlo simulations with fake axion signal ()
Example of power spectrum with SG fit
Cumulative normalized residuals over all scans

## Slide 16
Final plot -
QUAX@LNF this run
Touched the QCD line
Avg value
PRELIMINARY

## Slide 17
Bonus: superconducting cavities
cavity by FNAL
at 9T
ReBCO-tapes cavity
Q_loaded

## Slide 18
Next
Qubit photon detector*
JPA, fabrication by FBK
Optimization of tuning rod
Superconducting cavities
FPGA for acquisition
*S. Kono et al; Nature Phys 14, 546–549 (2018)

## Slide 19
Conclusions
First QUAX@LNF run with complete haloscope
  2 weeks of data taking.
  9 T magnet. Operated at 8 T.
  Tuning rod to scan frequencies.
Savitzky-Golay + Maximum Likelihood analysis.
Still much room for improvements.
QUAX competitive in the panorama.

## Slide 20
backup

## Slide 21
Figures of merit in a haloscope
The signal power is very faint
The scan rate depends critically on noise temperature

## Slide 22
L1
L2
L3
L5

## Slide 23
All calibrated scans
Calibration of downconversion hardware