## Slide 1
Gravitational wave vertical cryostat

## Slide 2
Pressure–temperature phase diagram of helium 4
arXiv:1307.8286 (2013)
Several phases are possible in the heat transfer to helium: superfluid He II, Solid, liquid, and vapor

## Slide 3
Properties of superfluid helium 4
SF He
Specific heat of liquid helium at saturated vapor pressure:
Specific heat of He 105 times higher than Cu conductor by unit mass
Lambda-discontinuity in specific heat capacity of liquid helium
In between 1.1 K and 2.17 K, (where as for a metal - )
Change in dominated by rotons and not by phonos
Cu
LHe
Thermal conductivity of liquid helium as functions of and :
Very sensitivity to pressure below 10 K and at higher pressures exhibiting increased thermal conductivity (keeping the bath at 1 atm could be a better solution).
Thermal conductivity over all 103 times that of OFHC copper
Steven W. Van Sciver, Helium Cryogenics (2012)
Cu

## Slide 4
Properties of superfluid helium 4
Steven W. Van Sciver, Helium Cryogenics (2012)
Specific heat dominated by rotons between 1.1 and 2.1 K and not by phonons
Due to strong temperature dependence, the superfluid component composes about 99% of He II at 1 K.

## Slide 5
Steven W. Van Sciver, Helium Cryogenics (2012)
Russell J. Donnelly, Physics Today 62, 10, 34 (2009)

## Slide 6
General superfluid (SF) helium properties
First sound wave: SF helium has an exceptionally low sound wave speed of 238 m/s.
Excitations: It also shows unique kinds of excitations, such as quantized vortices, and second and third sound waves.
Density: The low density (ρHe = 145 kg/m3) and effective mass of SF helium contribute to a high zero-point fluctuation (ZPF) amplitude, resulting in significant optomechanical/electromechanical coupling.
Dielectric constant: The dielectric constant of SF Helium is 1.057, indicating that it is a low-loss dielectric medium. This characteristic results in minimal light absorption or scattering, which leads to low optical loss.
Viscosity: The absence of viscosity in SF helium results in a very low sound attenuation (acoustic loss proportional to T4 ), which contributes to high mechanical quality factor.
Thermal conductivity: The high thermal conductivity of SF helium prevents any heating issues from RF/optical powers.
Band gap: Helium II does not exhibit linear absorption visible of infrared light, due to its large bandgap (19.9 eV), and the lack of chemical impurities which freeze to the walls of the container.
Tuning tool: SF helium can be employed as a tuning tool for resonators, allowing adjustments to the effective mass and resonance frequency.
In conclusion, the combination of low intrinsic absorption and the large thermal conductivity of superfluid helium contributes to improved RF/optical power handling.

## Slide 7
Steven W. Van Sciver, Helium Cryogenics (2012)
Production of 2 K superfluid helium via isenthalpic expansion
Considering an isenthalpic expansion of helium from 0.1 MPa, 4.2 K to 1.6 kPa corresponding to the saturated vapor pressure at 1.8 K
liq.
gas

## Slide 8
Joule-Thomson valve
((liq. He )
(liq. He + gas He)
After the expansion of liquid helium (LHe) from high pressure to low pressure through the JT valve, the resulting helium exists in both liquid and gaseous phases, while conserving enthalpy across the valve:
=
Here, , and represent the mass flow rates of the inlet liquid, outlet liquid, and outlet gas, respectively. Meanwhile, , and are the inlet enthalpy of helium, the outlet enthalpy of gaseous helium, and the outlet enthalpy of liquid helium, respectively.
/ = ( / (
In addition, the fraction of mass flow liquefied or yield is defined,
J. Phys.: Conf. Ser. 969 012084 (2008)
/
Furthermore, the mass flow rate through the JT valve is determined by
= . Consequently,

## Slide 9
Lambda plate in the Claudet bath

## Slide 10
FRESCA2 cryostat at CERN

## Slide 11
FRESCA2 cryostat at CERN

## Slide 12
3-LHC-Cryogenics-design-and-operation-optimization

## Slide 13
four-stage LHC cold compressors
Cold hydrodynamic helium compressors

## Slide 14
http://arxiv.org/abs/gr-qc/0502054v1

## Slide 15
1
General description of HB Box, H1 Box and ACPS in HERA North Hall

## Slide 16
Cold valves in ACPS Transfer line 3
Valve | Function | Type | DN | Kvs – for vendors | Kvs – max. valve lift (calculated) | Services | Tmin, K | PN, bar | Ps, bar | Tin, K | m, g/s | Pin, bar | DP, bar
ACPSVC2140 | ACPS TL3 4K supply | Control, NC | 15 | 3.24 – 4.33 | 2.88 – 63 % | Liq. serv. | 4.5 | 25 | 20 | 6.13 | 10 | 3.5 | 0.050
ACPSVC2240 | ACPS TL4 4K return | Control, NC | 20 | 6.9 – 7.8 | 6.12 – 63 % | Liq. serv. | 4.5 | 25 | 20 | 6.13 | 10 | 1.3 | 0.050
ACPSVC2240 | ACPS TL4 4K return | Control, NC | 20 | 7.8 – 9.5 | 7.02 – 63 % | Gas serv. | 4.5 | 25 | 20 | 6.13 | 10 | 1.3 | 0.050
ACPSVC2245 | ACPS TL4 4K cooldown | Control, NC | 25 | 14.7 – 15.6 | 13.66 – 84 % | Gas serv. | 4.5 | 25 | 20 | 300 | 20 | 1.8 | 0.50
4K/5K cold valves:
40K/80K cold valves:
Valve | Function | Type | DN | Kvs – for vendors | Kvs – max. valve lift (calculated) | Services | Tmin, K | PN, bar | Ps, bar | Tin, K | m, g/s | Pin, bar | DP, bar
ACPSVC3140 | ACPS TL4 40K supply | Control, NC | 10 | 1.73 – 2.16 | 1.40 – 76 % | Gas serv | 40 | 25 | 20 | 55 | 10 | 14 | 0.40
ACPSVC3240 | ACPS TL4 40K return | Control, NC | 15 | 2.60 – 3.24 | 2.37 – 76 % | Gas serv. | 40 | 25 | 20 | 80 | 10 | 14 | 0.20
ACPSVC3245 | ACPS TL4 40K cooldown | Control, NC | 20 | 6.9 – 7.8 | 5.26 - 63 % | Gas serv. | 300 | 25 | 20 | 300 | 15 | 7 | 5.7

## Slide 17
Flow scheme of GW vertical cryostat (GWVC)
ACPS
GWVC

## Slide 18
Flow scheme of GW vertical cryostat
helium transfer lines (4.5KF, 5KR, 40KF and 80KR)
vacuum vessel
40K/80K thermal shield
sub-atmospheric low pressure manifold 30 mbar and 2 K
U-shape copper liquid-liquid heat exchanger tube
JT valve 1 for producing LHe @ 4.2 K and 1 bar
JT valve 2 for producing SF helium @ 1.8 K and 16 mbar
2K low pressure heat exchanger
high pressure manifold line (300K, 12 – 16bar)
G-10 insulating tube/lambda tube
liquid He bath @ 4.2 K and 1 bar
SF He bath @ 1.8 K and 16 mbar
low pressure manifold (cooldown/warm-up)
cavity support plate
vibration isolation
SRF cavity
PZT actuator
Vacuum pump line
radiation shields
JT valve 3 for producing SF He @ 1.8 K and 16 bar

## Slide 19
U-shape copper HeII - HeII heat exchanger tube
JT valve 2 for producing SF He @ 1.8 K and 16 mbar
2K low pressure heat exchanger
Heat exchangers and JT valves
JT valve 1 for producing LHe @ 4.2 K and 1 bar
JT valve 3 for producing SF He @ 1.8 K and 16 bar

## Slide 20
two phase He@ 1 bar & 4.2 K
one phase SF He@1 bar & 1.8 K
two phase SF He@ 16 mbar & 1.8 K
Two phase SF (flowing) and one phase helium (static) in GWVC
With one phase helium, it‘s easy to avoid bubble formation and other instabilities like TCOs, TFs, etc.

## Slide 21
Design and thermal calculations for GWVC heat exchangers
U-shape copper HeII - HeII heat exchanger tube
counter flow low pressure liquid HeI- vapor HeII heat exchanger

## Slide 22
Vibration isolation
arXiv:2305.01419
PHYSICAL REVIEW ACCELERATORS AND BEAMS 22, 052002 (2019)

## Slide 23
Operation modes
"Warm-up and cool-down of experiments between 300 K and 1.8 K with certain temperature gradients.
Controlled production of both single-phase (at 1 bar) and two-phase (at 16 mbar) superfluid helium at 1.8 K using JT valves and heat exchangers.
The thermal shield is cooled down using helium supplied at 40 K and under 14 bar.
Pressure regulation inside the cryostat is achieved through the opening and closing of control valves.
In the event of a vacuum breakdown, helium is collected via a safety device.
The cold mass can be in direct contact with both single-phase and two-phase superfluid helium.

## Slide 24
Heat load budget and helium mass flow rate for the GWVC

## Slide 25
Heat load budgets for the GWVC
LHe @ 4.2 K & 1.0 bara
SF He @1.8 K and 1 bar
thermal radiation
vacuum vessel@300 K
thermal shield@40 K
MAGO cavity
support structures
penetration, convection, electric connections, etc.
RF power dissipation

## Slide 26
Static RF heat load to SRF cavities in the GWVC
Surface resistance: The Bardeen, Cooper and Schrieffer (BCS) theory of superconductivity can be used to develop expressions for the surface impedance of superconductors on the base of several fundamental material properties (as the mean free path, coherence length, etc.)
Power dissipation in the SRF cavity: At a finite temperature, the unpaired electrons in a superconductor experience the effect of the RF field, resulting in power dissipation on the metallic cavity walls based on their surface resistance and the surface magnetic field intensity.
where is expressed in Kelvin and is expressed in gigahertz [H. Padamsee, RF Superconductivity (2009)].
SCRF Cavity fabrication technology:
The first term represents the BCS contribution, the second term accounts for increased losses resulting from trapped DC magnetic fields, such as Earth's magnetic field. The third term encompasses various sources, including chemical residues on surfaces, foreign material inclusions, condensed gases, and the presence of hydrides and oxide layers.

## Slide 27
Dynamic RF heat load to SRF cavities in the GWVC

## Slide 28
Conduction heat load duo to support structures, RF components and cabling etc.
For estimating in the case of heat flow within the cold mass, one can use the thermal conductivity (𝑘) and the following formula, where and are the temperatures at the hot end and the cold end respectively, is the length of the bar, and is the cross sectional area of the bar. The unit of is W/K-meter.
Thermal conductivity (and its integral) varies greatly with temperature and with material. Proper choice of materials and thermal intercept strategies for the conduction paths to the cold environment is therefore necessary in the design of the SCRF components.

## Slide 29
Convection heat load
convection heat transfer between a surface at temperature with a bulk fluid at temperature is the Newton law of cooling
Analysis of convection exchanges are therefore important to make proper provision for the cooldown and warmup procedure
An insufficient heat transfer coefficient in the presence of high heat loads would drive the pipe surface temperatures to higher values to sustain the transfer

## Slide 30
The radiative heat transfer from one surface to another is expressed as following (doi:10.18429/JACoW-IPAC2015-WEPTY031):
where is radiative power on surface 2 from surface 1. , , and are temperature, emissivity and area respectively for surface 1 and 2. is view factor that determines proportion of radiation from surface 1 reaching to surface 2. is the Boltzmann constant.
Radiation heat load
The empirical formula for calculating the heat flux through the MLI layers sufficiently verified in practice:
Heat flux (W/m2)
= 8.9510-8, = 510-10
: radiation shield layer density (layers/cm)
: number of MLI layers,
= hot side temperature (K)
= cold side temperature (K)
Tm: mean insulation temperature, we take (TH+TC)/2
room temperature (300 K) emissivity of radiation shield (aluminum film emissivity = 0.03)
Nuclear Instruments and Methods in Physics Research A 763 (2014) 701–710 703
With MLI insulation, the radiative load can be brought to the following levels:
0.5 W/m2 to 1.5 W/m2 from the room temperature environment to the intermediate shield temperatures (~40–80 K),
0.05 W/m2 to 0.1 W/m2 from the thermal shields to negligible temperatures.

## Slide 31
Radiation heat load to GWVC
We need to calculate the area of the 40, 4K, and 2K cold surface regions that are covered by MLI.
Radiation heat load of 1.55 W/m2 from 300 K to the shield temperature of 40 K with 30 MLI
0.1 W/m2 from the thermal shield at 40 K to 4K and 2K cold masses with 10 MLI.
Tshield = 50 K
Touter vessel = 300 K

## Slide 32
Heat load duo to RF losses/Ohmic losses

## Slide 33
ACPS TL3
= 10 g/s, 4.5 K & 3.5 bar
Mass flow rates required for cooling down the SRF cavity
SFHe @1.8 K and 16 mbar to warm compressor
LHe @ 4.2 K & 1.0 bara
SF He @1.8 K and 1 bar
MAGO cavity (heat load = 30 W)
LP CFHEX
JT valve: JT2KF01
JT valve: JT4KF01
= 9.62 g/s
= 0.38 g/s
Enthalpy values of helium supplied through JT4KF01:
Enthalpy of inlet supercritical helium, hi @ (4.2 K, 3.5 bar) = 10.69 J/g
Enthalpy of outlet saturated LHe, @ (4.2 K, 1.0 bar) = 9.90 J/g
Enthalpy of outlet saturated GHe, @ (4.2 K, 1.0 bar)J/g
Enthalpy values of helium supplied through JT2KF01:
Enthalpy of inlet saturated LHe, hi @ (4.2 K, 1 bar) = 9.90 J/g
Enthalpy of outlet saturated SF He, @ (1.8 K, 16 mbar) = 0.84 J/g
Enthalpy of outlet saturated SF He, @ (1.8 K, 16 mbar)J/g
Latent of saturated SF He, @ (1.8 K, 16 mbar) = 22.98 J/g
of SF He = 5.89 g/s
of SF He = 3.72 g/s
Enthalpy values of helium in the bath:
Enthalpy of single phase SF He, @ (1.8 K, 1 bar) = 1.52 J/g
HeII – HeII heat exchanger
Heat absorption = 5.89*22.98 = 135.5 W

## Slide 37
THE GERSEMI VERTICAL CRYOSTAT AT FREIA
arXiv:2103.05265v1

## Slide 38
Cryostat in two parts
Elevating this part to a greater height can help maintain hydraulic pressure during cryostat filling.
Additionally, it can assist in reducing vibrations and minimizing noise.
But it will strongly depend on the fund of the project.

## Slide 39
In which orientation will the cavity be mounted on the cryogenic insert?
Will the MAGO cavity be submerged in SF helium or remain in a vacuum?
What quality factor and resonance frequency would be aimed for?
How do we plan to address the issues of microphonic noise, vibration isolation, flux pinning (very slow cooldown and magnetic shield) and electronic noise?
How can we estimate all potential sources of different heat loads?
Simulation and calculation of various physical parameters for the set-up, such as stress analysis, thermal analysis, etc.
Complete understanding of the flow scheme and translation into a 3D drawing.
Preparation of specifications for the insert, cold compressors, and cryostat.
How many different applications would you like to configure for the cryostat? For instance, applications involving an applied magnetic field or filling the cavity with SF helium.
Specific questions related to the project

## Slide 40
Thank you for your attention!!!