## Slide 1: Dielectric laser accelerators for electron compression and quantum sensing
Zhexin Zhao, PhD
Postdoctoral Researcher at FAU Erlangen-Nürnberg
zhexin.zhao@fau.de
March 19, 2024

## Slide 2: Introduction: On-chip particle accelerators
SLAC
https://www6.slac.stanford.edu/about/contact-slac
Varian medical systems
news.fnal.gov/2022/05/
m.indiamart.com
Dielectric Laser Accelerators (DLAs)
Conventional accelerators
Miniturization
2-mile long
Table-top
(On-chip)
Chlouba, T., et al. "Coherent nanophotonic electron accelerator." Nature 622.7983 (2023): 476-480.
Notes: Particle accelerators: Science. 2-mile linac, particle physics. Coherent X-ray; Medical Equipments, Industrial processing. Useful but bulky.
If miniaturized, it will be much accessible and enable new applications. Therefore, scientists study dielectric laser accelerators to build a particle accelerator on a chip. Since the main acceleration stage is dielectric structure, powered by laser, DLA. Picture: silicon chip.
are important for science. Here is a picture of the 2-mile long linear accelerator at stanford linear accelerator center. It has been the driver of fundamental physical discovery for decades. And it powered the free-electron laser to generate the brightest coherent x-ray radiation. Accelerators are also widely used in radiotherapy and industrial processing. However, accelerators are big. Here is a picture of the magnets and the radio frequency cavity for the control and acceleration of electrons. With laser technology and integrated photonics, researchers studied how to build a particle accelerator on a chip.
Conventional accelerators and applications
Useful but bulky

## Slide 3: Potential applications of DLAs
Zong, A. (2021). Ultrafast Electron Diffraction. Springer, Cham.
Ultrafast electron diffraction and microscopy
England, et al. Reviews of Modern Physics 86.4 (2014): 1337.
Medical devices
Shentcis, Michael, et al." Nature Photonics 14.11 (2020): 686-692.
X-rays
van der Waals materials
Free-electron (X-ray) light sources
Wong, Liang Jie, et al. Nature Photonics 10.1 (2016): 46.
Notes: DLAs can open up many applications. The accelerated free electrons can generate tunable radiation, including x-ray.
References: Nilsson, Daniel. "Zone plates for hard x-ray free-electron lasers." PhD diss., KTH Royal Institute of Technology, 2013.
Zong, A. (2021). Ultrafast Electron Diffraction. In: Emergent States in Photoinduced Charge-Density-Wave Transitions. Springer Theses. Springer, Cham. https://doi.org/10.1007/978-3-030-81751-0_3

## Slide 4: Outline
Electron pulse
Optical resonator, e.g., DLA
Electron compression
Quantum sensing

## Slide 5: Electron microscopy
High spatial resolution
High temporal resolution
Garcia de Abajo, F. Javier, and Valerio Di Giulio. "Optical excitations with electron beams: Challenges and opportunities." ACS photonics 8.4 (2021): 945-974.
Zhang, Ming, et al. The Journal of Physical Chemistry Letters 13.7 (2022): 1668-1680.
Molecular dynamics
Zhou, Fei, et al. Physical Review B 100.18 (2019): 184308.
Lattice dynamics

## Slide 6: Electron pulse compression
Objective: To achieve high temporal resolution in electron microscopy
To measure fs dynamics requires fs probes.
THz electron compressor:
 Electron pulse compression: ps  fs.
 THz generation efficiency is typically low.
Science 352.6284 (2016): 429-433.
Electron pulse
THz energy modulation

## Slide 7: Electron pulse compression
Optical modulation can generate attosecond electron pulse trains
Electron pulse
Optical energy modulation
Attosecond electron pulse trains
Electron source
Electron pulses

## Slide 8: Attosecond electron pulse trains with optical modulation
Black, Dylan S., Uwe Niedermayer, Yu Miao, Zhexin Zhao, Olav Solgaard, Robert L. Byer, and Kenneth J. Leedle. Physical review letters 123, no. 26 (2019): 264802.

## Slide 9: Attosecond electron pulse trains with optical modulation
Schönenberger, Norbert, Anna Mittelbach, Peyman Yousefi, Joshua McNeur, Uwe Niedermayer, and Peter Hommelhoff. Physical review letters 123, no. 26 (2019): 264803.
Notes: Pay attension of the transverse dim of the electron.
The beam may diverges after the first interaction stage!

## Slide 10: Electron pulse compression with optical beat note
How to use optical modulation to compress the whole (sub-relativistic) electron pulse from ps to fs?
Electron pulse
Optical resonator, e.g., DLA
Electron pulse
Optical modulation
Zhao, Zhexin, Kenneth J. Leedle, Dylan S. Black, Olav Solgaard, Robert L. Byer, and Shanhui Fan. "Electron pulse compression with optical beat note." Physical Review Letters 127, no. 16 (2021): 164802.

## Slide 11: Working principle
Electron pulse
Drift length
Optical beat node
Zhao, Zhexin, Kenneth J. Leedle, Dylan S. Black, Olav Solgaard, Robert L. Byer, and Shanhui Fan. "Electron pulse compression with optical beat note." Physical Review Letters 127, no. 16 (2021): 164802.

## Slide 12: Improvement with high harmonics
Challenge: Only a small portion of the electrons can be captured in the central density peak after compression.
With high harmonics, larger portion of the total energy modulation is aligned with a linear slow-varying energy modulation.
Electron pulse
Enlarged view near

## Slide 13: Numerical compression results
Parameters:
Initial energy of the electron: keV
Initial energy spread of the electron pulse: eV
Initial electron pulse duration: ps
Optical pulse duration: ps
Optical frequencies: THz, THz,
N (# of harmonics) | FWHM | Peak ratio (% captured within FWHM)
1 | 2.3 fs | 3%
4 | 2.9 fs | 21%

## Slide 14: Peak ratio
With more harmonics, the peak ratio increases significantly.
FWHM decreases with increasing modulation amplitude.
With more harmonics, the FWHM remains almost unchanged.
Compressed pulse duration
~THz
Theory: FWHM =
Notes: ~THz
Theory: FWHM =
Δ𝐸 ̅(𝜏)=2ℇ𝐴(𝜏) sin⁡((𝜔_1−𝜔_2)/2 𝜏) ~THz
Theory: FWHM = 𝛿𝐸_0/ℇ(𝜔_1−𝜔_2)

## Slide 15: Electron pulse compression with optical beat note
All-optical electron pulse compression with optical beat note
Compression comparable to THz, without THz generation
Compress electrons with a wide range of initial durations by tuning the optical beat frequency.
Numerical demonstration: 1 ps  3 fs
Electron pulse
Optical resonator, e.g., DLA
Electron pulse
Optical modulation
Zhao, Zhexin, Kenneth J. Leedle, Dylan S. Black, Olav Solgaard, Robert L. Byer, and Shanhui Fan. "Electron pulse compression with optical beat note." Physical Review Letters 127, no. 16 (2021): 164802.

## Slide 16: Outline
Electron pulse
Optical resonator, e.g., DLA
Electron compression
Quantum sensing

## Slide 17: Quantum description
The state of the electron can be described by a wave function.
Temporal extension of the electron wave packet can be longer than light periodicity.
A density distribution description is suitable for electrons.
An electron is a point particle.
Classical description
Notes: When the classical description is suitable?
Single electron region: quantum?
Remove the figure
Electron in a DC field: Airy
Bloch oscillation
State the obvious

## Slide 18: Engineer the free-electron wave function with a DLA
The quantum nature of electron-laser acceleration observed in a DLA
Adiv, Yuval, et al. "Quantum nature of dielectric laser accelerators." Physical Review X 11.4 (2021): 041042.
With the wavefunction engineered free electrons, what is new in the electron-matter interaction?
Notes: State the completely uncontroversal.

## Slide 19: Free-electron—atom interaction
Objective: Investigate free electrons as the probe for quantum systems
Previous work: Semi-classical approach
Limitations of the semi-classical model:
  The back-action on the free electron is missing.
  Entanglement arising from the interaction cannot be revealed.
Gover, Avraham, and Amnon Yariv. Physical Review Letters 124.6 (2020): 064801.

## Slide 20: Quantum free-electron—atom interaction: Theory
Scattering matrix:
S
Electron measurements
Measurement results depend on the initial free-electron wave function.
Coupling coefficient
Electron loses energy . Atom transits from ground to excited state.
Electron and atom state are unchanged
Linearized electron dispersion relation
Zhao, Zhexin, Xiao-Qi Sun, and Shanhui Fan. "Quantum entanglement and modulation enhancement of free-electron-bound-electron interaction." Physical Review Letters 126, no. 23 (2021): 233402
Notes: Ref

## Slide 21: Probe the atomic coherence with modulated free electrons
Electron energy loss spectrum example:
Resonant modulated electron
This anti-symmetric EELS signal can probe the atomic coherence.
Plane-wave like electron
Zhao, Zhexin, Xiao-Qi Sun, and Shanhui Fan. "Quantum entanglement and modulation enhancement of free-electron-bound-electron interaction." Physical Review Letters 126, no. 23 (2021): 233402
Notes: Change on the free-electron due to the interaction:
Change on the free-electron due to the interaction: Δ𝜌_𝑒=𝑇𝑟_𝑎 [𝑆𝜌_𝑒𝑎^𝑖 𝑆^†−𝜌_𝑒𝑎^𝑖 ]

## Slide 22: Create entanglement
 | Free-electron energy | 2 identical atoms
Initial state |  | Ground state
Final state | (post selection) | Entangled state
 | Free-electron energy | 2 identical atoms
Initial state |  | Ground state
Final state |  | Entangled state
Zhao, Zhexin, Xiao-Qi Sun, and Shanhui Fan. "Quantum entanglement and modulation enhancement of free-electron-bound-electron interaction." Physical Review Letters 126, no. 23 (2021): 233402

## Slide 23: Interaction between the two-level system and a dilute electron beam
Atomic excitation can build up.
Rabi oscillation frequency ,
  if .
Consistent with semi-classical approach:
  .
Steady state: increased excitation probability with modulated electrons.

## Slide 24: Quantum free-electron—atom interaction: Summary
Modulated free electrons can probe the quantum coherence.
Creating entanglement
Interaction between the two-level atom and a modulated dilute electron beam: Consistent with semi-classical theory
Zhao, Zhexin, Xiao-Qi Sun, and Shanhui Fan. "Quantum entanglement and modulation enhancement of free-electron-bound-electron interaction." Physical Review Letters 126, no. 23 (2021): 233402
Enhanced interaction due to free-electron wave function modulation
Enhanced electron energy loss spectrum to probe atomic coherence
Notes: Driving the 2-level atom
Electron energy loss/gain spectrum (EELS)
Creating entanglement
Interaction between the two-level system and a dilute electron beam

## Slide 25: Summary
Modulation stage
2-level atom
Quantum sensing
Electron pulse
Optical resonator, e.g., DLA
Electron compression

## Slide 26: Acknowledgement
Stanford Graduate Fellowship
Siemann Graduate Fellowship
Collaborators:
Prof. Shanhui Fan
Prof. Robert L. Byer
Prof. Olav Solgaard
Dr. Dylan S. Black
Dr. Kenneth J. Leedle
Dr. Xiao-Qi Sun
Notes: Dylan S. Black,2 Xiao-Qi Sun,3 Tyler W. Hughes,2 Kenneth J. Leedle,2 Si Tan,2 R. Joel England,4 Olav Solgaard,2 Robert L. Byer,2 Shanhui Fan,2 and Peter Hommelhoff

## Slide 27: Thank you!