## Slide 1
Test-beam 2022 Analysis
Towards publication
Wolfgang Lohmann, DESY, BTU and RWTH

## Slide 2
We used an electron beam of 5 GeV
The track of a beam particle is defined by 5 telescope planes
Testbeam data
4 sensors were tested,
Two silicon sensors, thickness 500 mm, denoted as C74 and C75
Two GaAs sensors, thickness 500 mm, denoted as Anton1 and Yan 1.

## Slide 3
Number of triggers
C74 18 x 106 scan over the sensor
7 x 106 at position – 37,5, - 6.5
C75 27 x 106 scan over the sensor
18 x 106 at position – 1.5, - 88.5
A1 46 x 106 scan over the sensor
Y1 44 x 106 scan over the sensor
33 x 106 at position 1, - 94,4
Testbeam data

## Slide 4
Goals of data analysis
Homogeneity of the response
Take only tracks hitting the central
part of a pad (e.g.the red area
Plot the signal size, determine MPV
of signals in each pad
Use the pedestal width to calculate
S/N
Apply calibration constants
To be done (at least for a few cases) using raw using raw data

## Slide 5
Goals of data analysis
Auxiliary informations:
Pedestals for all channels in all runs, pedestal width is needed for S/N
Calibration constants for all channels (important for homogeneity plots)
‚zero point‘ of signal distributions (to be done with raw data) at least for a few channles
Signal distribution from raw data without using the FPGA preprocessing algorithm

## Slide 6
Example pedestal-signal
response

## Slide 7
Goals of data analysis
Performance near the edges of the pads
Take tracks hitting a certain strip in x
Plot the signal size of these events, determine MPV of signals in each strip
Plot the MPV as a function of x
(or equivalently y)
Example of such a plot from previous
studies

## Slide 8
Goals of data analysis
Cross talk 1
At the GaAs sensors, the signals of the pads are routed to the edge via traces in between the pads. Electrons impinging on these traces may induce signals assigned wrongly to the pad where the trace is connected. To study these effects, events with predicted beam positions in between pads should be used.
Pad connected to Al readout trace
Select tracks in the orange area, and search for signals in pads to which the traces are connected

## Slide 9
Goals of data analysis
Cross talk 2
Both in Calice and GaAs sensors signal routing traces have a non-zero capacitance to neighbors, resulting in cross talk of signals between traces.
To study this effect runs with the beam spot in the lower part of the sensors should be used. Then, for signals in pads in the upper part, not covered by the beam, should be searched for.
Beamspot here
Search for potential signals here, in addition to signals in the beamspot area

## Slide 10
Goals of data analysis
Analysis of data with tungsten absorber
Understand the response of the readout to larger signals, potential cross talk
Understand the response for “low gain”, define the overlap in amplitudes
Illustrate longitudinal and transversal shower profiles, compare with simulation and previous results (our first measurements of the shower tails)

## Slide 11
4.5 GeV electron beam,
500 μm sensor thickness
GEANT4 simulation
Estimated number of e/h pairs per μm GaAs for different electron energies,
In a 500 μm thick sensor this corresponds to 41000 electrons
Compare with simulation

## Slide 12
Person power
Who wants to do what????