Study of the timing performance
and eletronic response of
the SBT 4cells prototype
WOM-based liquid-scintillator detector 2 (WP 2.1)
4th High-D Consortium Meeting
Alessia Brignoli
Humboldt Universität zu Berlin
20th February 2024
20-02-2024 A. Brignoli – Humboldt University

---
Test beam measurements
Test beam measurements:
- 5000 events per position
- 5 GeV muon
- beam – σ = 13mm
- trigger:
beam telescope (4PMTs),
in front of the detector
+
additional scintillator with PMT,
in the back of the detector
resolution O(0.8 ns)
- 0° - 0° rotation
Time distribution, beam telescope PMT
For this analysis

---
Time response
The time response of the detector has been calculated as the average time response of the two WOMs for each cell:
1. Sum of waveforms over each WOM, per event
2. Smoothing and Constant Fraction Discrimination (CFD) at 25%
3. Average of the two WOMs, per event j:
{T} rsub {j} = {1} over {2} (T rsub {WOM rsub{up} , j} + T rsub {WOM rsub{down} , j})
SiPMs grouped in 8 group of 5 SiPMs each (channels)

---
Time response
The shown results are mean and standard deviation of the average time distribution
Time variation over a cell of the detector: ± 2ns
→ Reducible with likehood method

---
Time response
In order to get the time resolution for a fixed position, calculation of the time difference in the central position of the box:
From the distribution, the error is 1.49 ns
→ time resolution for the two WOMs:
    1.04 ns
→ time resolution on the average time:
     0.52 ns
Distribution of time difference for central position
[Speaker Notes: Its walls will be made of 30 mm thick Corten steel (S355JO(J2/K2)W). To avoid buckling of the walls, they are equipped with a regular pattern of vertical and quasi horizontal stiffening members of 20 cm width, also made from 30 mm thick Corten steel sheets. The vertical stiffening members are parallel while the horizontal ones widen along the length of the vessel. The almost rectangular structure defined by the inner vacuum vessel wall and the stiffening members will be welded closed by Corten steel sheets of 30 mm thickness, defining the cells which can be filled with the LS to create the LS-SBT.]

---
Geant4 simulation
Geant4 simulation of the 4 cells detector
with geometry and materials properties implemented with high precision
Originally, the final output of the simulation was the photons arrival times
To have a better comparison between data and simulation, regarding time response and light yield, implementation of the electronic response of the SiPMs
[Speaker Notes: Its walls will be made of 30 mm thick Corten steel (S355JO(J2/K2)W). To avoid buckling of the walls, they are equipped with a regular pattern of vertical and quasi horizontal stiffening members of 20 cm width, also made from 30 mm thick Corten steel sheets. The vertical stiffening members are parallel while the horizontal ones widen along the length of the vessel. The almost rectangular structure defined by the inner vacuum vessel wall and the stiffening members will be welded closed by Corten steel sheets of 30 mm thickness, defining the cells which can be filled with the LS to create the LS-SBT.]

---
Simulating the waveform
From dark count charge spectrum:
(no beam; trigger on random signal; search for the maximum of amplitude in
the whole 320 ns window, per event: integrating 5 ns before maximum and 9 ns after)
 → 1pe waveform	→ Dark count probability ~ 75%	→ Electronic noise ~ 1mV
 → Gain	→ Crosstalk probability ~ 17%	→ After pulses probability and time (not yet)
Dark count spectra
1 photoelectron waveform
[Speaker Notes: Its walls will be made of 30 mm thick Corten steel (S355JO(J2/K2)W). To avoid buckling of the walls, they are equipped with a regular pattern of vertical and quasi horizontal stiffening members of 20 cm width, also made from 30 mm thick Corten steel sheets. The vertical stiffening members are parallel while the horizontal ones widen along the length of the vessel. The almost rectangular structure defined by the inner vacuum vessel wall and the stiffening members will be welded closed by Corten steel sheets of 30 mm thickness, defining the cells which can be filled with the LS to create the LS-SBT.]

---
Simulating the waveform
Example of simulated waveform
Example of waveform from data
Simulated electronic noise
[Speaker Notes: Its walls will be made of 30 mm thick Corten steel (S355JO(J2/K2)W). To avoid buckling of the walls, they are equipped with a regular pattern of vertical and quasi horizontal stiffening members of 20 cm width, also made from 30 mm thick Corten steel sheets. The vertical stiffening members are parallel while the horizontal ones widen along the length of the vessel. The almost rectangular structure defined by the inner vacuum vessel wall and the stiffening members will be welded closed by Corten steel sheets of 30 mm thickness, defining the cells which can be filled with the LS to create the LS-SBT.]

---
Shape of the waveform
Average waveform
Afterpulses contribution?
Dark count contribution
[Speaker Notes: Its walls will be made of 30 mm thick Corten steel (S355JO(J2/K2)W). To avoid buckling of the walls, they are equipped with a regular pattern of vertical and quasi horizontal stiffening members of 20 cm width, also made from 30 mm thick Corten steel sheets. The vertical stiffening members are parallel while the horizontal ones widen along the length of the vessel. The almost rectangular structure defined by the inner vacuum vessel wall and the stiffening members will be welded closed by Corten steel sheets of 30 mm thickness, defining the cells which can be filled with the LS to create the LS-SBT.]

---
Comparison with the data
Simulation settings that play important roles in the waveform generation:
for the amplitude	for the shape
→ LAB-PPO transparency	→ LAB-PPO transparency
→ Cell coating reflectivity	→ Cell coating reflectivity
→ SiPMs Optical coupling
Other possible sources of discrepancies:
→ PMMA transparency	→ Scintillation decay times
→ WLS coating thickness
...
[Speaker Notes: Its walls will be made of 30 mm thick Corten steel (S355JO(J2/K2)W). To avoid buckling of the walls, they are equipped with a regular pattern of vertical and quasi horizontal stiffening members of 20 cm width, also made from 30 mm thick Corten steel sheets. The vertical stiffening members are parallel while the horizontal ones widen along the length of the vessel. The almost rectangular structure defined by the inner vacuum vessel wall and the stiffening members will be welded closed by Corten steel sheets of 30 mm thickness, defining the cells which can be filled with the LS to create the LS-SBT.]

---
Reflective coating
Average waveform
- Depends on the position of the beam
- Effect on the falling edge of the waveform
- Depends on the different cell
[Speaker Notes: Its walls will be made of 30 mm thick Corten steel (S355JO(J2/K2)W). To avoid buckling of the walls, they are equipped with a regular pattern of vertical and quasi horizontal stiffening members of 20 cm width, also made from 30 mm thick Corten steel sheets. The vertical stiffening members are parallel while the horizontal ones widen along the length of the vessel. The almost rectangular structure defined by the inner vacuum vessel wall and the stiffening members will be welded closed by Corten steel sheets of 30 mm thickness, defining the cells which can be filled with the LS to create the LS-SBT.]

---
Liquid scintillator LAB
Average waveform
- Depends on the position of the beam, correlated with reflectivity
- Effect on the falling edge of the waveform
[Speaker Notes: Its walls will be made of 30 mm thick Corten steel (S355JO(J2/K2)W). To avoid buckling of the walls, they are equipped with a regular pattern of vertical and quasi horizontal stiffening members of 20 cm width, also made from 30 mm thick Corten steel sheets. The vertical stiffening members are parallel while the horizontal ones widen along the length of the vessel. The almost rectangular structure defined by the inner vacuum vessel wall and the stiffening members will be welded closed by Corten steel sheets of 30 mm thickness, defining the cells which can be filled with the LS to create the LS-SBT.]

---
Optical coupling
Difference in channels response, due to:
→ Optical coupling
Analysis and comparison with simulation
performed on the sum waveform over 8
channels of the WOM
[Speaker Notes: Its walls will be made of 30 mm thick Corten steel (S355JO(J2/K2)W). To avoid buckling of the walls, they are equipped with a regular pattern of vertical and quasi horizontal stiffening members of 20 cm width, also made from 30 mm thick Corten steel sheets. The vertical stiffening members are parallel while the horizontal ones widen along the length of the vessel. The almost rectangular structure defined by the inner vacuum vessel wall and the stiffening members will be welded closed by Corten steel sheets of 30 mm thickness, defining the cells which can be filled with the LS to create the LS-SBT.]

---
Conclusion
Conclusion
Regarding the time response:
- Time variance over one cell: ± 2 ns → can be improved with likelihood method
- Time resolution for a fixed position: ± 0.52 ns
Regarding the simulation, it is still a work in progress but:
- Good agreement of the rising edge of the waveform
- Studied how properties of material can affect the waveforms
- Spotted significant differences depending on the channel → Using summed waveform over WOM
Outlook
- Improving of the simulated waveform	→ implementing afterpulses
→ checking dark counts
 → further investigation over the falling edge
- Calibration of the electronic response for all the WOMs
- Realization of the time and light yield analysis on the simulated waveforms and comparison with	the data
- Acquisition of more data/positions during the next testbeam (March 2024)
[Speaker Notes: Its walls will be made of 30 mm thick Corten steel (S355JO(J2/K2)W). To avoid buckling of the walls, they are equipped with a regular pattern of vertical and quasi horizontal stiffening members of 20 cm width, also made from 30 mm thick Corten steel sheets. The vertical stiffening members are parallel while the horizontal ones widen along the length of the vessel. The almost rectangular structure defined by the inner vacuum vessel wall and the stiffening members will be welded closed by Corten steel sheets of 30 mm thickness, defining the cells which can be filled with the LS to create the LS-SBT.]

---
Thank you